České vysoké učení technické v Praze,  Fakulta elektrotechnická

Pokročilé architektury počítačů (A4M36PAP)

Semestrální projekt  – 01

Téma projektu:  Návrh jednoduchého výpočetního systému

Zadání:  Navrhněte a popište v jazyce Verilog jednoduchý výpočetní systém pozůstávající z procesoru, oddělené instrukční a datové paměti. Procesor bude podporovat instrukce add, sub, and, or, slt, addi,  lw, sw, beq, jal a jr ve formátu instrukční sady MIPS. Součástí procesoru musí být řídicí jednotka a aritmeticko-logická jednotka. Funkčnost Vašeho návrhu demonstrujte simulací níže uvedeného programu.

a = 5;

b = 4;

c = 3;

b = fun(a) + simple(a,b,c,5,10);

while(1)

;

kde definice použitých funkce jsou:

int fun(int x)

{

if (x == 0) return 1;

else return x+fun(x-1);

}

int simple(int a, int b, int c, int d, int e)

{

int x, y;

x = a+b+c

y = d-e;

x = x + y;

x = x & 7;

return x;

}

Předpokládejte, že všechny proměnné jsou typu int (4B) a jsou již uloženy v paměti na adresách 0x0010, 0x0014 a 0x0018, atd. datové paměti, proměnná a je větší než 0, a program je již uložen v instrukční paměti od adresy 0x0000 (tj. není potřeba řešit zavádění programu). Procesor po resetu (po spuštění) začíná vykonávat instrukce od adresy 0x0000. Předpokládejte volací konvenci O32.

Bližší specifikace a informace:

K dispozici je 32 pracovních registrů. Registry jsou 32-bitové a jsou číslovány $0 až $31. V registru $0 je vždy uložena hodnota 0.  Všechny MIPS instrukce jsou 32-bitové a jsou děleny do třech skupin: R (add, and, or, slt, sub), I (addi, beq, lw, sw) a J. Každá instrukce začíná 6-bitovým operačním kódem (opcode). Všechny R-instrukce mají opcode roven 000000(2), přičemž v tomto případě vykonávanou funkci určují bity 5:0 (funct).

| Typ | 31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16 | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| R | opcode(6) | rs(5) | rt(5) | rd(5) | shamt(5) | funct(6) |
| I | opcode(6) | rs(5) | rt(5) | immediate (16) |
| J | opcode(6) | address (26) |

Bližší popis, vykonávanou operaci, syntax a kódování pro instrukce podporované navrženým procesorem uvádějí tabulky níže.

### ADD – Add (with overflow)

| Description: | Adds two registers and stores the result in a register |
| --- | --- |
| Operation: | $d = $s + $t; |
| Syntax: | add $d, $s, $t |
| Encoding: | 0000 00ss ssst tttt dddd d000 0010 0000 |

### ADDI -- Add immediate (with overflow)

| Description: | Adds a register and a sign-extended immediate value and stores the result in a register |
| --- | --- |
| Operation: | $t = $s + imm; |
| Syntax: | addi $t, $s, imm |
| Encoding: | 0010 00ss ssst tttt iiii iiii iiii iiii |

### AND -- Bitwise and

| Description: | Bitwise ands two registers and stores the result in a register |
| --- | --- |
| Operation: | $d = $s & $t; |
| Syntax: | and $d, $s, $t |
| Encoding: | 0000 00ss ssst tttt dddd d000 0010 0100 |

### BEQ -- Branch on equal

| Description: | Branches if the two registers are equal |
| --- | --- |
| Operation: | if $s == $t go to PC+4+4*offset; else go to PC+4 |
| Syntax: | beq $s, $t, offset |
| Encoding: | 0001 00ss ssst tttt iiii iiii iiii iiii |

### LW -- Load word

| Description: | A word is loaded into a register from the specified address. |
| --- | --- |
| Operation: | $t = MEM[$s + offset]; |
| Syntax: | lw $t, offset($s) |
| Encoding: | 1000 11ss ssst tttt iiii iiii iiii iiii |

### OR -- Bitwise or

| Description: | Bitwise logical ors two registers and stores the result in a register |
| --- | --- |
| Operation: | $d = $s ¦ $t; |
| Syntax: | or $d, $s, $t |
| Encoding: | 0000 00ss ssst tttt dddd d000 0010 0101 |

### SLT -- Set on less than (signed)

| Description: | If $s is less than $t, $d is set to one. It gets zero otherwise. |
| --- | --- |
| Operation: | if $s < $t $d = 1; else $d = 0; |
| Syntax: | slt $d, $s, $t |
| Encoding: | 0000 00ss ssst tttt dddd d000 0010 1010 |

### SUB -- Subtract

| Description: | Subtracts two registers and stores the result in a register |
| --- | --- |
| Operation: | $d = $s - $t; |
| Syntax: | sub $d, $s, $t |
| Encoding: | 0000 00ss ssst tttt dddd d000 0010 0010 |

### SW -- Store word

| Description: | The contents of $t is stored at the specified address. |
| --- | --- |
| Operation: | MEM[$s + offset] = $t; |
| Syntax: | sw $t, offset($s) |
| Encoding: | 1010 11ss ssst tttt iiii iiii iiii iiii |

### JAL  -- Jump and link

| Description: | For procedure call. |
| --- | --- |
| Operation: | $31 = PC + 8; PC = (PC & 0xf0000000) ¦ (target << 2) |
| Syntax: | jal target |
| Encoding: | 0000 11ii iiii iiii iiii iiii iiii iiii |

### JR – Jump register

| Description: | Jumps to the address contained in the specified register |
| --- | --- |
| Operation: | goto address $s |
| Syntax: | jr $s |
| Encoding: | 0000 00ss sss0 0000 0000 0000 0000 1000 |

O32 volací konvence:

| Name | Number | Use | Callee must preserve? |
| --- | --- | --- | --- |
| $zero | $0 | constant 0 | N/A |
| $at | $1 | assembler temporary | No |
| $v0–$v1 | $2–$3 | values for function returns and expression evaluation | No |
| $a0–$a3 | $4–$7 | function arguments | No |
| $t0–$t7 | $8–$15 | temporaries | No |
| $s0–$s7 | $16–$23 | saved temporaries | Yes |
| $t8–$t9 | $24–$25 | temporaries | No |
| $k0–$k1 | $26–$27 | reserved for OS kernel | N/A |
| $gp | $28 | global pointer | Yes |
| $sp | $29 | stack pointer | Yes |
| $fp | $30 | frame pointer | Yes |
| $ra | $31 | return address | N/A |