Computer Architectures
Microprocessor evolution - from 4-bit ones to superscalar RISC
Pavel Píša, Michal Štepanovský
Czech Technical University in Prague, Faculty of Electrical Engineering
Ver.1.00

---
Technology and complexity comparison

---
Accumulator based architectures
- register+accumulator → accumulator
  - 4bit Intel 4004 (1971)
  - 8bit Intel8080 (1974) – registers pairs used to address data in 64kB address space
  - basic arithmetic-logic operations only – addition, subtraction, rotation for 8-bit accumulator
  - subroutines by CALL and RET instructions with 16-bit PC save on stack
  - a few 16-bit operations – increment/decrement of registers pairs, addition to HL and save to stack
  - microcode controlled/microprogrammed instructions execution – 2 to 11 clock cycles per instruction at 2 MHz clock signal

---
Intel 8080
http://en.wikipedia.org/wiki/Intel_8080

---
Fast memory ⇒ reduce register count and add address modes
- Motorola 6800, NMOS T. 6502 (1975) - accumulator, index, SP a PC only – use zero page as fast data, CU hardwired
- Texas TMS990 – workspace pointer only, even PC, SP, other registers in main memory, similar to transputers

---
Memory is bottleneck now ⇒ complex instruction set modelled according to C language constructs, CISC
- Motorola 68000 (1979) – 16/32bit
  - two operand instructions
  - register+=register, memory+=register, register+=memory, even one instruction memory=memory
  - based on microcode to process so rich instruction set
- Z-8000 16bit, Z-80000 32bit (1986) CISC
  - 6 phases pipelined execution, without microcode, 18000 transistors only

---
Data throughput and instruction fetching slow still ⇒ cache memory
- The problem has been solved quite well
- Common cache or Harvard arrangement I & D
- More levels (speed limited for bigger size – decoder, capacitance of common signals)
- But requires to solve data coherence when DMA access or SMP is used
  - synchronization instructions for peripherals access and synchronization eieio (PowerPC), mcr p15 (ARM), …
  - hardware support required for caches and SMP
    - protocol MSI , MESI (Pentium), MOSI
    - MOESI AMD64 (Modified, Owned, Exclusive, Shared, and Invalid)

---
Data coherence and multiple cached access
MOESI protocol
- Modified – cache line contains actual and modified data, none of other CPUs works with data, old/previous data are hold in main memory
- Owned – line holds actual data, line can be shared with other CPUs CPU but only in S state, main memory is not required to be up to date
- Exclusive – only this CPU and main memory contains cahe line data
- Shared – cache line is shared with other CPUs, one of them can be in O state, then data can differ to content in main memory
- Invalid – cache line does not hold any valid data
	M	O	E	S	I
M	N	N	N	N	Y
O	N	N	N	Y	Y
E	N	N	N	N	Y
S	N	Y	N	Y	Y
I	Y	Y	Y	Y	Y
http://en.wikipedia.org/wiki/MOESI_protocol

---
Other techniques to reduce memory access frequency ⇒ register windows, link/return address register
- SPARC - 8 global registers, 8 from previous window (parameters), 16 in actual window, up to 100 and more registers to stack windows. 8 registers in actual window is used to pass parameters into subroutine
- PowerPC, MIPS, ARM – speedup to call leaf-node functions with use of return address (link register) to store address of the instruction to be executed after return from subroutine

---
PowerPC architecture

---
SPARC – register windows
- CPU includes from 40 to 520 general purpose 32-bit registers
- 8 of them are global registers, remaining registers are divided in groups of 16 into at least 2 (max 32) register windows
- Each instruction has access to 8 global registers and 24 registers accessible through actually selected register windows position
- 24 windowed registers are divided into 8 input (in), 8 local (local) and 8 registers from the following window which are visible through current window as an output (out) registers (registers to prepare call arguments)
- Active window is given by value of 5-bit pointer – Current Window Pointer (CWP).
- CWP is decremented when subroutine is entered which selects following window as an active/current one
- Increment of CWP return to the previous register window
- Window Invalid Mask (WIM) is a bit-map which allows to mark any of windows as invalid and request exception (overflow or underflow) when window is activated/selected by CWP

---
SPARC - registers
R31
R30
R29
R28
R27
R26
R25
R24
R23
R22
R21
R20
R19
R18
R17
R16
R15
R14
R13
R12
R11
R10
R9
R8
Return from actual window ... %i7
The frame pointer %fp ... %i6
%i5
%i4
%i3
%i2
%i1
%i0
%l7
%l6
%l5
%l4
%l3
%l2
%l1
%l0
CALL out return address … %o7
The stack pointer %sp ... %o6
%o5
%o4
%o3
%o2
%o1
%o0
I / (in)
L (local)
O / (out)
G (global)
%g7
%g6
%g5
%g4
%g3
%g2
used by system %g1
zero %g0
R7
R6
R5
R4
R3
R2
R1
R0

---
SPARC – register windows operation

---
Pipelined execution, no microcode, but still problems with jump instructions
- Early jump instruction decode
- Use delay slots to keep pipeline busy, MIPS, DSP
- Static and dynamic conditional branch prediction, branch target address cache, speculative instruction execution

---
MIPS architecture variants
- Probably architecture with the highest use count on Earth at one time (all kinds of AP, embedded systems, etc.)
- Development still continues even for high performance desktops and supercomputers use – Loongson3A
- MIPS architecture inspired many SoftCore designs for FPGA
  - Xilinx Microblaze
  - Altera Nios

---
Loongson3A

---
Yet faster instructions execution ⇒ RISC architectures
- Reduce data flow dependency between instructions, three operand instructions, speculative instructions execution, register renaming, eliminate interdependencies on conditional flag register (DEC Alpha, multiple flag registers PowerPC, flags update suppress ARM)
- load-store architecture, computation only register+=register and or register=register+register and separate load-store instructions.
- Fixed instruction encoding ⇒ programs are usually longer but much faster instructions decoding, optimized for pipelined execution

---
Attempts to enhance code density ⇒ shorter alliases, variable instruction length even for RISC, VLIW
- ARM, 16bit aliases for most common 32bit instructions (Thumb mode)
- M-Core, 32bit CPU but only 16-bit instruction encoding
- ColdFire - RISC implementation based on 68000 instruction set, but only 16, 32, 48-bit length instructions are accepted

---
ARM architecture - registers

---
ARM architecture – ALU and operands encoding
Register, optionally with shift operation
Shift value can be either be:
5 bit unsigned integer
Specified in bottom byte of another register.
Used for multiplication by constant
Immediate value
8 bit number, with a range of 0-255.
Rotated right through even number of positions
Allows increased range of 32-bit constants to be loaded directly into registers
Result
Operand 1
Barrel
Shifter
Operand 2
ALU

---
ARM architecture – program status word
Interrupt Disable bits.
I = 1: Disables the IRQ.
F = 1: Disables the FIQ.
T Bit
Architecture xT only
T = 0: Processor in ARM state
T = 1: Processor in Thumb state
Mode bits
Specify the processor mode
Condition code flags
N = Negative result from ALU
Z = Zero result from ALU
C = ALU operation Carried out
V = ALU operation oVerflowed
Sticky Overflow flag - Q flag
Architecture 5TE/J only
Indicates if saturation has occurred
J bit
Architecture 5TEJ only
J = 1: Processor in Jazelle state
27
31
N Z C V Q
28
6
7
I F T mode
16
23
8
15
5
4
0
24
f
s
x
c
U n d e f i n e d
J

---
ARM architecture – CPU execution modes
- User : unprivileged mode under which most tasks run
- FIQ : entered when a high priority (fast) interrupt is raised
- IRQ : entered when a low priority (normal) interrupt is raised
- Supervisor : entered on reset and when a Software Interrupt instruction is executed
- Abort : used to handle memory access violations
- Undef : used to handle undefined instructions
- System : privileged mode using the same registers as user mode

---
Conclusion – Almost
- There is no magic solution for all discussed problems for all use cases
- It is necessary to combine discussed techniques and optimize the mix according to intended CPU area of use (the highest computational power/power efficient)
- use of heterogeneous systems for high performance computation – vector units, GPU, FPGA accelerators

---
ARM 64-bit – AArch64
- Calling uses LR, no register banking, ELR for exceptions
- PC is separate register (not included in general purpose registers file)
- 31 64-bi registers R0 to R30 (R30 = X30 ≅ LR)
  - Symbol Wn (W0) used for 32-bit access, Xn (X0) for 64-bit
  - Reg. code 31 same role ast MIPS 0, WZR/XZR in code
  - Reg. code 31 special meaning as WSP, SP for some opcodes
- Immediate operand 12-bit with optional LS 12 for arithmetics operations and repetitive bit masks generator for logic ones
- 32-bit operations ignores bits 32–63 for source and zeros these in the destination register

---
AArch64 – Branches and conditional operations
- Omitted conditional execution in all instructions as well as Thumb IT mechanism
- Conditional register retain, CBNZ, CBZ, TBNZ, TBZ added
- Only couple of conditional instructions
  - add and sub with carry, select (move C?A:B)
  - set 0 and 1 (or -1) according to the condition evaluation
  - conditional compare instruction
- 32-bit and 64-bit multiply and divide (3 registers), multiply with addition 64×64+64  64 (four registers), high bits 64 to 127 from 64×64 multiplication

---
AArch64 – Memory access
- 48+1 bit address, sign extended to 64 bits
- Immediate offset can be multiplied by access size optionally
- If register is used in index role, it can be multiplied by access size and can be limited to 32 bits
- PC relative ±4GB can be encoded in 2 instructions
- Only pair of two independent registers LDP and STP (ommited LDM, STM), added LDNP, STNP
- Unaligned access support
- LDX/STX(RBHP) for 1,2,4,8 and 16 bytes exclusive access

---
AArch64 – Address modes
- Simple register (exclusive)
  [base{,#0}]
- Offset
  [base{,#imm}]	– Immediate Offset
  [base,Xm{,LSL #imm}]	– Register Offset
  [base,Wm,(S|U)XTW {#imm}]	– Extended Register Offset
- Pre-indexed
  [base,#imm]!
- Post-indexed
  [base],#imm
- PC-relative (literal) load
  label
Bits	Sign	Scaling	WBctr	LD/ST type
0	-	-	-	LDX, STX, acquire, release
9	signed	scaled	option	reg. pair
10	signed	unscaled	option	single reg.
12	unsig.	scaled	no	single reg.

---
RISC-V – optimize and simplify RISC again
- Patterson, Berkeley RISC 1984 → initiation of RISC era, evolved into SPARC (Hennessy MIPS, Stanford University)
- Commercialization and extensions results in too complex CPUs again, with license and patents preventing even original inverstors to use real/actual implementations in silicon to be used for education and research
- MIPS is model architecture for prevalent amount of base courses and implementation of similar processor is part of follow up courses (A4M36PAP)
- Krste Asanovic and other Dr. Patterson's students initiated development of new architecture (start of 2010)
- BSD Licence to ensure openness in future
- Supported by GCC, binutils., Linux, QEMU, etc.
- Simpler than SPAC, more like MIPS but optimized on gate level load (fanout) and critical paths lengths in future designs
- Some open implementations already exists, project lowRISC contributes to research in security area and plans SoC implementation in silicon

---
RISC-V – architecture specification
- ISA specification can be found at http://riscv.org/
  - The RISC-V Instruction Set Manual, Volume I: User-Level ISA, Version 2.0
  - Andrew Waterman, Yunsup Lee, David Patterson, Krste Asanovic
  - Not only architecture description but even choices analysis with pro&cons of each selection and cost source description/analysis of alternatives
- classic design, 32 integer registers, the first tied to zero, regsrc1, regsrc2, regdest operands, uniqueness, rule kept strictly even for SaveWord, leads to non-continuous immediate operands encoding, PC not part of base register file, PC-relative addressing
- variants for 32, 64 a 128-bit registers and address-space defined
- high code density (16-bit instruction encoding variant planned)
- encoding reserves space for floating point (single, double, quad) and multimedia SIMD instructions systematic way, etc.