Pipelined Instruction Execution
Computer Architectures
https://cw.fel.cvut.cz/wiki/courses/b35apo/start
Pipelined Instruction Execution
Hazards, Stages Balancing, Super-scalar Systems
Pavel Píša, Petr Štěpán, Richard Šusta
Michal Štepanovský, Miroslav Šnorek
Main source of inspiration: Patterson and Hennessy
Czech Technical University in Prague, Faculty of Electrical Engineering
English version partially supported by:
European Social Fund Prague & EU: We invests in your future.
Ver.1.10

---
Motivation – AMD Bulldozer 15h (FX, Opteron) - 2011
Motivation – AMD Bulldozer 15h (FX, Opteron) - 2011

---
Motivation – Intel Nehalem (Core i7) - 2008
Motivation – Intel Nehalem (Core i7) - 2008

---
The Goal of Today Lecture
The Goal of Today Lecture
- Convert/extend CPU presented in the lecture 3 to the pipelined CPU design.
- The following instructions are considered for our CPU design:
  add, sub, and, or, slt, addi, lw, sw and beq

---
Single Cycle CPU Together with Memories
Single Cycle CPU Together with Memories
MemToReg
Control Unit
Opcode
Funct
MemWrite
Branch
ALUControl 2:0
6:0
ALUScr
TypeRISBUJ
31:25, 14:12
RegWrite
SrcA
19:15
Instr
Zero
PC
PC’
Result
ALU
24:20
AluOut
SrcB
ReadData
WriteData
WriteReg
11:7
4
15:0, 24:0
11:7
+
Imm
decode
SignImm
PCPlus4
PCBranch
+
PC
From lecture 3
Instr. Memory
A RD
Data Memory
A RD
WD
WE
Reg.
File
A1 RD1
A2 RD2
A3
WD3
WE3
0
1
0
1
0
1

---
Single Cycle CPU – Performance: IPS
Single Cycle CPU – Performance: IPS = IC / T = IPCavg.fCLK
- What is the maximal possible frequency of this CPU?
- It is given by latency on the critical path – it is lw in our case:
Tc = tPC + tMem + tRFread + tALU + tMem + tMux + tRFsetup
SrcA
Zero
19:15
Instr
PC
PC’
Result
ALU
24:20
AluOut
SrcB
ReadData
WriteData
WriteReg
11:7
4
31:25, 24:20
11:7
+
SignImm
Imm
decode
PCPlus4
PCBranch
+
PC
From lecture 3
Instr. Memory
A RD
Data Memory
A RD
WD
WE
Reg.
File
A1 RD1
A2 RD2
A3
WD3
WE3
0
1
0
1
0
1

---
Single Cycle CPU – Throughput: IPS
Single Cycle CPU – Throughput: IPS = IC / T = IPCavg.fCLK
- Tc = tPC + tMem + tRFread + tALU + tMem + tMux + tRFsetup
- Consider following parameters
  tPC	= 30 ns
  tMem	= 300 ns
  tRFread	= 150 ns
  tALU	= 200 ns
  tMux	= 20 ns
  tRFsetup	= 20 ns
  Then Tc = 1020 ns --> fCLK max = 980 kHz,
  IPS = 1 • 980e3 = 980 000 instructions per second
From lecture 3

---
Separate Instruction Fetch and Execution
Separate Instruction Fetch and Execution
Even non-pipelined processors separate instruction execution into stages :
Instruction Fetch – setup PC for memory and fetch pointed instruction.
Update PC = PC+4
The actual execution of the instruction
Instruction Fetch
Execution

---
Non-Pielined Execution with Instructions Prefetching
Non-Pielined Execution with Instructions Prefetching
SrcA
Zero
19:5
Instr
PC
PC’
Result
ALU
24:20
AluOut
SrcB
ReadData
WriteData
WriteReg
11:7
4
31:25, 24:20
11:7
+
Imm
decode
SignImm
PCBranch
+
PCPlus4
PC
in the figure, it indicates the clock input responding to the rising edge
Instr. Memory
A RD
Data Memory
A RD
WD
WE
Reg.
  File
A1 RD1
A2 RD2
A3
WD3
WE3
0
1
0
1
0
1

---
Single Cycle CPU – Throughput: IPS
Single Cycle CPU – Throughput: IPS = IC / T = IPCstr⋅fCLK
Consider following parameters:
tPC	= 30 ns	tMem	= 300 ns
tRFread	= 150 ns	tALU	= 200 ns
tMux	= 20 ns	tRFsetup	= 20 ns
If Tcfetch is executed paralel with Tcproc,
then Tcfetch < Tcproc, and Tcp = 150+200+300+20+20
= 690 ns → 1.45 MHz → IPS = 1 450 000

---
Delay Slot
Delay Slot
- Prefetched instruction is executed unconditionally even when the proceeding instruction is a taken branch
  - Branch takes place after the next instruction
- MIPS architecture defines execution of one delay slot, but most today architectures including RISC-V use branch prediction instead
- Compiler fills the branch delay slot
  - By selecting an independent instruction
    from the sequence before the branch
  - It has to be to execute instruction in the
    delay slot whether branch is taken or not
- If no suitable instruction is found
  - then the compiler fills delay slot with a NOP
label:
. . .
add $2,$3,$4
beq $1,$0,label
Delay Slot
label:
. . .
beq $1,$0,label
add $2,$3,$4

---
Delay Slot 2
Delay Slot
The task of the compiler is therefore to ensure that the following instructions in the branch delay slot are valid and useful. Three alternatives illustrating how the delay slot can be filled are depicted in the figures below.
The easiest way (at the same time the least efficient) is to fill the delay slot with a blank instruction - nop.

---
Pipelined Instructions Execution
Pipelined Instructions Execution
Suppose that instruction execution can be divided into 5 stages:
IF – Instruction Fetch, ID – Instruction decode (and Operands Fetch),
EX – Execute, MEM – Memory Access, WB – Write Back
and  = max { i }ki=1, where i is time required for signal propagation (propagation delay) through i-th stage.
IF – setup PC for memory and fetch pointed instruction. Update PC = PC+4
ID – decode the opcode and read registers specified by instruction, check for equality (for possible beq instruction), sign extend offset, compute branch target address for branch case (this is means to extend offset and add PC)
EX – execute function/pass register values through ALU
MEM – read/write main memory for load/store instruction case
WB – write result into RF for instructions of register-register class or instruction load (result source is ALU or memory)
IF
ID
EX
MEM
WB

---
Instruction-level Parallelism - Pipelining
Instruction-level Parallelism - Pipelining
IF	I1	I2	I3	I4	I5	I6	I7	I8	I9	I10
ID		I1	I2	I3	I4	I5	I6	I7	I8	I9
EX			I1	I2	I3	I4	I5	I6	I7	I8
MEM				I1	I2	I3	I4	I5	I6	I7
ST					I1	I2	I3	I4	I5	I6
	1	2	3	4	5	6	7	8	9	10
čas
- The time to execute n instructions in the k-stage pipeline:
          Tk = k. + (n – 1) 
- Speedup:
Prerequisite: pipeline is optimally balanced, circuit can arbitrarily divided
size 12{S rSub { size 8{k} } = { {T rSub { size 8{1} } } over {T rSub { size 8{k} } } } = { { ital "nk"τ} over {kτ+ \( n - 1 \) τ} } matrix { {} # {} } {"lim"} cSub { size 8{n rightarrow infinity } } S rSub { size 8{k} } =k} {}
5 






---
Pipeline Loads Example
Pipeline Loads Example
source: Gedare Bloom and Mary Jane Irwin

---
Instruction-level Parallelism - Pipelining 1
Instruction-level Parallelism - Pipelining
- Does not reduce the execution time of individual instructions, effect is just the opposite...
- Hazards:
  - structural (resolved by duplication),
  - data (result of data dependencies: RAW, WAR, WAW)
  - control (caused by instructions which change PC)...
- Hazard prevention can result in pipeline stall or pipeline flush
- Remark : Deeper pipeline (more stages) results in shorter sequences of gates in each stage which enables to increase the operating frequency of the processor…, but more stages means higher overhead (demand to arrange better instructions into pipeline and result in more significant lag in the case of stall or pipeline flush)

---
Instruction-level Parallelism – Semantics Violations
Instruction-level Parallelism – Semantics Violations
Data hazard:
add x1,x2,x3
sub x4,x1,x3
Control hazard:
beq x3,x4,m1
add x6,x1,x2
instruction 3
instruction 4
m1: add x4,x6,x7
Add writes new value to R1
flow of instructions and expected effect
SUB reads incorrect value from R1
Condition and new PC evaluation
PC set to branch target
Should be these instructions fetched (and executed then)?
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB

---
Non-pipelined Execution
Non-pipelined Execution
SrcA
19:15
Instr
Zero
PC
PC’
Result
ALU
24:20
AluOut
SrcB
ReadData
WriteData
WriteReg
11:7
4
15:0, 24:0
11:7
+
Imm
decode
SignImm
PCPlus4
PCBranch
+
PC
From lecture 3
Instr. Memory
A RD
Data Memory
A RD
WD
WE
Reg.
File
A1 RD1
A2 RD2
A3
WD3
WE3
0
1
0
1
0
1

---
Pipelined Execution
Pipelined Execution
AluOutW
SrcA
19:15
Instr
Zero
PC
PC’
Result
ALU
24:20
AluOutM
SrcB
ReadData
11:7
4
15:0, 24:0
11:7
+
Imm
decode
PCPlus4
PCBranch
SignImm
+
PCD
PCE
PCF
Instr. Memory
A RD
Data Memory
A RD
WD
WE
Reg.
File
A1 RD1
A2 RD2
A3
WD3
WE3
0
1
0
1
0
1
Fetch
Decode
Execute
Memory
WriteBack
WriteDataE
WriteRegE
WriteDataM
WriteRegM
WriteRegW

---
Pipelined Execution with Control Unit
Pipelined Execution with Control Unit
RegWrite
Control Unit
Opcode
Funct
MemToReg
Branch
ALUControl 2:0
6:0
MemWrite
ALUSrc
31:25
14:12
AluOutW
SrcA
19:15
Instr
Zero
PC
PC’
Result
ALU
24:20
AluOutM
SrcB
ReadData
11:7
TypeRISBUJ
4
15:0, 24:0
11:7
+
Imm
decode
PCPlus4
PCBranch
SignImm
+
PCD
PCE
PCF
Fetch
Decode
Execute
Memory
WriteBack
Instr. Memory
A RD
Data Memory
A RD
WD
WE
Reg.
File
A1 RD1
A2 RD2
A3
WD3
WE3
0
1
0
1
0
1
WriteDataE
WriteRegE
WriteDataM
WriteRegM
WriteRegW

---
The Same Design but Drawn Scaled Down…
The Same Design but Drawn Scaled Down…
RegWriteW
RegWriteE
RegWriteM
RegWriteD
Control unit
MemToRegE
MemToRegM
MemToRegD
MemWriteE
MemTo
RegW
MemWriteM
MemWriteD
ALUControlE
ALUControlD
6:0
Op
ALUSrcE
ALUSrcD
TypeRISBUJ
BranchM
31:25, 14:12
Funct
BranchD
BranchE
PCSrcM
Zero
PC´
InstrD
SrcAE
PC
19:15
ALUOutM
ReadDataW
24:20
SrcBE
WriteDataE
WriteDataM
ALUOutW
WriteRegD 4:0
WriteRegW 4:0
WriteRegE 4:0
WriteRegM 4:0
11:7
4
31:25, 24:20
11:7
SignImmD
+
SignImmE
PCBranch
PCPlus4F
+
PCD
PCE
ResultW
0
1
1
0
Data Memory
A
RD
WD
WE
Imm
decode
0
1
Reg.
File
A1
RD1
A2
RD2
A3
WD3
WE3
ALU
Instruction Memory
A
RD

---
Cause of the Data Hazards
Cause of the Data Hazards
1
2
3
4
5
6
7
8
Time (cycles)
s2
s0
add	s0, s2, s3
add
IM
RF
DM
RF
+
s3
s0
t0
and
IM
RF
DM
RF
and	t0, s0, s1
&
s1
s4
t1
or
or	t1, s4, s0
IM
RF
DM
RF
|
s0
s0
t2
sub
sub	t2, s0, s5
IM
RF
DM
RF
-
s5
- Register File – access from two pipeline stages (Decode, WriteBack) – actual write occurs at the first half of the clock cycle, the read in the second half ⇒ there is no hazard for sub s0 input operand
- RAW (Read After Write) hazard – and (or) requires s0 in 3 (4)
- How can such hazard be prevented without pipeline throughput degradation?

---
QtRVSim – Resolve Data Hazard by Stall
QtRVSim – Resolve Data Hazard by Stall
QtRVSim https://github.com/cvut/qtrvsim
https://gitlab.fel.cvut.cz/b35apo/stud-support/-/blob/master/seminaries/qtrvsim/hazards-from-lecture/alu-hazards.S

---
QtRVSim – Resolve Data Hazard by Stall 1
QtRVSim – Resolve Data Hazard by Stall
QtRVSim https://github.com/cvut/qtrvsim
https://gitlab.fel.cvut.cz/b35apo/stud-support/-/blob/master/seminaries/qtrvsim/hazards-from-lecture/alu-hazards.S

---
Forwarding to Avoid Data Hazards
Forwarding to Avoid Data Hazards
1
2
3
4
5
6
7
8
Time (cycles)
s2
s0
add
add	s0, s2, s3
IM
RF
DM
RF
+
s3
s0
t0
and
IM
RF
DM
RF
and	t0, s0, s1
&
s1
s4
t1
or
or	t1, s4, s0
IM
RF
DM
RF
|
s0
s0
t2
sub
sub	t2, s0, s5
IM
RF
DM
RF
-
s5
- If a result is available (computed) before subsequent instruction(s) requires the value then data hazard can be avoided by forwarding
- Hazard case is indicated when some of source registers in EX stage is the same as destination register in stage MEM or WB
- The register numbers are fed to the Hazard Unit
- The RegWrite signal from MEM and WB stage has to be monitored as well to check that register number on WriteReg lines takes effect – lw / sw

---
CPU after previous design steps
CPU after previous design steps
RegWriteW
RegWriteE
RegWriteM
RegWriteD
Control unit
MemToRegE
MemToRegM
MemToRegD
MemWriteE
MemTo
RegW
MemWriteM
MemWriteD
ALUControlE
ALUControlD
6:0
Op
ALUSrcE
ALUSrcD
TypeRISBUJ
BranchM
31:25, 14:12
Funct
BranchD
BranchE
PCSrcM
Zero
PC´
InstrD
SrcAE
PC
19:15
ALUOutM
ReadDataW
24:20
SrcBE
WriteDataE
WriteDataM
ALUOutW
WriteRegD 4:0
WriteRegW 4:0
WriteRegE 4:0
WriteRegM 4:0
11:7
4
31:25, 24:20
11:7
SignImmD
+
SignImmE
PCBranch
PCPlus4F
+
PCD
PCE
ResultW
0
1
1
0
Data Memory
A
RD
WD
WE
Imm
decode
0
1
Reg.
File
A1
RD1
A2
RD2
A3
WD3
WE3
ALU
Instruction Memory
A
RD

---
Data Hazards Solved by Forwarding
Data Hazards Solved by Forwarding
RegWriteW
RegWriteE
RegWriteM
RegWriteD
Control unit
MemToRegE
MemToRegM
MemToRegD
MemWriteE
MemTo
RegW
MemWriteM
MemWriteD
ALUControlE
ALUControlD
6:0
Op
ALUSrcE
ALUSrcD
TypeRISBUJ
BranchM
Funct
31:25, 14:12
BranchD
BranchE
PCSrcM
Zero
PC
PC´
InstrD
SrcAE
19:15
ALUOutM
ReadDataW
24:20
SrcBE
WriteDataE
WriteDataM
ALUOutW
WriteRegE 4:0
WriteRegD 4:0
11:7
WriteRegM 4:0
WriteRegW 4:0
4
31:25, 24:20
11:7
SignImmD
SignImmE
+
Rs1D
Rs1E
19:15
PCBranch
Rs2D
+
PCPlus4F
Rs2E
24:20
PCD
PCE
ResultW
Forward
AE
Forward
BE
RegWrite
W
RegWriteM
Hazard unit
0
1
1
0
Data Memory
A
RD
WD
WE
0
1
Reg.
File
A1
RD1
A2
RD2
A3
WD3
WE3
00
10
01
00
01
10
ALU
Instruction Memory
A
RD
Imm
decode

---
QtRVSim – Resolve Data Hazard by Forwarding
QtRVSim – Resolve Data Hazard by Forwarding
QtRVSim https://github.com/cvut/qtrvsim
https://gitlab.fel.cvut.cz/b35apo/stud-support/-/blob/master/seminaries/qtrvsim/hazards-from-lecture/alu-hazards.S

---
QtRVSim – Resolve Data Hazard by Forwarding 1
QtRVSim – Resolve Data Hazard by Forwarding
QtRVSim https://github.com/cvut/qtrvsim
https://gitlab.fel.cvut.cz/b35apo/stud-support/-/blob/master/seminaries/qtrvsim/hazards-from-lecture/alu-hazards.S

---
QtRVSim – Resolve Data Hazard by Forwarding 2
QtRVSim – Resolve Data Hazard by Forwarding
QtRVSim https://github.com/cvut/qtrvsim
https://gitlab.fel.cvut.cz/b35apo/stud-support/-/blob/master/seminaries/qtrvsim/hazards-from-lecture/alu-hazards.S

---
Data Hazard Avoided by Pipeline Stall
Data Hazard Avoided by Pipeline Stall
1
2
3
4
5
6
7
8
Time (cycles)
s2
s0
lw
IM
RF
DM
RF
lw	s0, 40(x0)
+
s3
trouble
s0
t0
and
IM
RF
DM
RF
and	t0, s0, s1
&
s1
s4
t1
or
or	t1, s4, s0
IM
RF
DM
RF
|
s0
s0
t2
sub
sub	t2, s0, s5
IM
RF
DM
RF
-
s5
- If subsequent instructions require result before it is available in CPU then the pipeline has to be stalled (stall state inserted)
- The stall is mean to solve hazard but affect system throughput
- Pipeline stages preceding that one which is affected by the hazard are stalled until all results required by subsequent instructions are available – results are forwarded to the sink which required their value

---
Data Hazard Avoided by Pipeline Stall 1
Data Hazard Avoided by Pipeline Stall
1
2
3
4
5
6
7
8
9
Time (cycles)
s2
s0
lw
IM
RF
DM
RF
lw	s0, 40(x0)
+
s3
s0
s0
t0
and
RF
DM
RF
IM
RF
and	t0, s0, s1
&
s1
s1
s4
t1
or
or
or	t1, s4, s0
IM
IM
RF
DM
RF
|
s0
s0
Stall
t2
sub
sub	t2, s0, s5
IM
RF
DM
RF
-
s5
- The stall is realized by the holding content of the inter-stage registers (gating their clocks or blocking their latch enable signals)
- Results from colliding stages have to be „discarded“ – certain control signals in CPU (RF or memory write enable, branch gating) are reset (held low)
- Both is achieved by introduction of control signals to hold and/or reset inter-stages registers

---
Processor Design Build Till Now
Processor Design Build Till Now
RegWriteW
RegWriteE
RegWriteM
RegWriteD
Control unit
MemToRegE
MemToRegM
MemToRegD
MemWriteE
MemTo
RegW
MemWriteM
MemWriteD
ALUControlE
ALUControlD
6:0
Op
ALUSrcE
ALUSrcD
TypeRISBUJ
BranchM
Funct
31:25, 14:12
BranchD
BranchE
PCSrcM
Zero
PC
PC´
InstrD
SrcAE
19:15
ALUOutM
ReadDataW
24:20
SrcBE
WriteDataE
WriteDataM
ALUOutW
WriteRegE 4:0
WriteRegD 4:0
11:7
WriteRegM 4:0
WriteRegW 4:0
4
31:25, 24:20
11:7
SignImmD
SignImmE
+
Rs1D
Rs1E
19:15
PCBranch
Rs2D
PCPlus4F
Rs2E
+
24:20
PCD
PCE
ResultW
Forward
AE
Forward
BE
RegWrite
W
RegWriteM
Hazard unit
0
1
1
0
Data Memory
A
RD
WD
WE
0
1
Reg.
File
A1
RD1
A2
RD2
A3
WD3
WE3
00
10
01
00
01
10
ALU
Instruction Memory
A
RD
Imm
decode

---
Processor with Remaining Data Hazards Avoided by Stall
Processor with Remaining Data Hazards Avoided by Stall
RegWriteW
RegWriteE
RegWriteM
RegWriteD
Control unit
MemToRegE
MemToRegM
MemToRegD
MemWriteE
MemTo
RegW
MemWriteM
MemWriteD
ALUControlE
ALUControlD
6:0
Op
ALUSrcE
ALUSrcD
TypeRISBUJ
BranchM
Funct
31:25, 14:12
BranchD
BranchE
PCSrcM
Zero
PC
PC´
InstrD
SrcAE
19:15
ALUOutM
ReadDataW
EN
24:20
SrcBE
WriteDataE
WriteDataM
ALUOutW
WriteRegE 4:0
WriteRegD 4:0
11:7
WriteRegM 4:0
WriteRegW 4:0
4
31:25, 24:20
11:7
SignImmD
SignImmE
+
Rs1D
Rs1E
19:15
PCBranch
Rs2D
PCPlus4F
Rs2E
+
24:20
PCD
PCE
CLR
EN
ResultW
Forward
AE
Forward
BE
RegWrite
W
RegWriteM
Stall F
Stall D
Hazard unit
0
1
1
0
Data Memory
A
RD
WD
WE
0
1
Reg.
File
A1
RD1
A2
RD2
A3
WD3
WE3
00
10
01
00
01
10
ALU
Instruction Memory
A
RD
Imm
decode

---
QtRVSim – Resolve LW Hazard by Stall
QtRVSim – Resolve LW Hazard by Stall
QtRVSim https://github.com/cvut/qtrvsim
https://gitlab.fel.cvut.cz/b35apo/stud-support/-/blob/master/seminaries/qtrvsim/hazards-from-lecture/lw-hazards.S

---
QtRVSim – Resolve LW Hazard by Stall 1
QtRVSim – Resolve LW Hazard by Stall
QtRVSim https://github.com/cvut/qtrvsim
https://gitlab.fel.cvut.cz/b35apo/stud-support/-/blob/master/seminaries/qtrvsim/hazards-from-lecture/lw-hazards.S

---
QtRVSim – Resolve LW Hazard by Stall 2
QtRVSim – Resolve LW Hazard by Stall
QtRVSim https://github.com/cvut/qtrvsim
https://gitlab.fel.cvut.cz/b35apo/stud-support/-/blob/master/seminaries/qtrvsim/hazards-from-lecture/lw-hazards.S

---
Control Hazards (Branch and Jump)
Control Hazards (Branch and Jump)
1
2
3
4
5
6
7
8
Time (cycles)
t1
beq
20: beq	t1,t2,40
IM
RF
DM
RF
+
t2
24: and	t0,s0,s1
s0
t0
and
IM
RF
DM
RF
&
s1
Flush
these
instructions
s4
t1
or
28: or	t1,s4,s0
IM
RF
DM
RF
|
s0
s0
t2
sub
2c: sub	t2,s0,s5
IM
RF
DM
RF
-
s5
30: ...
s2
t3
slt
slt
60: slt	t3,s2,s3
IM
RF
DM
RF
s3
Result is not known before 4th cycle. Why?

---
Control Hazards – Better to Know Result Earlier…
Control Hazards – Better to Know Result Earlier…
1
2
3
4
5
6
7
8
Time (cycles)
t1
beq
20: beq	t1,t2,40
IM
RF
DM
RF
+
t2
Flush
this
instructions
24: and	t0,s0,s1
s0
t0
and
IM
RF
DM
RF
&
s1
28: or	t1,s4,s0
2c: ...
s2
t3
slt
slt
60: slt	t3,s2,s3
IM
RF
DM
RF
s3
- If the result of comparison can be evaluated in the 2nd cycle misprediction penalty can be reduced
- But the processing of the comparison at earlier stage can induce new RAW hazards..!!!

---
Resolve Control Hazards by Early Evaluate and Flush
MIPS Resolve Control Hazards by Early Evaluate and Flush
RegWriteW
RegWriteE
RegWriteM
RegWriteD
Control unit
MemToRegE
MemToRegM
MemToRegD
MemWriteE
MemTo
RegW
MemWriteM
MemWriteD
ALUControlE
ALUControlD
31:26
Op
ALUSrcE
ALUSrcD
RegDstE
RegDstD
5:0
Funct
BranchD
EquaD
PCSrcD
=
PC
PC´
InstrD
SrcAE
25:21
ALUOutM
ReadDataW
EN
20:16
SrcBE
WriteDataE
WriteDataM
RsD
RsE
25:21
ALUOutW
RtD
RtE
20:16
WriteRegE 4:0
WriteRegM 4:0
WriteRegW 4:0
15:11
RdD
RdE
SignImmD
15:0
SignImmE
4
PCPlus4D
PCPlus4F
CLR
EN
CLR
PCBranchD
ResultW
Forward
AE
Forward
BE
RegWrite
W
RegWriteM
Stall F
Stall D
Hazard unit
0
1
+
0
1
1
0
Data Memory
A
RD
WD
WE
<<2
Sign
Ext
+
ALU
0
1
00
10
01
00
01
10
Reg.
File
A1
RD1
A2
RD2
A3
WD3
WE3
Instruction Memory
A
RD

---
Resolve RAW Hazards by Forwarding or Stalling
MIPS Resolve RAW Hazards by Forwarding or Stalling
Forward /
Stall
Stall
RegWriteW
RegWriteE
RegWriteM
RegWriteD
Control unit
MemToRegE
MemToRegM
MemToRegD
MemWriteE
MemTo
RegW
MemWriteM
MemWriteD
ALUControlE
ALUControlD
31:26
Op
ALUSrcE
ALUSrcD
RegDstE
RegDstD
5:0
Funct
BranchD
EquaD
PCSrcD
=
PC
PC´
InstrD
SrcAE
25:21
ALUOutM
ReadDataW
EN
20:16
SrcBE
WriteDataE
WriteDataM
RsD
RsE
25:21
ALUOutW
RtD
RtE
20:16
WriteRegE 4:0
WriteRegM 4:0
WriteRegW 4:0
15:11
RdD
RdE
SignImmD
15:0
SignImmE
4
No
Action
Required
PCPlus4D
PCPlus4F
CLR
EN
CLR
PCBranchD
ResultW
Forward
AE
Forward
BE
RegWrite
W
Forward
BD
RegWriteM
Stall F
Stall D
BranchD
Hazard unit
0
1
+
0
1
1
0
Data Memory
A
RD
WD
WE
<<2
Sign
Ext
+
ALU
0
1
00
10
01
00
01
10
0
1
0
1
Reg.
File
A1
RD1
A2
RD2
A3
WD3
WE3
Instruction Memory
A
RD

---
QtMips – Resolve BEQ Source Hazard by Stall
QtMips – Resolve BEQ Source Hazard by Stall
Memory
Program
Cache
Hit:	8
Miss:	7
Memory
Data
Cache
Hit:	0
Miss:	0
Registers
ALU
Peripherals
Terminal
PC
0x80020040
+
4
Control
unit
Sign
extension
<<2
+
=
NONE
Exception
JumpReg
PcToR31
MemToReg
MemWrite
MemRead
AluCtrl
RegDest
AluSrc
Branch
1
0
112a0003
00001234
00000000
00000003
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
00000000
0
0
00
0
0
0
0
0
0
1
2
3
4
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
2
3
4
RsD
9
RtD
10
RtD
10
RdD
0
9
Cycles
Stalls
IF/ID
ID/EX
EX/MEM
MEM/WB
AND $8, $16, $17
BEQ $9, $10, 0x80020040
NOP
ADDI $10, $0, 4660
ADDI $9, $0, 4660
Hazard	Unit
STALL
FORWARD
NORMAL
RegWrite
1
0
0
1
RtE
0
RdE
0
0
10
RsE
0
0
0
0
1
AND $t0, $s0, $s1
BEQ $t1, $t2, 0x80020040
NOP
ADDI $t2, $0, 4660
ADDI $t1, $0, 4660

---
QtMips – Resolve BEQ Control Hazard
QtMips – Resolve BEQ Control Hazard
Memory
Program
Cache
Hit:	8
Miss:	8
Memory
Data
Cache
Hit:	0
Miss:	0
Registers
ALU
Peripherals
Terminal
PC
0x80020044
+
4
Control
unit
Sign
extension
<<2
+
=
NONE
Exception
JumpReg
PcToR31
MemToReg
MemWrite
MemRead
AluCtrl
RegDest
AluSrc
Branch
0
0
02114024
00000000
11111111
00004024
0
0
0
0
1
0
0
0
0
0
1
2
3
4
0
0
0
0
1
2
3
4
0
0
0
0
1
2
3
4
00000003
0
0
00
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
2
3
4
RsD
16
RtD
17
RtD
17
RdD
8
10
Cycles
Stalls
IF/ID
ID/EX
EX/MEM
MEM/WB
SLT $11, $18, $19
AND $8, $16, $17
BEQ $9, $10, 0x80020040
NOP
ADDI $10, $0, 4660
Hazard	Unit
NORMAL
NORMAL
NORMAL
RegWrite
1
1
0
0
RtE
10
RdE
0
10
0
RsE
9
0
0
0
0
SLT $t3, $s2, $s3
AND $t0, $s0, $s1
BEQ $t1, $t2, 0x80020040
NOP
ADDI $t2, $0, 4660

---
Branch Prediction and Speculative Execution
Branch Prediction and Speculative Execution

---
We are Finished – Pipelined Processor is Designed
We are Finished – Pipelined Processor is Designed
RegWriteW
RegWriteE
RegWriteM
RegWriteD
Control unit
MemToRegE
MemToRegM
MemToRegD
MemWriteE
MemTo
RegW
MemWriteM
MemWriteD
ALUControlE
ALUControlD
6:0
Op
ALUSrcE
ALUSrcD
TypeRISBUJ
BranchM
Funct
31:25, 14:12
BranchD
BranchE
PCSrcM
Zero
PC
PC´
InstrD
SrcAE
19:15
ALUOutM
ReadDataW
EN
24:20
SrcBE
WriteDataE
WriteDataM
ALUOutW
WriteRegE 4:0
WriteRegD 4:0
11:7
WriteRegM 4:0
WriteRegW 4:0
4
31:25, 24:20
11:7
SignImmD
SignImmE
+
Rs1D
Rs1E
19:15
PCBranch
Rs2D
PCPlus4F
Rs2E
+
24:20
PCD
PCE
CLR
EN
ResultW
Forward
AE
Forward
BE
RegWrite
W
RegWriteM
Stall F
Stall D
Hazard unit
0
1
1
0
Data Memory
A
RD
WD
WE
0
1
Reg.
File
A1
RD1
A2
RD2
A3
WD3
WE3
00
10
01
00
01
10
ALU
Instruction Memory
A
RD
Imm
decode

---
Pipelined CPU – Performance: IPS
Pipelined CPU – Performance: IPS = IC / T = IPCavg.fCLK
- What is maximal acceptable frequency for the CPU?
- Which stage is the slowest one?
- The cycle time is determined by the slowest stage
- For our case:
  Tc = 300 ns --> 3 333 kHz
  If the pipeline fill overhead is neglected (i.e. no pipeline stalls and flushes are considered) then ideal IPC = 1.
  IPS = 1 • 3 333e3 = 3 333 000 instructions per second
- Introduction of the 5-stage pipeline increases performance (throughput) 3 333 000/ 980 000 = 3.4 times! (considering IPC=1)

---
What is Result of the Design?
What is Result of the Design?
Return back to non-pipelined CPU version
MemWrite
MemToReg
Branch
ALUControl 2:0
ALUScr
TypeRISBUJ
RegWrite
+
+
4
PC’
PC
Instr
19:15
24:20
11:7
15:0, 24:0
11:7
SrcA
SrcB
Zero
AluOut
WriteData
WriteReg
PC
PCBranch
ReadData
Result
PCPlus4
Instr. Memory
A RD
Data Memory
A RD
WD
WE
Reg.
File
A1 RD1
A2 RD2
A3
WD3
WE3
0
1
0
1
0
1
Imm
decode
6:0
31:25, 14:12
Control Unit
Opcode
Funct
SignImm
ALU

---
What is Result of the Design? 1
What is Result of the Design?
Return back to non-pipelined CPU version
Control unit
(control path)
Memory
WE
Instr. Memory
A RD
A RD
A RD
WD
Data/ALU
(data path)
WE
WE
Data Memory
A RD
WD
MemWrite
MemToReg
Branch
ALUControl 2:0
ALUScr
TypeRISBUJ
RegWrite
+
+
4
PC’
PC
Instr
19:15
24:20
11:7
15:0, 24:0
11:7
SrcA
SrcB
Zero
AluOut
WriteData
WriteReg
PC
PCBranch
ReadData
Result
PCPlus4
Reg.
File
A1 RD1
A2 RD2
A3
WD3
WE3
0
1
0
1
0
1
Imm
decode
6:0
31:25, 14:12
Control Unit
Opcode
Funct
SignImm
ALU

---
What is Result of the Design? 2
What is Result of the Design?
Processor
Control unit
PC
PC
Instr. Memory
Instruction
Data-path
(ALU, registers)
A RD
RD A
Write enable
Address for data Read/Write
WE
Data Memory
Address
Read data
RD A
A RD
Results
Data to Write
WD
WD

---
CPU Design Result – Pipelined Version
CPU Design Result – Pipelined Version
RegWriteW
RegWriteE
RegWriteM
RegWriteD
Control unit
MemToRegE
MemToRegM
MemToRegD
MemWriteE
MemTo
RegW
MemWriteM
MemWriteD
ALUControlE
ALUControlD
6:0
Op
ALUSrcE
ALUSrcD
TypeRISBUJ
BranchM
Funct
31:25, 14:12
BranchD
BranchE
PCSrcM
Zero
PC
PC´
InstrD
SrcAE
19:15
ALUOutM
ReadDataW
EN
24:20
SrcBE
WriteDataE
WriteDataM
ALUOutW
WriteRegE 4:0
WriteRegD 4:0
11:7
WriteRegM 4:0
WriteRegW 4:0
4
31:25, 24:20
11:7
SignImmD
SignImmE
+
Rs1D
Rs1E
19:15
PCBranch
Rs2D
PCPlus4F
Rs2E
+
24:20
PCD
PCE
CLR
EN
ResultW
Forward
AE
Forward
BE
RegWrite
W
RegWriteM
Stall F
Stall D
Hazard unit
0
1
1
0
Data Memory
A
RD
WD
WE
0
1
Reg.
File
A1
RD1
A2
RD2
A3
WD3
WE3
00
10
01
00
01
10
ALU
Instruction Memory
A
RD
Imm
decode

---
Pipelined CPU – Timing
Pipelined CPU – Timing
The timing/AC characteristics of synchronous sequential circuit :
tsetup – inputs setup time
thold – inputs hold time
Signal integrity constrain for the setup time before the clock:
Tc >= tpcq + tpd + tsetup
tpd – combinatorial logic propagation delay

---
Pipelined Processor – Timing
Pipelined Processor – Timing
Constraint for the setup time (consider the clock distribution jitter):
Tc >= tpcq + tpd + tsetup + tskew
Clock distribution jitter is limiting factor,
if it reaches or exceeds value of tpd
(too deep pipeline / too many stages…)

---
Clock Distribution Network Skew
Clock Distribution Network Skew
- Positive Clock Skew – clock arrives at the capturing sequential later than it arrives at the launching sequential
- Negative Clock Skew – clock arrives at the launching sequential later than it arrives at the capturing sequential
- Local Clock Skew – skew between any two sequentials with a valid timing path between them.
- Global Clock Skew – clock skew between any two sequentials in the design irrespective of whether a timing paths exists between them
diagram source: peda clock-tree-skew
2
1
2
1
2
1
2
1
R
1
S
4
Q
6
CLK
3
Q
5
D
2
FF1
1
3
2
3
2
1
R
1
S
4
Q
6
CLK
3
Q
5
D
2
FF2
2
1
CLK
Data IN
Data OUT
X
Y
Z
3
2
1

---
Clock Distribution Network
Clock Distribution Network – H-tree
2
2
1
1
3
4
4
3
CLK-in
source: Tawfik, S., Kursun, V.: Clock Distribution Networks with Gradual Signal Transition Time Relaxation for Reduced Power Consumption.

---
Pipeline Stages Balancing
Pipeline Stages Balancing
Linear pipelining:
(applies to tree based adder, multiplier, (unrolled) iterative divider..)
- Balancing: the goal is to divide the processing into N stages in such way, that stage propagation delays are roughly the same…
- The number of stages reflects preference of performance (throughput) versus latency.

---
Superpipeline and Beyond
Superpipeline and Beyond
Not well balanced 5-stage pipeline:
IF	ID EX	MEM	WB
Deeper pipeline is result of decomposing stages into more stages
IF IS RF EX DF DS TC WB
- It allows CPU to work at higher frequencies but introduces many problems as well..
- Complex forwarding, more pipeline stalls, hazards need to be solved by complex logic
DM
RF
IM
RF
DM
RF
IM
RF

---
Typical Pipeline Depths in Today's CPUs
Typical Pipeline Depths in Today's CPUs
P5 (Pentium) : 5
P6 (Pentium 3): 10
P6 (Pentium Pro): 14
NetBurst (Willamette, 180 nm) - Celeron, Pentium 4: 20
NetBurst (Northwood, 130 nm) - Celeron, Pentium 4, Pentium 4 HT: 20
NetBurst (Prescott, 90 nm) - Celeron D, Pentium 4, Pentium 4 HT, Pentium 4 ExEd: 31
NetBurst (Cedar Mill, 65 nm): 31
NetBurst (Presler 65 nm) - Pentium D:	31
Core : 14
Bonnell: 16
K7 Architecture - Athlon : 10-15
K8 - Athlon 64, Sempron, Opteron, Turion 64: 12-17
ARM 8-9: 5
ARM 11: 8
Cortex A7 2-wide 8-10
Cortex A8 2-wide 13
Cortex A15 3-wide 15-25
Haswell 14-19
Cooper Lake 14-19
AMD Zen 19
AMD Zen2 19
Cortex-A35 2-wide 8
Cortex-A53 2-wide 8
Cortex-A57 3-wide 15
Cortex-A77 4-wide 11–13
Denver 2/7-wide 13
M4 6-wide 15
Lightning 7-wide 16
SiFive FE310-G000 5
SiFive FU540-C000 5
The Optimum Pipeline Depth for a Microprocessor: http://citeseerx.ist.psu.edu/viewdoc/download?doi=10.1.1.93.4333&rep=rep1&type=pdf

---
Branch Stall Discussion and Delay Slots
Branch Stall Discussion and Delay Slots
- The instruction memory read and fetch is expensive and result of condition evaluation in branch instructions (even worse target in indirect branch instructions) has to be evaluated before next fetch and execute. The stall state is waste of cycles. Options to use that cycle(s) are:
  - Start fetch and execution of instruction(s) following branch and flush/discard results if it is resolved that it should not be executed
  - Extend above by adding condition results/branch predictor (taken/not-taken) and branch target cache (BTB)
  - Execute one or more instructions after branch unconditionally in (so called) delay slot
- Delay slots unconditional execution is common for many DSP (digital signal processor) and some RISC architectures (MIPS, SPARC)