Computer Architectures
Number Representation and Computer Arithmetics
Pavel Píša, Michal Štepanovský, Miroslav Šnorek
Czech Technical University in Prague, Faculty of Electrical Engineering
English version partially supported by:
European Social Fund Prague & EU: We invests in your future.
Ver.1.10

---
Today PC Computer Base Platform – Motherboard

---
Block Diagram of Components Interconnection
Microprocessor
Root
complex
End
point
End
point
End
point
RAM
RAM
RAM
End
point
End
point
End
point
End
point
End
point
End
point
End
point
Switch

---
Block Diagram of Components Interconnection
GPU
Microprocessor
Root
complex
End
point
End
point
End
point
RAM
RAM
RAM
End
point
End
point
End
point
End
point
End
point
End
point
End
point
Switch

---
Block Diagram of Components Interconnection
Additional USB ports
Wi-fi?
GPU
Microprocessor
Root
complex
End
point
End
point
End
point
RAM
RAM
RAM
End
point
End
point
End
point
End
point
End
point
End
point
End
point
Switch

---
Lectures Topics in the Diagram
Lecture 4
Memory subsystem – virtual memory, paging
Lecture 7
Input/output subsystem from SW perspective.
Lecture 2 Design of simple single-cycle CPU Instruction execution.
Control unit.
Lecture 5
Pipelined instruction execution, hazards causes and resolution
Lecture 6
Input/output subsystem from HW perspective. PCI buses, PCIe interconnection, USB, SerialATA, HyperTransport, QuickPath interconnect
Microprocessor
Root
complex
End
point
End
point
End
point
RAM
RAM
RAM
End
point
End
point
End
point
End
point
End
point
End
point
End
point
Switch
Lecture 3
Memory subsystem – hierachical concept. Static and dynamic memory

---
Computer
Application
Algorithm
APO course interest
Programming Language
Operating System/Virtual Machine
Instruction Set Architecture (ISA)
Microarchitecture
Gates/Register-Transfer Level (RTL)
Circuits
Devices
Physics
Reference: John Kubiatowicz: EECS 252 Graduate Computer Architecture, Lecture 1. University of California, Berkeley
Original domain of the computer architects
(‘50s-’80s)
Domain of recent computer architecture
(‘90s - ???)
Reliability, power, …
Parallel computing, security, …

---
Reasons to study computer architectures
- To invent/design new computer architectures
- To be able to integrate selected architecture into silicon
- To gain knowledge required to design computer hardware/systems (big ones or embedded)
- To understand generic questions about computers, architectures and performance of various architectures
- To understand how to use computer hardware efficiently (i.e. how to write good software)
  - It is not possible to efficiently use resources provided by any (especially by modern) hardware without insight into their constraints, resource limits and behavior
  - It is possible to write some well paid applications without real understanding but this requires abundant resources on the hardware level. But no interesting and demanding tasks can be solved without this understanding.

---
More motivation and examples
- The knowledge is necessary for every programmer who wants to work with medium size data sets or solve little more demanding computational tasks
- No multimedia algorithm can be implemented well without this knowledge
- The 1/3 of the course is focussed even on peripheral access
- Examples
  - Facebook – HipHop for PHP  C++/GCC  machine code
  - BackBerry (RIM) – our consultations for time source
  - RedHat – JAVA JIT for ARM for future servers generation
  - Multimedia and CUDA computations
  - Photoshop, GIMP (data/tiles organization in memory)
  - Knot-DNS (RCU, Copy on write, Cuckoo hashing, )

---
The course's background and literature
- Course is based on worldwide recognized book and courses; evaluation Graduate Record Examination – GRE
  Paterson, D., Henessy, J.: Computer Organization and Design, The HW/SW Interface. Elsevier, ISBN: 978-0-12-370606-5
  - John L. Henessy – president of Stanford University, one of founders of MIPS Computer Systems Inc.
  - David A. Patterson – leader of Berkeley RISC project and RAID disks research
- Our experience even includes distributed systems, embedded systems design (of mobile phone like complexity), peripherals design, cooperation with carmakers, medical and robotics systems design

---
Topics of the lectures
- Architecture, structure and organization of computers and its subsystems.
- Central Processing Unit (CPU)
- Memory
- Pipelined instruction execution
- Input/output subsystem of the computer
- Input/output subsystem (part 2)
- External events processing and protection
- Processors and computers networks
- Parameter passing
- Classic register memory-oriented CISC architecture
- INTEL x86 processor family
- CPU concepts development (RISC/CISC) and examples
- Multi-level computer organization, virtual machines
- Analog and digital I/O interfacing

---
The 1. lecture contents
- Number representation in computers
  - numeral systems
  - integer numbers, unsigned and signed
  - floating point representation for real numbers
  - boolean values
- Basic arithmetic operations and their implementation
  - addition, subtraction
  - shift right/left
  - multiplication and division

---
Motivation: What is the output of next code snippet?
int main() {
int a = -200;
printf("value: %u = %d = %f = %c \n", a, a, *((float*)(&a)), a);
return 0;
}
value: 4294967096 = -200 = nan = 8
and memory content is: 0x38 0xff 0xff 0xff
when run on little endian 32 bit CPU.

---
Terminology basics
- Positional (place-value) notation
- Decimal/radix point
- z … base of numeral system
- smallest representable number
- Module = , one increment/unit higher than biggest representable number for given encoding/notation
- A, the representable number for given n and m selection, where k is natural number in range 0,zn+m+1 -1
- The representation and value
radix point
an
an-1
a0
a-1
a-m
n
-m
-1
0
…
…

---
Integer number representation (unsigned, non-negative)
- The most common numeral system base in computers is z=2
- The value of ai is in range {0,1,…z-1}, i.e. {0,1} for base 2
- This maps to true/false and unit of information (bit)
- We can represent number 0 … 2n-1 when n bits are used
- Which range can be represented by one byte?
  1B (byte) … 8 bits, 28 = 256d combinations, values 0 … 255d = 0b11111111b
- Use of multiple consecutive bytes
  - 2B … 216 = 65536d, 0 … 65535d = 0xFFFFh ,(h … hexadecimal, base 16, a in range 0, … 9, A, B, C, D, E, F)
  - 4B … 232 = 4294967296d, 0 … 4294967295d = 0xFFFFFFFFh

---
Signed integer numbers
- Work with negative numbers is required for many applications
- When appropriate representation is used then same hardware (with minor extension) can be used for many operations with signed and unsigned numbers
- Possible representations
  - sign-magnitude code, direct representation, sign bit
  - two's complement
  - ones' complement
  - excess-K, offset binary or biased representation

---
Integer – sign-magnitude code
- Sign and magnitude of the value (absolute value)
- Natural to humans -1234, 1234
- One (usually most significant – MSB) bit of the memory location is used to represent the sign
- Bit has to be mapped to meaning
- Common use 0 ≈ “+”, 1 ≈ “-”
- Disadvantages:
  - When location is k bits long then only k-1 bits hold magnitude and each operation has to separate sign and magnitude
  - Two representations of the value 0
-2n-1+1 … 0 … 2n-1-1

---
Integer – two's complement
- Other option is to designate one half of range/combinations for non-negative numbers and other one for positive numbers
- Transform to the representation
  D(A) = A	iff A≥0
  D(A) = Z-∣A∣	iff A<0
- Advantages
  - Continuous range when cyclic arithmetics is considered
  - Single and one to one mapping of value 0
  - Same HW for signed and unsigned adder
- Disadvantage
  - Asymmetric range (-(-1/2Z))
-2n-1 … 0 … 2n-1-1

---
Integers – ones' complement
- Transform to the representation
  D(A) = A	iff A≥0
  D(A) = Z-1-∣A∣	iff A<0 (i.e. subtract from all ones)
- Advantages
  - Symmetric range
  - Almost continuous, requires hot one addition when sign changes
- Disadvantage
  - Two representations of value 0
  - More complex hardware
- Negate (-A) value can be computed by bitwise complement (flipping) of each bit in representation
-2n-1+1 … 0 … 2n-1-1

---
Integer – biased representation
- Known as excess-K or offset binary as well
- Transform to the representation
  D(A) = A+K
- Usually K=Z/2
- Advantages
  - Preserves order of original set in mapped set/representation
- Disadvantages
  - Needs adjustment by -K after addition and +K after subtraction processed by unsigned arithmetic unit
  - Requires full transformation before and after multiplication
-K … 0 … 2n-1-K

---
Back to two's complement and the C language
- Two's complement is most used signed integer numbers representation in computers
- Complement arithmetic is often used as its synonym
- “C” programing language speaks about integer numeric type without sign as unsigned integers and they are declared in source code as unsigned int.
- The numeric type with sign is simply called integers and is declared as signed int.
- Examples of the values representations when 32 bits are used:
  - 0D = 00000000H,
  - 1D = 00000001H, -1D = FFFFFFFFH,
  - 2D = 00000002H, -2D = FFFFFFFEH,
  - 3D = 00000003H, -3D = FFFFFFFDH,
- Considerations about value overflow and underflow from order grit are discussed later.

---
Two's complement – addition and subtraction
- Addition
  - 0000000 0000 0111B ≈ 7D Symbols use: 0=0H, 0=0B
  - + 0000000 0000 0110B ≈ 6D
  - 0000000 0000 1101B ≈ 13D
- Subtraction can be realized as addition of negated number
  - 0000000 0000 0111B ≈ 7D
  - + FFFFFFF 1111 1010B ≈ -6D
  - 0000000 0000 0001B ≈ 1D
- Question for revision: how to obtain negated number in two's complement binary arithmetics?

---
Binary adder hadrware
Hardware of ripple-carry adder
Common symbol for adder
Internal structure
Realized by 1-bit full adders
where half adder is
x y
z
w
w = x y
z =x . y

---
Fast parallel adder realization and limits
- The previous, cascade based adder is slow – carry propagation delay
- The parallel adder is combinatorial circuit, it can be realized through sum of minterms (product of sums), two levels of gates (wide number of inputs required)
- But for 64-bit adder 1020 gates is required
Solution #1
Use of carry-lookahead circuits in adder combined with adders without carry bit
Solution #2
Cascade of adders with fraction of the required width
Combination (hierarchy) of #1 and #2 can be used for wider inputs

---
Speed of the adder
- Parallel adder is combinational logic/circuit. Is there any reason to speak about its speed? Try to describe!
- Yes, and it is really slow. Why?
- Possible enhancement – adder with carry-lookahead (CLA) logic!
carry-lookahead

---
CLA – carry-lookahead
- Adder combined with CLA provides enough speedup when compared with parallel ripple-carry adder and yet number of additional gates is acceptable
- CLA for 64-bit adder increases hardware price for about 50% but the speed is increased (signal propagation time decreased) 9 times.
- The result is significant speed/price ratio enhancement.

---
The basic equations for the CLA logic
- Let:
  - the generation of carry on position (bit) j is defined as:
  - the need for carry propagation from previous bit:
- Then:
  - the result of sum for bit j is given by:
  - and carry to the higher order bit (j+1) is given by:
size 12{g rSub { size 8{j} } =x rSub { size 8{j} } y rSub { size 8{j} } } {}
size 12{p rSub { size 8{j} } =x rSub { size 8{j} } ⊕y rSub { size 8{j} } =x rSub { size 8{j} } { bar {y}} rSub { size 8{j} } or { bar {x}} rSub { size 8{j} } y rSub { size 8{j} } } {}
size 12{s rSub { size 8{j} } =c rSub { size 8{j} } left ( {overline {x rSub { size 8{j} } ⊕y rSub { size 8{j} } }} right ) or { bar {c}} rSub { size 8{j} } left (x rSub { size 8{j} } ⊕y rSub { size 8{j} } right )=c rSub { size 8{j} } { bar {p}} rSub { size 8{j} } or { bar {c}} rSub { size 8{j} } p rSub { size 8{j} } =p rSub { size 8{j} } ⊕c rSub { size 8{j} } } {}
size 12{c rSub { size 8{j+1} } =x rSub { size 8{j} } y rSub { size 8{j} } or left (x rSub { size 8{j} } ⊕y rSub { size 8{j} } right )c rSub { size 8{j} } =g rSub { size 8{j} } or p rSub { size 8{j} } c rSub { size 8{j} } } {}

---
CLA
The carry can be computed as:
c1 = g0  p0c0
c2 = g1  p1c1 = g1  p1(g0  p0c0) = g1  p1g0  p1p0c0
c3 = g2  p2c2 = g2  p2(g1  p1g0  p1p0c0) = g2  p2g1  p2p1g0  p2p1p0c0
c4 = g3  p3c3 = ... = g3  p3g2  p3p2g1  p3p2p1g0  p3p2p1p0c0
c5 = ...
  Description of the equation for c3 as an example:
The carry input for bit 3 is active when carry is generated in bit 2 or carry propagates condition holds for bit 2 and carry is generated in the bit 1 or both bits 2 and 1 propagate carry and carry is generated in bit 0

---
Arithmetic unit for add/subtract operations
Inspiration: X36JPO, A. Pluháček
SUB
ADD
bitwise not

---
Arithmetic overflow (underflow)
- Result of the arithmetic operation is incorrect because, it does not fit into selected number of the representation bits (width)
- But for the signed arithmetics, it is not equivalent to the carry from the most significant bit.
- The arithmetic overflow is signaled if result sign is different from operand signs if both operands have same sign
- or can be detected with exclusive-OR of carry to and from the most significant bit

---
Arithmetic shift to the left and to the right
- arithmetic shift by one to the left/right is equivalent to signed multiply/divide by 2 (digits movement in positional (place-value) representation)
- Notice difference between arithmetic, logic and cyclic shift operations
loss of the
precision
Remark: Barrel shifter can be used for fast variable shifts

---
Addition and subtraction for the biased representation
Short note about other signed number representation
- Overflow detection
  - for addition:
    same sign of addends and different result sign
  - for subtraction:
    signs of minuend and subtrahend are opposite and sign of the result is opposite to the sign of minuend

---
Unsigned binary numbers multiplication

---
Sequential hardware multiplier (32b case)
AC MQ
The speed of the multiplier is horrible

---
Algorithm for multiplication
A = multiplicand;
MQ = multiplier;
AC = 0;
for( int i=1; i <= n; i++) // n – represents number of bits
{
if(MQ0 = = 1) AC = AC + A; // MQ0 = LSB of MQ
SR (shift AC MQ by one bit right and insert information about carry from the MSB from previous step)
}
end.
when loop ends AC MQ holds 64-bit result

---
Example of the multiply X by Y
Multiplicand x=110 and multiplier y=101.
i	operation	AC	MQ	A	comment
		000	101	110	initial setup
1	AC = AC+MB	110	101		start of the cycle
	SR	011	010
2	nothing	011	010		because of MQ0 = = 0
	SR	001	101
3	AC = AC+MB	111	101
	SR	011	110		end of the cycle
The whole operation: xy = 110101 = 011110, ( 65 = 30 )

---
Signed multiplication by unsigned HW for two's complement
One possible solution
C = A • B
Let A and B representations are n bits and result is 2n bits
D(C) = D(A) • D(B)
– (D(B)<<n)	if A < 0
– (D(A)<<n)	if B < 0
Consider for negative numbers
(2n+A) • (2n+B) = 22n+2n A + 2n B + A•B
where 22n is out of the result representation, next two elements have to be eliminated if input is negative

---
Wallace tree based multiplier
Q=X .Y, X and Y are considered as and 8bit unsigned numbers
( x7 x6 x5 x4 x­3 x2 x1 x0). (y7 y6 y5 y4 y3 y2 y1 y0) =
0	0	0	0	0	0	0	0	x7y0	x6y0	x5y0	x4y0	x3y0	x2y0	x1y0	x0y0	P0
0	0	0	0	0	0	0	x7y1	x6y1	x5y1	x4y1	x3y1	x2y1	x1y1	x0y1	0	P1
0	0	0	0	0	0	x7y2	x6y2	x5y2	x4y2	x3y2	x2y2	x1y2	x0y2	0	0	P2
0	0	0	0	0	x7y3	x6y3	x5y3	x4y3	x3y3	x2y3	x1y3	x0y3	0	0	0	P3
0	0	0	0	x7y4	x6y4	x5y4	x4y4	x3y4	x2y4	x1y4	x0y4	0	0	0	0	P4
0	0	0	x7y5	x6y5	x5y5	x4y5	x3y5	x2y5	x1y5	x0y5	0	0	0	0	0	P5
0	0	x7y6	x6y6	x5y6	x4y6	x3y6	x2y6	x1y6	x0y6	0	0	0	0	0	0	P6
0	x7y7	x6y7	x5y7	x4y7	x3y7	x2y7	x1y7	x0y7	0	0	0	0	0	0	0	P7
Q15	Q14	Q13	Q12	Q11	Q10	Q9	Q8	Q7	Q6	Q5	Q4	Q3	Q2	Q1	Q0
The sum of P0+P1+...+P7 gives result of X and Y multiplication.
Q = X .Y = P0 + P1 + ... + P7

---
Wallace tree based fast multiplier
The basic element is an CSA circuit (Carry Save Adder)
S = Sb + C
Sbi = xi  yi  zi
Ci+1 = xi yi + yi zi + zi xi


&
&
&
1

---
Hardware divider
negate
hot one
return
reminder
quotient

---
Hardware divider logic (32b case)
divident = quotient  divisor + reminder
negate
hot one
AC MQ
return
reminder
quotient

---
Algorithm of the sequential division
MQ = dividend;
B = divisor; (Condition: divisor is not 0!)
AC = 0;
for( int i=1; i <= n; i++)	{
SL (shift AC MQ by one bit to the left, the LSB bit is kept on zero)
if(AC >= B) {
AC = AC – B;
MQ0 = 1;	// the LSB of the MQ register is set to 1
}
}
 Value of MQ register represents quotient and AC remainder

---
Example of X/Y division
Dividend x=1010 and divisor y=0011
i	operation	AC	MQ	B	comment
		0000	1010	0011	initial setup
1	SL	0001	0100
	nothing	0001	0100		the if condition not true
2	SL	0010	1000
		0010	1000		the if condition not true
3	SL	0101	0000		r  y
	AC = AC – B; MQ0 = 1;	0010	0001
4	SL	0100	0010		r  y
	AC = AC – B; MQ0 = 1;	0001	0011		end of the cycle
x : y = 1010 : 0011 = 0011 reminder 0001, (10 : 3 = 3 reminder 1)

---
Higher dynamic range for numbers (REAL/float)
- Scientific notation, semilogarithmic, floating point
  - The value is represented by:
    - EXPONENT (E) – represents scale for given value
    - MANTISSA (M) – represents value in that scale
    - the sign(s) are usually separated as well
- Normalized notation
  - The exponent and mantissa are adjusted such way, that mantissa is held in some standard range. 〈0.5, 1) or 〈1, 2) for considered base z=2
  - Generally: the first digit is non-zero or mantissa range is 〈1, z)

---
Standardized format for REAL type numbers
- Standard IEEE-754 defines next REAL representation and precision
  - single-precision – in the C language declared as float
  - double-precision – C language double

---
Examples of (de)normalized numbers in base 10 and 2
binary
The radix point position for E and M
Sign of M

---
The representation/encoding of floating point number
- Mantissa encoded as the sign and absolute value (magnitude) – equivalent to the direct representation
- Exponent encoded in biased representation (K=127 for single precision)
- The implicit leading one can be ommited due to normalization of m ∈ 〈1, 2) – 23+1 implicit bit for single
X = -1s 2A(E)-127 m
where m ∈ 〈1, 2)
m = 1 + 2-23 M
Radix point position for E and M
Sign of M

---
Implied (hidden) leading 1 bit
- Most significant bit of the mantissa is one for each normalized number and it is not stored in the representation for the normalized numbers
- If exponent representation is zero then encoded value is zero or denormalized number which requires to store most significant bit
- Denormalized numbers allow to keep resolution in the range from the smallest normalized number to zero

---
Underflow/lost of the precision for IEEE-754 representation
- The case where stored number value is not zero but it is smaller than smallest number which can be represented in the normalized form
- The direct underflow to the zero can be prevented by extension of the representation range by denormalized numbers
smallest representable number
denormalized
0
underflow
normalized
normalized numbers

---
ANSI/IEEE Std 754-1985 – 32b a 64b formats
ANSI/IEEE Std 754-1985 — single precision format — 32b
fraction point
ANSI/IEEE Std 754-1985 — double precision format — 64b
g . . . 11b
f . . . 52b

---
Representation of the fundamental values
Zero
Positive zero	0 00000000 00000000000000000000000	+0.0
Negative zero	1 00000000 00000000000000000000000	-0.0
Infinity
Positive infinity	0 11111111 00000000000000000000000	+0.0
Negative infinity	1 11111111 00000000000000000000000	-0.0
Representation corner values
Smallest normalized	* 00000001 00000000000000000000000	±2(1-127) / ±1.1755 10-38
Biggest denormalized	* 00000000 11111111111111111111111	±(1-2-23)2(1-126)
Smallest denormalized	* 00000000 00000000000000000000001	±2-232-126 / ±1.4013 10-45
Max. value	0 11111110 11111111111111111111111	(2-2-23)2(127) / +3.4028 10+38

---
Not a number (NaN)
- All ones in the exponent
- Mantissa not equal to the zero
- Used, where no other value fits (i.e. +Inf + -Inf, 0/0)
- Compare to (X+ +Inf) where +Inf is sane result

---
IEEE-754 special values summary
sign bit	Exponent representation	Mantissa	Represented value/meaning
0	0<e<255	any value	normalized positive number
1	0<e<255	any value	normalized negative number
0	0	>0	denormalized positive number
1	0	>0	denormalized negative number
0	0	0	positive zero
1	0	0	negative zero
0	255	0	positive infinity
1	255	0	negative infinity
0	255	≠0	NaN – does not represent a number
1	255	≠0	NaN – does not represent a number

---
Comparison
- Comparison of the two IEEE-754 encoded numbers requires to solve signs separately but then it can be processed by unsigned ALU unit on the representations
  A ≥ B ⇐⇒ A − B ≥ 0 ⇐⇒ D(A) − D(B) ≥ 0
- This is advantage of the selected encoding and reason why sign is not placed at start of the mantissa

---
Addition of floating point numbers
- The number with bigger exponent value is selected
- Mantissa of the number with smaller exponent is shifted right – the mantissas are then expressed at same scale
- The signs are analyzed and mantissas are added (same sign) or subtracted (smaller number from bigger)
- The resulting mantissa is shifted right (max by one) if addition overflows or shifted left after subtraction until all leading zeros are eliminated
- The resulting exponent is adjusted according to the shift
- Result is normalized after these steps
- The special cases and processing is required if inputs are not regular normalized numbers or result does not fit into normalized representation

---
Hardware of the floating point adder

---
Multiplication of floating point numbers
- Exponents are added and signs xor-ed
- Mantissas are multiplied
- Result can require normalization
  max 2 bits right for normalized numbers
- The result is rounded
- Hardware for multiplier is of the same or even lower complexity as the adder hardware – only adder part is replaced by unsigned multiplier

---
Floating point arithmetic operations overview
Addition:	A⋅za , B⋅zb , b < a	unify exponents
        B⋅zb = (B⋅zb-a)⋅zb-(b-a)	by shift of mantissa
 A⋅za + B⋅zb = [A+(B⋅zb-a)]⋅za	sum + normalization
Subtraction:	unification of exponents, subtraction and normalization
Multiplication:	A⋅za ⋅ B⋅zb = A⋅B⋅za+b
        A⋅B	- normalize if required
 A⋅B⋅za+b = A⋅B⋅z⋅za+b-1	- by left shift
Division:	A⋅za/B⋅zb = A/B⋅za-b
        A/B	- normalize if required
        A/B⋅za-b = A/B⋅z⋅za-b+1	- by right shift