## Slide 1: Applications of Evolutionary Algorithms
Evolutionary Algorithms
and Their Applications
Jiří Kubalík
Czech Institute of Informatics, Robotics, and Cybernetics
CTU in Prague
email: jiri.kubalik@cvut.cz

## Slide 2: Evolutionary Algorithms
Evolutionary Algorithms are general-purpose stochastic optimization algorithms.
Problem solution can be represented as binary string, real-valued string, string of symbols, tree or graph.
Optimized objective function can be continuous/discrete, multimodal, nonlinear, multidimensional, noisy.
The problem can involve multiple optimization objectives as well.
A typical evolutionary model:
Population
Parents
Offspring
Selection
Replacement
Crossover + Mutation
Evaluation

## Slide 3: Multiple Traveling Salesman Problem
MTSP – rescue operations planning
  Given N cities and K agents, find an optimal tour for each agent so that every city is visited exactly once.
  The optimization objective is to minimize the overall time spent by the squad (i.e. the slowest team member) during the environment exploration.

## Slide 4: Evolutionaty Algorithms for Dynamic Opt.
Dynamic optimizations - a class of problems whose specifications commonly termed
  optimization objectives, and/or
  problem-specific constraints, and/or
  environmental parameters and problem settings
change over time, resulting in continuously moving optima.
    Ex.: Scheduling, manufacturing, trading with stochastic arrival of new tasks, machine faults, climatic change, market fluctuation, economic and financial factors.
    The goal of optimization in dynamic environment is to
  continuously track the optimum, or
  find robust solutions that perform satisfactorily even when the environmental parameters change.

## Slide 5: Evolutionaty Algorithms for Dynamic Opt.

## Slide 6: Application Areas of EAs
EAs are popular for their
  simplicity,
  effectiveness,
  robustness.
Holland: "It's best used in areas where you don't really have a good idea what the solution might be. And it often surprises you with what you come up with.“
Well suited for black-box optimization
  No information about what the optimal solution looks like, no information about how to go about finding it in a principled way.
  Very little information about what the optimized function looks like.
  Very little heuristic information to go on.
  Brute-force search is out of the question because of the huge search space.
Applications
  control,
  engineering design,
  image processing,
  planning & scheduling,
  VLSI circuit design,
  network optimization & routing problems,
  optimal resource allocation,
  marketing,
  credit scoring & risk assessment,
  and many others.

## Slide 7: Human-Competitive Results
John R. Koza et al.: What's AI Done for Me Lately? Genetic Programming's Human-Competitive Results.

## Slide 8: Six Post-2000 patented analog circuits
John R. Koza et al.: What's AI Done for Me Lately? Genetic Programming's Human-Competitive Results.

## Slide 9: Automated Design of Electrical Circuits
Automated “What You Want Is What You Get” process for circuit synthesis.
Genetic programming used to synthesize both
  the structure/topology, and
  sizing (numerical component values)
for circuits that duplicate the patented inventions’ functionality.
Method
  Starts from a high-level statement of a circuit’s desired behavior and characteristics and only minimal knowledge about analogue electrical circuits.
  Then, a fitness measure is created that reflects the invention’s performance and characteristics – it specifies the desired time- or frequency-domain outputs, given various inputs.
  Employs a circuit simulator for analyzing candidate circuits, but does not rely on domain expertise or knowledge concerning the synthesis of circuits.

## Slide 10: Automated Design of Electrical Circuits
Method
  For each problem, a test fixture consisting of appropriate hard-wired components (such as a source resistor or load resistor) connected to the input ports and desired output ports is used.
Test fixture

## Slide 11: WYWIWYG: Embryonic Electrical Circuit
The Mapping between Program Trees and Electrical Circuits
The growth process used for electrical circuits begins with a very simple embryonic electrical circuit and builds a more complex circuit by progressively executing the functions in a circuit-constructing program tree.
The embryonic circuit used on a particular problem depends on the number of input signals and the number of output signals.
The result of this process is
  the topology of the circuit,
  the choice of the types of components that are situated at each location within the topology,
  and the sizing of the components.
Component-creating function (inductor-, capacitor-, …creating functions)
Connection-modifying function – series/parllel division function, delta-shaped composition

## Slide 12: WYWIWYG: Fitness Assignment
Circuit-constructing program tree evaluation in the population begins with its execution.
  This execution applies the functions in the program tree to the very simple embryonic circuit, thereby developing the embryonic circuit into a fully developed circuit.
  A netlist that identifies each component of the circuit, the nodes to which that component is connected, and the value of that component is then created.
Circuit is then simulated using SPICE (an acronym for Simulation Program with Integrated Circuit Emphasis) to determine its behavior.
Fitness measure may incorporate many characteristic or combination of characteristics of the circuit, including
  the circuit's behavior in the time domain,
  its behavior in the frequency domain,
  its power consumption,
  or the number, cost, or surface area of its components.

## Slide 13: GP Control Parameters Setup
Population size: 640,000
Pcrossover = 89%
Pmutation = 1%
Preproduction = 10%
Maximum 200 nodes for each value-producing branch
Parallel Parsytec computer system
  64 x 80 MHz Power PC 601 processors arranged in a toroidal mesh
Parallel GA
  deme size: 10,000
  64 demes
  Migration rate: 2%
Note, this is far from being a brute force search.

## Slide 14: Low-Voltage Balun Circuit
A balun (balance/unbalance) circuit’s purpose is to produce two outputs from a single input
  each having half of the input’s amplitude;
  one output should be in phase with the input while the other should be 180
degrees out of phase with the input, and both should have the same DC offset.
The fitness measure was based on
  a frequency sweep analysis designed to measure the magnitude and phase of the circuit’s two outputs and
  a Fourier analysis designed to measure harmonic distortion.

## Slide 15: Genetically Evolved Low-Voltage Balun Circuit
Evolved circuit is roughly a fourfold improvement over the patented circuit in terms of the fitness measure.
  It is superior both in terms of its frequency response and harmonic distortion.
  Test fixture Evolved balun circuit
John R. Koza et al.: What's AI Done for Me Lately? Genetic Programming's Human-Competitive Results.

## Slide 16: Voltage-Current Conversion Circuit
Voltage-current conversion circuit’s purpose is to take two voltages as input and to produce as output a stable current whose magnitude is proportional to the difference between the voltages.
Fitness measure is based on four time-domain input signals.
Genetically evolved circuit (entirely different than the patented circuit)
  has roughly 62 percent of the average (weighted) error of the patented circuit and
  outperformed the patented circuit on additional previously unseen test cases.
John R. Koza et al.: What's AI Done for Me Lately? Genetic Programming's Human-Competitive Results.

## Slide 17: Mixed Analog-Digital Register-Controlled Variable Capacitor
Mixed analog-digital variable capacitor circuit has a capacitance controlled by the value stored in a digital register.
Fitness measure was based on the error accumulated by 16 combinations of time-domain test signals ranging over all eight possible values of a 3-bit digital register for two different analog input signals.
The evolved circuit performs as well as the patented circuit.
Evolved circuit Patented circuit
John R. Koza et al.: What's AI Done for Me Lately? Genetic Programming's Human-Competitive Results.

## Slide 18: HUMIES
Annual “HUMIES” awards for human-competitive results produced by genetic and evolutionary computation held at the Genetic and Evolutionary Computation Conference (GECCO)
Entries present human-competitive results that have been produced by any form of genetic and evolutionary computation (including, but not limited to genetic algorithms, genetic programming, evolution strategies, evolutionary programming, learning classifier systems, grammatical evolution, gene expression programming, differential evolution, etc.) and that have been published in the open literature.
Human-competitive results awarded in areas:
- Analog circuit design - Game strategies
- Quantum circuit design - Image processing
- Physics - Antenna design
- Digital circuits/programs - Classical optimization
- Chemistry - …
http://www.genetic-programming.org/combined.html

## Slide 19: 2004 Human-Competitive Awards in Genetic and Evolutionary Computation
http://www.genetic-programming.org/gecco2004hc.html
$1500 – Gold
  Jason D. Lohn, Gregory S. Hornby, Derek S. Linden: An Evolved Antenna for Deployment on NASA's Space Technology 5 Mission
  Lee Spector: Automatic Quantum Computer Programming: A Genetic Programming Approach
$500 – Silver
  Alex Fukunaga: Evolving Local Search Heuristics for SAT Using GP
  Hod Lipson: How to Draw a Straight Line Using a GP: Benchmarking Evolutionary Design Against 19th Century Kinematic Synthesis
  Bijan Khosraviani, Raymond E. Levitt, John R. Koza: Organization Design Optimization Using Genetic Programming
$500 – Bronze
  Adrian Stoica, Ricardo Zebulum, Didier Keymeulen, Michael Ian Ferguson, Vu Duong, Xin Guo: Taking evolutionary circuit design from experimentation to implementation: some useful techniques and a silicon demonstration

## Slide 20: The winner of Humies 2004
Three nanosats (20in diameter).
Measure effect of solar activity on the Earth's magnetosphere.
© Jason D. Lohn, Gregory S. Hornby, Derek S. Linden: Human-Competitive Results: Evolved Antennas for Deployment on NASA’s Space Technology 5 Misson

## Slide 21: Evolved Antennas for Deployment on NASA’s Space Technology 5 Mission
Original ST5 Antenna Requirements
  Transmit: 8470 MHz
  Receive: 7209.125 MHz
  Gain:
    >= 0dBic, 40 to 80 degrees
    >= 2dBic, 80 degrees
    >= 4dBic, 90 degrees
  50 Ohm impedance
  Voltage Standing Wave Ratio (VSWR):
    < 1.2 at Transmit Freq
    < 1.5 at Receive Freq
  Fit inside a 6” cylinder
ST5 Quadrifilar Helical Antenna
  designed by a team of human designers
  won the contract
© Jason D. Lohn, Gregory S. Hornby, Derek S. Linden: Human-Competitive Results: Evolved Antennas for Deployment on NASA’s ST5 Misson

## Slide 22: Evolved Antenna for Space Technology 5 mission
Branching EA: Antenna Genotype
  Genotype is a tree-structured encoding that specifies the construction of a wire form
  Genotype specifies design of 1 arm in 3D-space:
rx
f
f
f
f
rz
rx
f
2.5cm
5.0cm
Feed Wire
Branching in genotype results in branching
in wire form
© Jason D. Lohn, Gregory S. Hornby, Derek S. Linden: Human-Competitive Results: Evolved Antennas for Deployment on NASA’s Space Technology 5 Misson

## Slide 23: Evolved Antenna for Space Technology 5 mission
Branching EA: Antenna Construction Commands
  forward(length radius)
  rotate_x(angle)
  rotate_y(angle)
  rotate_z(angle)
  Forward() command can have 0,1,2, or 3 children.
  Rotate_x/y/z() commands have exactly 1 child (always non-terminal).
Fitness function (to be minimized):
  F = VSWR_Score * Gain_Score * Penalty_Score
rx
f
f
f
f
rz
rx
f

## Slide 24: Evolved Antenna for Space Technology 5 mission
1st Set of Genetically Evolved Antennas
Non-branching:
ST5-4W-03
Branching:
ST5-3-10
© Jason D. Lohn, Gregory S. Hornby, Derek S. Linden: Human-Competitive Results: Evolved Antennas for Deployment on NASA’s Space Technology 5 Misson

## Slide 25: Evolved Antenna for Space Technology 5 mission
2nd Set of genetically evolved antennas for new mission requirements
EA 1 – Vector of Parameters
EA 2 – Constructive Process
© Jason D. Lohn, Gregory S. Hornby, Derek S. Linden: Human-Competitive Results: Evolved Antennas for Deployment on NASA’s Space Technology 5 Misson

## Slide 26: Evolved Antenna for Space Technology 5 mission
Conclusion
  Meets mission requirements
  Better than conventional design
  Successfully passed space qualification
  First Evolved Hardware in Space when mission launched in 2005
Direct competition: The antenna designed by the contracting team of human designers for the Space Technology 5 mission - which won the bid against several competing organizations to supply the antenna - did not meet the mission requirements while the evolved antennas did meet these requirements.
Evolutionary design:
  Fast design cycles save time/money (4 weeks from start-to-first-hardware)
  Fast design cycles allow iterative “what-if”
  Can rapidly respond to changing requirements
  Can produce new types of designs
  May be able to produce designs of previously unachievable performance

## Slide 27: 2007 Human-Competitive Awards in Genetic and Evolutionary Computation
http://www.genetic-programming.org/hc2007/cfe2007.html
$5000 – Gold
  Steven Manos et al.: Evolutionary Design of Single-Mode Microstructured Polymer Optical Fibres using an Artificial Embryogeny Representation
$3000 – Silver
  Ami Hauptman, Moshe Sipper: Evolution of an Efficient Search Algorithm for the Mate-In-N Problem in Chess
$1000 – Bronze
  Jaume Bacardit et al.: Automated Alphabet Reduction Method with Evolutionary Algorithms for Protein Structure Prediction
  Xavier Llorà et al.: Towards Better than Human Capability in Diagnosing Prostate Cancer Using Infrared Spectroscopic Imaging

## Slide 28: Evolutionary Design of Single-Mode Microstructured Polymer Optical Fibres
Steven Manos, Leon Poladian, Maryanne Large: Evolutionary Design of Microstructured Polymer Optical Fibres using an Artificial Embryogeny Representation
reference: http://www.genetic-programming.org/hc2007/cfe2007.html
Applications of optical fibres
  Long distance telecommunications
  Computer networks
  Automotive and aeronautical
  Electrical current measurement
  Temperature and strain sensing
  Medical (lasers and endoscopy)
The behaviour of light depends on this
internal structure
New functionality = more complex designs?

## Slide 29: Single-moded fibres
First mode (confined)
Second mode (leaky)
Single-moded fibres support the propagation of only the fundamental mode.
These fibres are important in applications such as high-bandwidth communications, temperature sensing and strain sensing.
By discovering fibres that don’t have a typical hexagonal design, we can start doing more interesting things with them.
Typical hexagonal design
Single-moded operation
Standard design since the early 1990’s

## Slide 30: Evolved single-mode designs
All designs have confined fundamental modes with lc,1  10-1 dB/m, with losses more typically being lc,1  10-3 dB/m.
The loss of the second mode lc,2>104 dB/m in all cases.
All single-moded, yet phenotypically different.

## Slide 31: Manufactured single-mode MPOF
Evolved designs are simpler than previous designs, and easier to manufacture.
Provided us with a rich set of never before seen single-moded microstructured fibre designs to investigate further.

## Slide 32: A different fitness function
Highly multi-moded fibres designed for use in LANs and other short-distance high-bandwidth applications.
‘GIMP 1’
‘GIMP 3’
Hand-designed fibre
Patented GA-designed
fewer holes, easier to manufacture.

## Slide 33: How to Draw a Straight Line Using a GP
Hod Lipson: How to Draw a Straight Line Using a GP: Benchmarking Evolutionary
Design Against 19th Century Kinematic Synthesis
  This entry presents the application of genetic programming to the synthesis of compound 2D kinematic mechanisms, and benchmarks the results against one of the classical kinematic challenges of 19th century mechanical design.
Test Case: The Straight Line Problem
  The straight-line problem seeks a kinematic mechanism that traces a straight line without reference to an existing straight line.
  For example, a circle is easy, a line is a challenge!
line
circle

## Slide 34: How to Draw a Straight Line Using a GP
Some key straight-line mechanisms
See
http://kmoddl.library.cornell.edu
Silverster-Kempe’s
(1877)
Chebyshev
(1867)
Chebyshev
(1867)
Chebyshev-Evans
(1907)
Peaucelier
(1873)
Robert
(1841)

## Slide 35: How to Draw a Straight Line Using a GP
Start with Embryo with desired # of DoF, e.g. a four-bar mechanism (1 DoF)
Two variation operators maintain DoF
E.g. Transform dyad into tryad
Example: A tree that constructs this 1-DoF compound mechanism
Top down encoding of a mechanism
Notes: Here is a top-down encoding of a mechanism:
Top-down construction of a mechanism starts with an embryonic machine with the desired number of DoF, such as the four-bar (which has one DoF).
A tree of operators then recursively modifies that mechanism by replacing single links with assemblies of links with an equivalent DoF, so that the total number of DoF remains unchanged. Two such transformations are shown The D and T operators.
The D operator creates a new node and connects it to both the endpoints of a given link, essentially creating a rigid triangular component. The T operator replaces a given link with two links that pass through a newly created node. The new node is also connected to some other existing node. In both operators, the position of the new nodes is specified in coordinates local to link being modified. Operators provably DoF invariant
On the right, we see how application of a tree of operators to the embryonic mechanism, will transform it into an arbitrary compound mechanism with exactly one DoF. Terminals of the tree are the actual links of the mechanism.

## Slide 36: How to Draw a Straight Line Using a GP
Comparison of mechanisms can be difficult
  Equivalent mechanisms may appear very different
  Masked by excess and redundant topology
Two transformations allow moving in “neutral pathways” of mechanisms
  Rigid diagonal swap
  Redundant dyad removal/addition
Notes: [optional]
Comparison of mechanism can be difficult, as apparently different machines may be functionally equivalent. Complex mechanisms can be reduced to simpler mechanisms with equivalent curve traces by through iterative transformations.
These are essentially neutral operators that can be used in the search as well.

## Slide 37: How to Draw a Straight Line Using a GP
Used GP with Top-down tree encoding and 2-bar or 4-bar embryo
  Population size: 100
  Crossover 90%
  Mutation 10% (Node positions, Operator types)
Selection: Stochastic Universal Sampling
Evaluation of an evolved straight-line mechanism
  The mechanism is actuated at an arbitrary handle and the aspect ratios of bounding boxes of node trajectories are measured.
  One node of the evolved machine on the left traces a curve that is linear to 1:5300 accuracy.
  The evolved mechanism on the right traces a curve that is linear to 1:28340 accuracy
Notes: We used a GP with a population of 100 individuals and fitness proportional selection using stochastic-universal-sampling.
The fitness was the linearity of the most linear curve traced by any of the mechanisms’ vertices, when the crank node was turned 45 degrees.
Linearity is the aspect ratio of the tightest bounding box around node traces.

## Slide 38: How to Draw a Straight Line Using a GP
A typical run – each dot represents an evaluated individual
Notes: The search progressed in steps of discovery, as shown in this typical run.
A variety of mechanisms were produced, most with linearity exceeding 1000 (i.e., deviation of one millimeter over a meter) and some as high as 28000 (35m over a meter).

## Slide 39: Some results
Linearity 1:4979
Notes: This machine has a linearity of 4979

## Slide 40: Some results
Infringes on Robert’s Linkage (1841)
Published: Kempe A. B., (1877), How To Draw A Straight Line, London
Linearity 1:5300
Notes: This machine has a linearity of 5300
It clearly infringes on earlier principles of Robert’s Linkage (1841)

## Slide 41: Some results
Linearity 1:12819
Notes: This machine has a linearity of 12000

## Slide 42: Some results
Linearity 1:28340
Notes: This machine has a linearity of 28000
Many more solutions were evolved

## Slide 43: 2005 Human-Competitive Awards in Genetic and Evolutionary Computation cont.
$1000 – Silver
  Richard J. Terrile et al.:
    Evolutionary Computation Technologies for the Automatic Design of Space Systems,
    Evolutionary Computation applied to the Tuning of MEMS gyroscopes,
    Multi-Objective Evolutionary Algorithms for Low-Thrust Orbit Transfer Optimization
$500 – Bronze
  Moshe Sipper et al.: Attaining Human-Competitive Game Playing with Genetic Programming (Backgammon Players, Robocode Players, Chess Endgame) Moshe Sipper: Evolved to win (http://www.moshesipper.com/evolved-to-win.html)
  Uli Grasemann, Risto Miikkulainen: Effective Image Compression using Evolved Wavelets

## Slide 44: Moshe Sipper: Evolved to Win
Board games
  Checkers
  Chess endgames
  Backgammon
  Simulation games
  Robocode
  Robot Auto Racing Simulator
  Puzzles
  Rush hour
  FreeCell

## Slide 45
GP used to evolve heuristics to guide staged deepening search for the hard game of FreeCell.
Trained and tested on 32,000 problems—known as Microsoft 32K—all solvable but one.
FreeCell requires an enormous amount of search, due both to long solutions and to large branching factors.
Source: Elyasaf, A. at all.: Evolutionary Design of FreeCell Solvers. 2013
Learning Game Strategies: FreeCell
It remains out of reach for optimal heuristic search algorithms, such as variants of A*.
FreeCell remains intractable even when powerful enhancement techniques are employed, such as transposition tables and macro moves.
The previous top gun is the Heineman’s FreeCell solver
  Heineman’s staged deepening algorithm, based on a hybrid A* / hillclimbing search
  Heineman’s heuristic
solved 96% of Microsoft 32K.

## Slide 46: Automatically Finding Patches Using GP

## Slide 47: Automatically Finding Patches Using GP
Fully automated GP-based method for locating and repairing bugs in software
  Set of testcases consists of both
    a set of negative testcases – that characterize a fault
    A set of positive testcases that encode functionality requirements.
  Special GP representation of evolved repaired programs.
    An abstract syntax tree (AST) including all of the statements in the program (CIL toolkit for manipulating C programs)
    A weighted path through the program – a list of pairs [statement, weight] where the weight is based on that statement’s occurences in the tescases.
  Genetic operators are restricted to AST nodes visited when executing the negative testcases.
  Genetic operators realize insertion, deletion, and swapping program statements and control flow. Insertions based on the existing program structures are favored.
  After a primary repair that passes all negative and positive testcases has been found, it is further minimized w.r.t. the number of differences between the original and repair program.

## Slide 48: Automatically Finding Patches Using GP
Example: Euclid’s greatest common divisor
Weimer, W. et al.: Automatically Finding Patches Using Genetic Programming
Original program

## Slide 49: Automatically Finding Patches Using GP
Example: Euclid’s greatest common divisor
Weimer, W. et al.: Automatically Finding Patches Using Genetic Programming
Original program Primary repair
generated given the bias towards modifying lines that are involved in producing the faults and the preference for insertions similar to existing code.

## Slide 50: Automatically Finding Patches Using GP
Example: Euclid’s greatest common divisor
Weimer, W. et al.: Automatically Finding Patches Using Genetic Programming
Original program Primary repair
generated given the bias towards modifying lines that are involved in producing the faults and the preference for insertions similar to existing code.
After repair minimization

## Slide 51: Automatically Finding Patches Using GP
10 different C programs of different size totaling 63,000 lines of code (LOC)
Weimer W. et al.: Automatically Finding Patches Using Genetic Programming
Forrest S. et al.: A Genetic Programming Approach to Automated Software Repair, GECCO 2009

## Slide 52: Evolutionary Design of Image Filters

## Slide 53: Evolutionary design of image filters
Can EA design an image filter which exhibits better filtering properties and lower implementation cost w.r.t. conventional solutions?
Target domain: filters suppressing shot noise, Gaussian noise, burst noise, edge detectors, …

## Slide 54: Image filter in CGP
9 x 8bits
1 x 8bits
Array of programmable. elements (PE).
No feedbacks.
All I/O and connections on 8 bits.
PE over 8 bits:
  Minimum
  Maximum
  Average
  Constants
  logic operators
  shift
Sekanina L.: EvoAISP 2002

## Slide 55
Golden Image
Filtered Image
-
|ABS|
+
Reg
I: golden image
K: filtered image
R: rows
C: columns
Fitness function

## Slide 56: Burst Noise Filtering
switching image filters
5 x 5 filtering window

## Slide 57: Burst Noise Filtering
AMF
CWMF
PWMAD
Image corrupted by 5% impulse bursts noise.
evolved
VAŠÍČEK, BIDLO, SEKANINA: Evolution of efficient real-time non-linear image filters for FPGAs. Soft Computing. 17(11), 2013

## Slide 58: Applications of Evolutionary Algorithms
Symbolic Regression for RL

## Slide 59: Symbolic Regression
Fitting models in the form of mathematical expressions to a set of discrete data points
f = -15.42978401 + 2.42980826 * ((x1 – (x1 * -1.49416733 + x2 * 0.51196778 + 0.00000756)) + (sqrt(power((x1 – (x1 * -1.49416733 + x2 * 0.51196778 + 0.00000756)), 2) + 1) – 1) / 2) ...
-3.141592654 -30 -23.34719731 -2.932153143 -30 -22.67195916 -2.722713633 -30 -22.07798667 -2.513274123 -30 -21.63117778 -2.303834613 -30 -21.2992009 ... ... ...

## Slide 60
  Dynamic system of interest is described by the state transition function
  )
  with
  state:
  action:
  as a generative model given by a numerical simulation of complex differential equations.
  Control goal is specified through a reward function which assigns a scalar reward to each state transition from to :
  This function typically calculates the reward based on the distance of the current state from a given reference state that should be attained.
  Goal of RL is to find an optimal control policy π which maximizes
    , for all .
  Optimal V-function computed by solving the Bellman optimality equation
Reinforcement Learning Framework

## Slide 61: Single Node Genetic Programming (SNGP)
Graph-based GP technique
Evolves a linear population of individuals, each representing a single program node
Program node types
  Terminals – variables, constants
  Functions

## Slide 62
Learning Transition Function

## Slide 63: Inverted Pendulum
The pendulum system consists of a weight of mass m attached to an actuated link that rotates in a vertical plane.
The state vector is , where is the angle and is the angular velocity.
The control input is the voltage .
The control goal is to stabilize the pendulum in the unstable equilibrium .

## Slide 64: Experiments with Real Inverted Pendulum
Data were collected while applying random input to the system.

## Slide 65: Experiments with Real Inverted Pendulum

## Slide 66: Experiments with Real Inverted Pendulum
Example of the refined model

## Slide 67
  Task: Finding a symbolic model from a set of discrete samples of known numerical approximation of the V and policy functions.
Symbolic V function
vs.
Numerical approximation
Symbolic policy
vs.
Fitting V and Policy function

## Slide 68: Learning V function

## Slide 69: EAs for Agents Clustering
Problem: Static agents clustering within multi-agent system from messages sent and received between every pair of agents.
Goal: To find a partitioning of agents into N clusters such that
  communication within clusters is maximized and inter-cluster communication is minimized and
  the clusters are of similar size in order to efficiently distribute agents across multiple execution units.
Copyright © 2007 Rockwell Automation, Inc. All rights reserved
Example: MAS, where agents are used for control of the transportation of products or discrete materials on the factory’s shop floor using a network of conveyor belts.
  partitioning of 67 agents into 4 clusters

## Slide 70: EAs for Agents Clustering
Example: MAS, where agents are used for control of the transportation of products or discrete materials on the factory’s shop floor using a network of conveyor belts.
Goal is to find an optimal partitioning of 67 agents into 4 clusters.
Copyright © 2007 Rockwell Automation, Inc. All rights reserved
MAS: The material-handling application

## Slide 71: mPOEMS: Initialization of SB

## Slide 72: mPOEMS: After 1st iteration

## Slide 73: mPOEMS: After 2nd iteration

## Slide 74: mPOEMS: After 5th iteration

## Slide 75: mPOEMS: After 10th iteration

## Slide 76: mPOEMS: After 20th iteration

## Slide 77: mPOEMS: Final SB after 100 iterations

## Slide 78: mPOEMS: Final SB
Solutions spread along the lower-right
boundary of the solution space.

## Slide 79
Facility Layout
Design Support Tool

## Slide 80: PROBLEM
Notes: How to place workstations into a production hall

## Slide 81: Facility Layout Optimization
Goal – find a layout optimal w.r.t. the given objective function
  minimize a size of the hall partition occupied by production lines
  minimize overall length of communications among connected production lines
Floorplanning – generally an NP-complete problem
  very hard solve to optimality
  computational complexity grows exponentially with the size of the problem
(meta)heurististics needed
  Local search
  Evolutionary algorithms
  Hybrid approaches = EA + LS
  NSGA-II

## Slide 82
Problem: Floorplanning also known as 2D rectangle packing problem.
  Given: A set of N unoriented blocks (rectangles) with fixed dimensions.
  Goal: To place all blocks on a plane so that there is no overlap between any pair of rectangles and the bounding rectangular area is minimal (or the dead space is minimal).
Prototype solution (floorplan)
is encoded by B*-Tree non-slicing
representation.
Each tree is expressed by a linear string of symbols in a prefix not.
Optimization works on linear structs.
Ex.: Blocks {a, b, c, d, e, f} should be placed in a rectangular area so that the bounding rectangular area is minimal (or the dead space, shown in gray, is minimal).
floorplan
B*-tree representation
Floorplanning

## Slide 83
Floorplanning
  Visualization of a POEMS run on data with 300 blocks.
By V. Hordějčuk.
VIDEO

## Slide 84: Input: Hall

## Slide 85: Input: Workstations
  Mobility
    Free – position and rotation randomly initialized, both the position and rotation can change during the optimization process
    Limited – optimization starts from recommended position, rotation allowed
    Pinned – fixed position, rotation allowed
    Fixed – both the position and rotation are fixed for the whole optimization process

## Slide 86: Indirect Representation
Indirect representation – a priority list as a sequence of triples <id, r, h>
  id – workstation identifier
  r – workstation rotation
  h – constructive heuristic
expresses the order in which workstations will be inserted into the developed layout and the heuristic used to process each workstation.
  Rotation
  0, 90, 180, horizontal/vertical mirroring
  Constructive heuristics
  h1, h2
  Example: [<ws6, 90, h1>, <ws6, 0, h2>, <ws6, -90, h1>, … , <ws3, 180, h2>]

## Slide 87: Placement Heuristics
heuristic 1
  Inside the bounding box.
  To the right of the bounding box while minimizing the width of the bounding box.
heuristic 2
  Inside the bounding box.
  Below the bounding box while minimizing the height of the bounding box.

## Slide 88: Objective: Minimize Space Used
Minimize a portion of the hall occupied by production lines (maximize available space).

## Slide 89: Objective: Minimize Connections
Minimize sum of the communication links among connected production lines (Euclidean distance, Hamming distance, …).

## Slide 90: Multi-Objective Optimization
Optimize both criteria simultaneously.

## Slide 91: Evolution of Modular Robot Gaits

## Slide 92: Evolution of Modular Robot Gaits
  Design of an effective and efficient evolutionary-based system for automated generating of modular robot gaits:
  robots composed of a number of simple cubic-shaped robotic blocks,
  each block is endowed with slots (three of them on the main body and one is on the movable arm) that enable them to connect to each other and form more complex robots
  Approaches:
  Co-evolution of a single leg motion pattern and a coordination strategy
  HyperGP – HyperNEAT with CPPN replaced with GP
  GP with automatically defined functions
module
modular robot
simulation

## Slide 93: Evolution of Modular Robot Gaits

## Slide 94
Surprising Creativity of Digital Evolution

## Slide 95
Elbow Walking, Cully et al. (2015)
  an algorithm that enables damaged robots to successfully adapt to the damage
  the evolution solves the case where all six feet touch the ground 0% of the time
Source: Lehman, J. at all.: The Surprising Creativity of Digital Evolution: A Collection of Anecdotes from the Evolutionary
Computation and Artificial Life Research Communities. 2018
Surprising Creativity of Digital Evolution

## Slide 96
Evolution of Muscles and Bones, Cheney et al. [68]
  evolution to discover from scratch the benefit of complementary (opposing) muscle groups, similar to such muscle pairs in humans, e.g. biceps and triceps – and also to place them in a functional way
Source: Lehman, J. at all.: The Surprising Creativity of Digital Evolution: A Collection of Anecdotes from the Evolutionary
Computation and Artificial Life Research Communities. 2018
Surprising Creativity of Digital Evolution

## Slide 97
Re-enabling Disabled Appendenges, Ecarlat and colleagues [85]
  The goal was to accumulate a wide variety of controllers, to move the cube onto the table, to grasp the cube, to launch it into a basket in front of the robot, …
  Then the robot’s gripper was crippled, preventing it from opening and closing, …
Source: Lehman, J. at all.: The Surprising Creativity of Digital Evolution: A Collection of Anecdotes from the Evolutionary
Computation and Artificial Life Research Communities. 2018
Surprising Creativity of Digital Evolution