Microprocessor Evolution - from 4-bit Ones to Superscalar RISC
Computer Architectures
Microprocessor Evolution - from 4-bit Ones to Superscalar RISC
Pavel Píša, Michal Štepanovský
Czech Technical University in Prague, Faculty of Electrical Engineering
Ver.1.00

---
Cypripedium Calceolus for My Mother

---
Early Technology and Complexity Comparison
Early Technology and Complexity Comparison

---
Accumulator Based Architectures
Accumulator Based Architectures
- register+accumulator → accumulator
  - 4bit Intel 4004 (1971)
  - 8bit Intel8080 (1974) – registers pairs used to address data in 64kB address space
  - basic arithmetic-logic operations only – addition, subtraction, rotation for 8-bit accumulator
  - subroutines by CALL and RET instructions with 16-bit PC save on stack
  - a few 16-bit operations – increment/decrement of registers pairs, addition to HL and save to stack
  - microcode controlled/microprogrammed instructions execution – 2 to 11 clock cycles per instruction at 2 MHz clock signal

---
Intel 8080
Intel 8080
http://en.wikipedia.org/wiki/Intel_8080

---
Fast memory ⇒ reduce register count and add address modes
Fast memory ⇒ reduce register count and add address modes
- Motorola 6800, NMOS T. 6502 (1975) - accumulator, index, SP a PC only – use zero page as fast data, CU hardwired
- Texas TMS990 – workspace pointer only, even PC, SP, other registers in main memory, similar to transputers

---
Memory is bottleneck now ⇒ complex instruction set modeled according to C language constructs, CISC
Memory is bottleneck now ⇒ complex instruction set modeled according to C language constructs, CISC
- Intel 8086 (16-bit upgrade to 8080)
  - 8× 8-bit register form 4 pairs (16-bit registers), additional 4 16-bit registers – SP, BP (C functions frame), SI (source-index), DI (destination index), 1 MB address space by segments, register+=register, memory+=register, register+=memory
- Motorola 68000 (1979) – 16/32bit
  - two operand instructions
  - register+=register, memory+=register, register+=memory, even one instruction memory=memory
  - based on microcode to process so rich instruction set
- Z-8000 16bit, Z-80000 32bit (1986) CISC
  - 6 phases pipelined execution, without microcode, 18000 transistors only

---
Intel 8086 and 32-bit i386
Intel 8086 and 32-bit i386
Data Segment
Code Segment
Extra Segment
Stack Segment
Instruction Pointer
Program Status and Control Register
EAX
EFLAGS
GS
FS
ES
SS
DS
CS
ESP
EBP
EDI
ESI
EDX
ECX
EBX
EIP
0
31
31
0
0
31
15
0
General-Purpose Registers
Segment Registers
AX
DX
CX
BX
16-bit
32-bit
SI
DI
BP
SP
AL
BL
CL
DL
AH
BH
CH
DH
Accumulator
Base
Count
Data
Source Index
Destination Index
Base Pointer
Stack Pointer
7
8
15
16

---
Basic Integer Registers of M68xxx/CPU32/ColdFire
Basic Integer Registers of M68xxx/CPU32/ColdFire
User mode
System mode
31
16
15
0
A7# (SSP)
SUPERVISOR STACK
POINTER
15
8
7
0
(CCR)
SR
STATUS REGISTER
31
0
VBR
VECTOR BASE REGISTER
31
3
2
0
SFC
ALTERNATE FUNCTION
DFC
CODE REGISTERS
16
15
8
7
0
D0
D1
D2
D3
DATA REGISTERS
D4
D5
D6
D7
16
15
0
A0
A1
A2
A3
ADDRESS REGISTERS
A4
A5
A6
16
15
0
A7 (USP)
USER STACK POINTER
0
PC
PROGRAM COUNTER
15
8
7
0
0
CCR
CONDITION CODE REGISTER
31

---
Status Register – Conditional Code Part
Status Register – Conditional Code Part
- N – negative ... = 1 when the most significant bit of the result is set; otherwise cleared. (the result is negative for two's complement representation)
- Z – zero ... = 1 when result is zero – all bits are zero
- V – overflow .. = 1 when an arithmetic overflow occurs implying that the result cannot be represented in the operand size (signed case for add, sub, …)
- C – carry ... = 1 when when a carry out of the most significant bit occurs (add) or a borrow occurs (sub)
- X - extend (extended carry) .. Set to the value of the C-bit for arithmetic operations; otherwise not affected or set to a specified result
15
14
13
12
11
10
9
8
7
6
5
4
3
2
1
0
T1
T0
S
0
0
I2
I1
I0
0
0
0
X
N
Z
V
C
EXTEND
NEGATIVE
ZERO
OVERFLOW
CARRY
INTERRUPT
PRIORITY MASK
SUPERVISOR/USER
STATE
TRACE
ENABLE
SYSTEM BYTE
USER BYTE
(CONDITION CODE REGISTER)

---
Status Register – System Byte
Status Register – System Byte
- T1, T0 – trace … if some of these bits is set then exception is generated after every instruction execution or when program flow changes (jump, call, return)
- S – supervisor … if set to 1 then CPU runs in the supervisor state/mode and SP maps to SSP. Else CPU runs in user mode, SP maps to USP and changes to the system byte are not possible and user mode privileges rules/restrictions are applied to memory access (controlled by MMU).
- I2, I1, I0 - interrupt mask … up to this interrupt priority level are requests blocked/masked – i.e. they need to wait. The level 7 is exception because it is non-maskable, i.e. exception acceptance cannot be delayed.
15
14
13
12
11
10
9
8
7
6
5
4
3
2
1
0
T1
T0
S
0
0
I2
I1
I0
0
0
0
X
N
Z
V
C
EXTEND
NEGATIVE
ZERO
OVERFLOW
CARRY
INTERRUPT
PRIORITY MASK
SUPERVISOR/USER
STATE
TRACE
ENABLE
SYSTEM BYTE
USER BYTE
(CONDITION CODE REGISTER)

---
Addressing Modes – Basic 68000 Modes
Addressing Modes – Basic 68000 Modes
- Up to 14 addressing modes for operand selection
- Rn operand represents value of data Dn or address An register
- (An) memory content at the address specified by An
- (An)+ memory content at An with following An increment by value equivalent to the operand length (post-increment)
- -(An) the An register is decremented by operand size first and then specifies memory located operand (pre-decrement)
- (d16,An) memory at An + 16-bit sign extended offset
- (d8,An,Xn) memory at An + 8-bit sign extended offset + index register (another Am or Dm) which can be eventually limited to lower 16 bits, index can be multiplied by 1, 2, 4 or 8 for CPU32 and 68020+ processors
- (xxx).W 16-bit absolute address – upper and lower 32kB
- (xxx).L 32-bit absolute address

---
Data throughput and instruction fetching slow still ⇒ cache memory
Data throughput and instruction fetching slow still ⇒ cache memory
- The problem has been solved quite well
- Common cache or Harvard arrangement I & D
- More levels (speed limited for bigger size – decoder, capacitance of common signals)
- But requires to solve data coherence when DMA access or SMP is used
  - synchronization instructions for peripherals access and synchronization eieio (PowerPC), mcr p15 (ARM), …
  - hardware support required for caches and SMP
    - protocol MSI , MESI (Pentium), MOSI
    - MOESI AMD64 (Modified, Owned, Exclusive, Shared, and Invalid)

---
Data Coherence and Multiple Cached Access
Data Coherence and Multiple Cached Access
MOESI protocol
- Modified – cache line contains actual and modified data, none of other CPUs works with data, old/previous data are hold in main memory
- Owned – line holds actual data, line can be shared with other CPUs CPU but only in S state, main memory is not required to be up to date
- Exclusive – only this CPU and main memory contains cahe line data
- Shared – cache line is shared with other CPUs, one of them can be in O state, then data can differ to content in main memory
- Invalid – cache line does not hold any valid data
	M	O	E	S	I
M	N	N	N	N	Y
O	N	N	N	Y	Y
E	N	N	N	N	Y
S	N	Y	N	Y	Y
I	Y	Y	Y	Y	Y
http://en.wikipedia.org/wiki/MOESI_protocol

---
Yet faster instructions execution ⇒ RISC architectures
Yet faster instructions execution ⇒ RISC architectures
- Reduce data flow dependency between instructions, three operand instructions, speculative instructions execution, more registers to reduce memory accesses, register renaming, eliminate interdependencies on conditional code/flag register (MIPS RISC-V eliminate CC altogether, DEC Alpha, multiple flag registers PowerPC, flags update suppress ARM)
- load-store architecture, computation only register+=register and or register=register+register and separate load-store instructions.
- Fixed instruction encoding ⇒ programs are usually longer but much faster instructions decoding, optimized for pipelined execution

---
Pipelined execution, branches cause even more problems
Pipelined execution, branches cause even more problems
- Early branch and jump instructions decode
- Processes instructions in delay slots MIPS, DSP
- Static and dynamic branch prediction, branch target address buffer (cache), speculative instructions execution
Source: wikipedia

---
Parallel Instructions Execution – Superscalar CPU
Parallel Instructions Execution – Superscalar CPU
Fetch
Instruction / decode buffer
Decode
Dispatch buffer
Dispatch
Reservation stations
Issue
Execute
Finish
Reorder / Completion buffer
Complete
Store buffer
Retire

---
Other techniques to reduce memory access frequency ⇒ register windows, link/return address register
Other techniques to reduce memory access frequency ⇒ register windows, link/return address register
- Generally more registers (RISCs usually 31+1, ARM 32-bit 16, compare with 32-bit 386 still only 8 registers)
- SPARC - 8 global registers, 8 from previous window (parameters), 16 in actual window, up to 100 and more registers to stack windows. 8 registers in actual window is used to pass parameters into subroutine
- PowerPC, MIPS, ARM – speedup to call leaf-node functions with use of return address (link register) to store address of the instruction to be executed after return from subroutine

---
PowerPC Architecture
PowerPC Architecture

---
Summit Supercomputer – IBM AC922 – 2018 TOP500 #1
Summit Supercomputer – IBM AC922 – 2018 TOP500 #1
- June 2018, US Oak Ridge National Laboratory (ORNL), 200 PetaFLOPS, 4600 “nodes”, 2× IBM Power9 CPU +
- 6× Nvidia Volta GV100
- 96 lanes of PCIe 4.0, 400Gb/s
- NVLink 2.0, 100GB/s CPU2GPU
- GPU-to-GPU
- 2TB DDR4-2666 per node
- 1.6 TB NV RAM per node
- 250 PB storage
- POWER9-SO, Global Foundries 14nm FinFET, 8×109 tran., 17-layer, 24 cores, 96 threads (SMT4)
- 120MB L3 eDRAM (2 CPU 10MB), 256GB/sv
Source: http://www.tomshardware.com/

---
SPARC – Register Windows
SPARC – Register Windows
- CPU includes from 40 to 520 general purpose 32-bit registers
- 8 of them are global registers, remaining registers are divided in groups of 16 into at least 2 (max 32) register windows
- Each instruction has access to 8 global registers and 24 registers accessible through actually selected register windows position
- 24 windowed registers are divided into 8 input (in), 8 local (local) and 8 registers from the following window which are visible through current window as an output (out) registers (registers to prepare call arguments)
- Active window is given by value of 5-bit pointer – Current Window Pointer (CWP).
- CWP is decremented when subroutine is entered which selects following window as an active/current one
- Increment of CWP return to the previous register window
- Window Invalid Mask (WIM) is a bit-map which allows to mark any of windows as invalid and request exception (overflow or underflow) when window is activated/selected by CWP

---
SPARC - Registers
SPARC - Registers
R31
R30
R29
R28
R27
R26
R25
R24
R23
R22
R21
R20
R19
R18
R17
R16
R15
R14
R13
R12
R11
R10
R9
R8
Return from actual window ... %i7
The frame pointer %fp ... %i6
%i5
%i4
%i3
%i2
%i1
%i0
%l7
%l6
%l5
%l4
%l3
%l2
%l1
%l0
CALL out return address … %o7
The stack pointer %sp ... %o6
%o5
%o4
%o3
%o2
%o1
%o0
I / (in)
L (local)
O / (out)
G (global)
%g7
%g6
%g5
%g4
%g3
%g2
used by system %g1
zero %g0
R7
R6
R5
R4
R3
R2
R1
R0

---
SPARC – Register Windows Operation
SPARC – Register Windows Operation

---
SPARC in Space – Cobham Gaisler GR740
SPARC in Space – Cobham Gaisler GR740
Fault-tolerant, quad-core, SPARC V8, 7-stage pipeline, 8 register windows, 4x4 KiB I + 4x4 KiB D cache, IEEE-754, 2 MiB L2 cache
Source: https://www.gaisler.com/index.php/products/components/gr740

---
Quad-Core LEON4FT (GR740) Development Board
Quad-Core LEON4FT (GR740) Development Board
Source: https://www.gaisler.com/index.php/products/boards/gr-cpci-gr740

---
MIPS Architecture Variants
MIPS Architecture Variants
- Probably architecture with the highest use count on Earth at one time (all kinds of AP, embedded systems, etc.)
- Development still continues even for high performance desktops and supercomputers use – Loongson3A
- MIPS Aptiv – MIPS32 MCU for embedded applications
- MIPS Warrior – MIPS P6600 MIPS64 Release 6 – hardware virtualization with hardware table walk, 128-bit SIMD
- MIPS architecture inspired many SoftCore designs for FPGA, examples
  - Xilinx Microblaze
  - Altera Nios

---
Pipelined execution, no microcode, but still problems with jump instructions
Pipelined execution, no microcode, but still problems with jump instructions
- Early jump instruction decode
- Use delay slots to keep pipeline busy, MIPS, DSP
- Static and dynamic conditional branch prediction, branch target address cache, speculative instruction execution

---
Loongson3A
Loongson3A

---
MIPS 64-bit Base of China Computing
MIPS 64-bit Base of China Computing
- Loongson 3A5000 – desktop processor, 12nm, 4 cores @ at 2.5GHz
- Loongson 3C5000 – server processor, 12nm, 16 cores, supports 4 to 16-way servers

---
Attempts to enhance code density ⇒ shorter aliases, variable instruction length even for RISC, VLIW
Attempts to enhance code density ⇒ shorter aliases, variable instruction length even for RISC, VLIW
- ARM, 16bit aliases for most common 32bit instructions (Thumb mode, requires mode switching, later on function by function call basis)
- MIPS Aptiv, same on function basis
- M-Core, 32-bit CPU but only 16-bit instruction encoding
- SuperH, 32/64-bit CPU, 16-bit instructions encoding
- ColdFire - RISC implementation based on 68000 instruction set, but only 16, 32, 48-bit length instructions are accepted
- RISC-V, reserved bits of 32-bit instructions to allow seamless combination of 32 and 16-bit instructions

---
ARM Architecture - Registers
ARM Architecture - Registers

---
ARM Architecture – ALU and Operands Encoding
ARM Architecture – ALU and Operands Encoding
Register, optionally with shift operation
Shift value can be either be:
5 bit unsigned integer
Specified in bottom byte of another register.
Used for multiplication by constant
Immediate value
8 bit number, with a range of 0-255.
Rotated right through even number of positions
Allows increased range of 32-bit constants to be loaded directly into registers
Result
Operand 1
Barrel
Shifter
Operand 2
ALU

---
ARM Architecture – Program Status Word
ARM Architecture – Program Status Word
Interrupt Disable bits.
I = 1: Disables the IRQ.
F = 1: Disables the FIQ.
T Bit
Architecture xT only
T = 0: Processor in ARM state
T = 1: Processor in Thumb state
Mode bits
Specify the processor mode
Condition code flags
N = Negative result from ALU
Z = Zero result from ALU
C = ALU operation Carried out
V = ALU operation oVerflowed
Sticky Overflow flag - Q flag
Architecture 5TE/J only
Indicates if saturation has occurred
J bit
Architecture 5TEJ only
J = 1: Processor in Jazelle state
27
31
N Z C V Q
28
6
7
I F T mode
16
23
8
15
5
4
0
24
f
s
x
c
U n d e f i n e d
J

---
ARM Architecture – CPU Execution Modes
ARM Architecture – CPU Execution Modes
- User : unprivileged mode under which most tasks run
- FIQ : entered when a high priority (fast) interrupt is raised
- IRQ : entered when a low priority (normal) interrupt is raised
- Supervisor : entered on reset and when a Software Interrupt instruction is executed
- Abort : used to handle memory access violations
- Undef : used to handle undefined instructions
- System : privileged mode using the same registers as user mode

---
Conclusion – Almost
Conclusion – Almost
- There is no magic solution for all discussed problems for all use cases
- It is necessary to combine discussed techniques and optimize the mix according to intended CPU area of use (the highest computational power/power efficient)
- use of heterogeneous systems for high performance computation – vector units, GPU, FPGA accelerators

---
Why Instruction Set Architecture Matters
Why Instruction Set Architecture Matters
- Why can’t Intel sell mobile chips?
  99%+ of mobile phones/tablets are based on ARM’s v7/v8 ISA
- Why can’t ARM partners sell servers?
  99%+ of laptops/desktops/servers are based on the AMD64 ISA (over 95%+ built by Intel)
- How can IBM still sell mainframes?
  IBM 360 is the oldest surviving ISA (50+ years)
ISA is the most important interface in a computer system
ISA is where software meets hardware. (SiFive/RISC-V)

---
ARM 64-bit – AArch64
ARM 64-bit – AArch64
- Calling uses LR, no register banking, ELR for exceptions
- PC is separate register (not included in general purpose registers file)
- 31 64-bi registers R0 to R30 (R30 = X30 ≅ LR)
  - Symbol Wn (W0) used for 32-bit access, Xn (X0) for 64-bit
  - Reg. code 31 same zero role as MIPS 0, WZR/XZR in code
  - Reg. code 31 special meaning as WSP, SP for some opcodes
- Immediate operand 12-bit with optional LS 12 for arithmetics operations and repetitive bit masks generator for logic ones
- 32-bit operations ignores bits 32–63 for source and zeros these in the destination register

---
AArch64 – Branches and Conditional Operations
AArch64 – Branches and Conditional Operations
- Omitted conditional execution in all instructions as well as Thumb IT mechanism
- Conditional register retain, CBNZ, CBZ, TBNZ, TBZ added
- Only couple of conditional instructions
  - add and sub with carry, select (move C?A:B)
  - set 0 and 1 (or -1) according to the condition evaluation
  - conditional compare instruction
- 32-bit and 64-bit multiply and divide (3 registers), multiply with addition 64×64+64  64 (four registers), high bits 64 to 127 from 64×64 multiplication

---
AArch64 – Memory Access
AArch64 – Memory Access
- 48+1 bit address, sign extended to 64 bits
- Immediate offset can be multiplied by access size optionally
- If register is used in index role, it can be multiplied by access size and can be limited to 32 bits
- PC relative ±4GB can be encoded in 2 instructions
- Only pair of two independent registers LDP and STP (ommited LDM, STM), added LDNP, STNP
- Unaligned access support
- LDX/STX(RBHP) for 1,2,4,8 and 16 bytes exclusive access

---
AArch64 – Address Modes
AArch64 – Address Modes
- Simple register (exclusive)
  [base{,#0}]
- Offset
  [base{,#imm}]	– Immediate Offset
  [base,Xm{,LSL #imm}]	– Register Offset
  [base,Wm,(S|U)XTW {#imm}]	– Extended Register Offset
- Pre-indexed
  [base,#imm]!
- Post-indexed
  [base],#imm
- PC-relative (literal) load
  label
Bits	Sign	Scaling	WBctr	LD/ST type
0	-	-	-	LDX, STX, acquire, release
9	signed	scaled	option	reg. pair
10	signed	unscaled	option	single reg.
12	unsig.	scaled	no	single reg.

---
Apple A12Z Bionic – 64-bit ARM-based
Apple A12Z Bionic – 64-bit ARM-based
- People who are really serious about software should make their own hardware. Alan Kay
- Apple A12Z, 8 cores (ARM big.LITTLE: 4 "big" Vortex + 4 "little" Tempest), Max. 2.49 GHz, ARMv8.3‑A
- Cache L1 128 KB instruction, 128 KB datam L2 8 MB
- GPU Apple designed 8-Core

---
Fujitsu – Supercomputer Fugaku – A64FX, 2020 TOP500 #1
Fujitsu – Supercomputer Fugaku – A64FX, 2020 TOP500 #1
- Combine Armv8.2-A (AArch64 only) with Fujistu supercomputer technology, SPARC64 V till now
- 48 computing cores + 4 assistant cores, SVE 512-bit wide SIMD
- HBM2 32GiB, 7nm FinFET, 8,786M transistors
- Tofu 6D Mesh/Torus, 28Gbps x 2 lanes x 10 ports, PCIe
Source: Fujitsu High Performance CPU for the Post-K Computer, 2018
Netwrok
on
Chip
HBM2
PCIe
controller
Tofu
controller
HBM2
HBM2
HBM2

---
RISC-V – Optimize and Simplify RISC Again
RISC-V – Optimize and Simplify RISC Again
- Patterson, Berkeley RISC 1984 → initiation of RISC era, evolved into SPARC (Hennessy MIPS, Stanford University)
- Commercialization and extensions results in too complex CPUs again, with license and patents preventing even original inverstors to use real/actual implementations in silicon to be used for education and research
- MIPS is model architecture for prevalent amount of base courses and implementation of similar processor is part of follow up courses (A4M36PAP)
- Krste Asanovic and other Dr. Patterson's students initiated development of new architecture (start of 2010)
- BSD Licence to ensure openness in future
- Supported by GCC, binutils., Linux, QEMU, etc.
- Simpler than SPAC, more like MIPS but optimized on gate level load (fanout) and critical paths lengths in future designs
- Some open implementations already exists Rocket (SiFive, BOOM ), project lowRISC contributes to research in security area, in ČR Codasip
- Already more than 20 implementations in silicon

---
RISC-V – Architecture Specification
RISC-V – Architecture Specification
- ISA specification can be found at http://riscv.org/
  - The RISC-V Instruction Set Manual, Volume I: User-Level ISA, Version 2.0
  - Andrew Waterman, Yunsup Lee, David Patterson, Krste Asanovic
  - Not only architecture description but even choices analysis with pro&cons of each selection and cost source description/analysis of alternatives
- classic design, 32 integer registers, the first tied to zero, regsrc1, regsrc2, regdest operands, uniqueness, rule kept strictly even for SaveWord, leads to non-continuous immediate operands encoding, PC not part of base register file, PC-relative addressing
- variants for 32, 64 a 128-bit registers and address-space defined
- high code density (16-bit instruction encoding variant planned)
- encoding reserves space for floating point (single, double, quad) and multimedia SIMD instructions systematic way, etc.

---
RISC-V – Registers
RISC-V – Registers
Integer registers
Floating point registers
Variant	XLEN
RV32	32
RV64	64
RV128	128
Variant	FLEN
F	32
D	64
Q	128
Floating-point control and status register
Source: https://riscv.org/specifications/

---
RISC-V – Instruction Length Encoding
RISC-V – Instruction Length Encoding
Source: https://riscv.org/specifications/

---
RISC-V – 32-bit Instructions Encoding
RISC-V – 32-bit Instructions Encoding
Source: https://riscv.org/specifications/

---
BOOM Superscalar RISC-V into Rocket Chip
BOOM Superscalar RISC-V into Rocket Chip
Rename Map Tables & Freelist
Issue
ALU
Window
Unified
Physical
Decode &
Fetch
Register
Rename
File
FPU
(PRF)
ROB
Commit
out-of-order
back-half
in-order
front-half
9k source lines + 11k from Rocket
Main developer: Christopher Celio
Source: https://riscv.org/wp-content/uploads/2016/01/Wed1345-RISCV-Workshop-3-BOOM.pdf

---
RISC-V – HiFive Unleashed
RISC-V – HiFive Unleashed
- SiFive FU540-C000 (built in 28nm)
  - 4+1 Multi-Core Coherent Configuration, up to 1.5 GHz
  - 4x U54 RV64GC Application Cores with Sv39 Virtual
  - Memory Support
  - 1x E51 RV64IMAC Management Core
  - Coherent 2MB L2 Cache
  - 64-bit DDR4 with ECC
  - 1x Gigabit Ethernet
- 8 GB 64-bit DDR4 with ECC
- Gigabit Ethernet Port
- 32 MB Quad SPI Flash
- MicroSD card for removable storage
- FMC connector for future expansion with add-in card

---
RISC-V – HiFive Unleashed 1
RISC-V – HiFive Unleashed

---
More RISC-V projects
More RISC-V projects
- Libre RISC-V https://libre-riscv.org/
  - Quad-core 28nm RISC-V 64-bit (RISCV64GC core with Vector SIMD Media / 3D extensions)
  - 300-pin 15x15mm BGA 0.8mm pitch
  - 32-bit DDR3/DDR3L/LPDDR3 memory interface
- More RISC-V resources
  - https://riscv.org/
  - RISC-V YouTube channel https://www.youtube.com/channel/UC5gLmcFuvdGbajs4VL-WU3g