Interconnection networks
Advanced Computer Architectures
Verilog – introduction
Czech Technical University in Prague, Faculty of Electrical Engineering
Slides authors: Michal Štepanovský, update Pavel Píša

---
HDL – Hardware Description Language
HDL – Hardware Description Language
Two widespread HDL languages:
  - VHDL (VHSIC Hardware Description Language; VHSIC = Very High Speed Integrated Circuits)
  - Verilog
  - Both include even constructs/commands not synthetizable into hardware realization
- Design description:
  - Behavioral (function description in abstract way)
  - Structural (interconnection of components)

---
Verilog – behaviorální popis
Verilog – behavioral description
Logic circuit combinational
module label (input list_of_inputs,
        output list_of_outputs);
wire declaration_of_internal_variables;
assign bind_output_to_inputs_and_wires_function;
assign bind_output_to_inputs_and_wires_function;
endmodule
Modul – HW block with inputs and outputs

---
Verilog – příklad
Verilog – example
module inv (input x,
        output y);
assign y = ~x;
module and (input a, b,
        output y);
assign y = a & b;
x y
&
a y
b

---
Verilog – příklad č.2
Verilog – example no. 2

---
Verilog – příklad – behaviorální popis
Verilog – example – behavioral description
module gates (input [3:0] a, b,
        output [3:0] y1, y2,y3, y4, y5);
assign y1 = a & b; // AND
assign y2 = a | b; // OR
assign y3 = a ^ b; // XOR
assign y4 = ~(a & b); // NAND
assign y5 = ~(a | b); // NOR

---
Verilog – simulace – Obecně
Verilog – simulation – in general
1. “encapsulate” simulated circuit into module without inputs and outputs
2. Declare internal variables of the module (reg, wire) for input presets (reg) and observe of the outputs (wire) of the simulated circuit
3. Assign internal variables to the simulated circuit inputs and outputs
4. specification of time sequence of circuit stimuli

---
Verilog – simulace – Obecně
Verilog – simulation – in general
`timescale 1ns / 1ps
module testbench_a();
reg a, b; // inputs
wire c; // outputs
simulated_circui_name instance_name(
.a(a),
.b(b),
.c(c),
);
initial begin
a = 0;
b = 0;
end
always #40 a = ~a;
always #80 b = ~b;
no inputs or outputs
create internal, stimuli/monitor
create simulated circuit instance and assignment of testbench internal variables to inputs and outputs
signal names starting by dot are names of inputs and outputs in module declaration, bracketed are names of stimuli and monitor signals
Inputs initialization
always blocks (multiple statements for single allways are enclosed by begin end pair) are executed concurrently…
Invert each 80 ns

---
Verilog – behaviorální popis – pokračování v úvodu do jazyka
Verilog – behavioral description – continue language syntax

---
Verilog – behaviorální popis
Verilog – behavioral description
Ternar operator „?“
module mux2 (input [3:0] d0, d1,
input s,
  output [3:0] y);
assign y = s ? d1 : d0;
reduce
  module and5(input [4:0] a, output y);
assign y = &a;
místo
assign y = a[4] & a[3] & a[2] & a[1] & a[0];
similar for operators: |, ^, ~&, a ~| (or, xor, nand, a nor)

---
Verilog – behaviorální popis
Verilog – behavioral description
numbers
N'BaseVale // N: bit width; Base: b,o,d,h
b – binry, o – octal, d – decimal, h - hexa
3'b101 // 101
'b11	// when assigned to 6-bit variable 000011
3'd5	// 101
third state value „z“
module tristateBuffer (input [3:0] a,
    input en,
    output [3:0] y);
    assign y = en ? a : 4'bz;

---
Verilog – behaviorální popis
Verilog – behavioral description
invalid value „x“
„x“ is result of simultaneous assignment of 0 and 1, uninitialized output, when gate cannot determine output value („z“ on input; 1 and „z“ = „x“ but 0 and „z“ = 0)
Concatenation { }
y = c2c1d0d0d0c0101 is build by :
    assign y = {c[2:1],{3{d[0]}},c[0],3’b101};
na = ~a; nb = ~b; nc = ~c; can be rewritten as:
    {na, nb, nb} = ~{a, b, c};

---
Verilog – behaviorální popis
Verilog – behavioral description
delay
‘timescale 1ns/1ps // unit/resolution
module example (input a, b,
  output y);
    assign #3 y = a & b; // 3 units = 3 ns
Delays are used only during simulation, they are ignored during synthesis.

---
Verilog – strukturální popis
Verilog – structural description
Logic circuit combinational
module name (input input_list,
        output output_list);
wire internal_variables_declaration;
module_name instance_name(port_mapping);
module_name instance_name(port_mapping);

---
Verilog - příklad
Verilog – structural description – example

---
Verilog – strukturální popis
Verilog – structural description – example
module mux4 (input [3:0] d0, d1, d2, d3,
  input [1:0] s,
        output [3:0] y);
wire [3:0] low, high;
mux2 lowmux (d0, d1, s[0], low);
mux2 highmux (d2, d3, s[0], high);
mux2 finalmux (low, high, s[1], y);

---
Verilog – strukturální popis
Verilog – structural description
module mux2 (input [3:0] d0, d1,
  input s,
  output [3:0] y);
  tristateBuffer t0 (d0, ~s, y); // ~s expression allowed
  tristateBuffer t1 (d1, s, y);
module tristateBuffer (input [3:0] a,
    input en,
    output [3:0] y);
    assign y = en ? a : 4'bz;

---
Verilog
Verilog
- Output value binding by assign statement is evaluated for each change of expression input on the right side
- Otput value controlled by always @() is evaluated only for specified conditions (left side of the statement/expression holds its value even when inputs of the right side change value)
- Blocking assignment are evaluated „=“ sequentionally as they are introduced in the source
- Nonblocking assignments „<=“ are evaluated simultaneously; left sides of all assignments are updated after evaluation of right sides
Logic circuit sequential

---
Verilog – always
Verilog – always
Suggestions:
Use blocking assignemnts for combinational circuits, non-blocking for sequential
Output assignment by always directives:
always @ (sensitivity_list)
   statement;
  - statement is evalueted only occurs event which is enumerated in sensitivity_list
  - If always @(*) is specified then it is trigerred by any change on inputs of all enclosed statements
  - All signals on the left side of assignemnt (=, <=) has to be declared as reg

---
Verilog – blokující vs. neblokující přiřazení
Verilog – blocking vs. non blocking assignments
module circuit (input a, b,
  output reg y);
reg x;
always @(*)
  begin
    x = a ^ b; //blocking
    y = x & a; //blocking
  end
module circuit (input a, b,
  output reg y);
reg x;
always @(*)
  begin
    x <= a ^ b; //non-blocking
    y <= x & a; //non-blocking
  end
Assume that a=b=0. Then y=0. a is assigned to 1 (a=1) at some time instant, which triggers always block evaluation. Blocking statements are executed in order of their appearance, that is x is set to new value before y is evaluated. When non-blocking assignments are used then all right sides are evaluated simultaneously and then right sides are assigned as separated step. The consequence is that y stays equal to 0. But change of x from 0 to 1 results in repeated triggering of always block, and following expected evaluation of y. But if sensitivity list is changed to: always @(a,b) instead of @(*) then the behavior of the two circuits differs

---
Verilog
Verilog
module abc(
    input a,
    input b,
    output reg y
    );
  always @(*)
    y = a;
  always @(*)
    y = b;
module abc(
    input a,
    input b,
    output reg y
    );
  always @(*)
    y <= a;
  always @(*)
    y <= b;
module abc(
    input a,
    input b,
    output reg y
    );
  always @(*)
    assign y = a;
  always @(*)
    y = b;

---
Verilog
Verilog
Variables declarations as:
- reg x; means, that variable is a single bit signal which is used ob the left side in always
- reg [7:0] x; declares 8-bit variable…
- reg x[7:0]; declares x as vector of eight one bit variables which can be accessed by index (x[0], x[1],…)
- reg [7:0] x[15:0]; declares 16 elements vector of 8-bit variables …

---
Verilog – always
Verilog – always
D flip-flop triggered by rising edge of clk (positive edge):
module D_flip_flop (input clk,
 input [3:0] d,
    output reg [3:0] q);
always @ (posedge clk)
q <= d;
D flip-flop with asynchronous reset:
module D_flip_flop_r (input clk, reset,
      input [3:0] d,
      output reg [3:0] q);
always @ (posedge clk, posedge reset)
if (reset) q <= 4’b0;
else q <= d;

---
Verilog – always
Verilog – always
When sensitivity_list reacts/triggers on change of all inputs and output value is assigned for all combinations on inputs then always @ () is can be used to describe combinational circuit description. example:
module comb (input a, b
   output reg y);
   always @ (a,b)
  y = ~a & b;
It is better to use “*”:
module comb (input a, b
   output reg y);
   always @ (*)	// <--
  y = ~a & b;

---
Verilog – if-else
Verilog – if-else
if, if-else, case, casez has to be used inside always. Examples:
module D_flip_flop_en_r (input clk, reset, enable,
        input [3:0] d,
        output reg [3:0] q);
always @ (posedge clk, posedge reset)
if (reset) q <= 4’b0;
else if (en) q <= d;

---
Verilog – case
Verilog – case
module seven_segment_display_decoder (input [3:0] data,
        output reg [6:0] segments);
always @ (*)
case (data)
 0: segments = 7’b111_1110;
 1: segments = 7’b011_0000;
 2: segments = 7’b110_1101;
 3: segments = 7’b111_1001;
 4: segments = 7’b011_0011;
 5: segments = 7’b101_1011;
 6: segments = 7’b101_1111;
 7: segments = 7’b111_0000;
 8: segments = 7’b111_1111;
 9: segments = 7’b111_1011;
 default: segments 7’b000_0000;
endcase

---
Verilog – casez
Verilog – casez
casez: the “?” placeholder matches 0 or 1, bit/place value is ignored.
module priority_circuit(input [3:0] a,
output reg [3:0] y);
always @ (*)
casez (a)
 4’b1???: y = 4’b1000;
 4’b01??: y = 4’b0100;
 4’b001?: y = 4’b0010;
 4’b0001: y = 4’b0001;
 default: y = 4’b0000;
endcase

---
Verilog – konečný automat Mealy/Moore
Verilog – Mealy/Moore finite state machine
module FSM (input x, clk, reset,
    output y);
reg [1:0] state, nextstate;
parameter S0 = 2’b00;	// parameter – constant definition
parameter S1 = 2’b01;
parameter S2 = 2’b10;
always @ (posedge clk, posedge reset)
if (reset) state <= S0;
else state <= nextstate;
always @ (*)
case (state)	// next state logic
S0: if (x) nextstate = S1;
   else nextstate = S0;
S1: nextstate = S2;
S2: nextstate = S0;
default: nextstate = S0;
endcase
assign y = (x & state == S0 ) ? 1’b1 : 1’b0; // output logic

---
Verilog – jiný konečný automat Moore
Verilog – another Moore finite state machine
Outputs table
State	Output y
S0	0010
S1	0110
S2	1010
module FSM2 (input x, clk, reset,
    output reg [3:0] y);
reg [1:0] state, nextstate;
parameter S0 = 2'b00;
parameter S1 = 2'b01;
parameter S2 = 2'b10;
always @(posedge clk, posedge reset) // state register
if (reset) state <= S0;
else state <= nextstate;
S0
S1
S2
1
0
1
0
0
1

---
Verilog – konečný automat Moore
Verilog – Moore finite state machine
always @(*)
case (state)	// next state logic
S0: nextstate = x ? S1 : S2;
S1: nextstate = x ? S1 : S2;
S2: nextstate = x ? S1 : S0;
default: nextstate = S0; //!!
endcase
always @(*)
case (state)	// output logic
S0: y = 4'b0010;
S1: y = 4'b0110;
S2: y = 4'b1010;
default: y = 4'b0010; //!!
endcase
State	Output y
S0	0010
S1	0110
S2	1010
S0
S1
S2
1
0
1
0
0
1

---
Verilog – konečný automat Moore - Simulace
Verilog – Moore finite state machine - Simulace
`timescale 1ns / 1ps / module test_moore; / reg x; // Inputs / reg clk; / reg reset; / wire [3:0] y; // Output / FSM2 uut ( / .x(x), / .clk(clk), / .reset(reset), / .y(y) / );	initial begin / x = 0; / clk = 0; / reset = 0; / #230 x = 1; / #80 x = 0; / #100; / end / always #20 clk = ~clk; / endmodule

---
Verilog – konečný automat Moore
Verilog – Moore finite state machine
module FSM3 (input x, clk, reset,
    output reg [3:0] y);
reg [1:0] state, nextstate;
parameter S0 = 2'b00;
parameter S1 = 2'b01;
parameter S2 = 2'b10;
   initial state <= S0;
Setup and hold !!
Only difference between modules FSM3 and FSM2 is then next line...

---
Verilog – parametrizované moduly
Verilog – parameterized modules
# (parameter …) exacly after modue name modulu
module mux2
# (parameter width = 8)
(input [width:0] d0, d1,
input s,
output [width:0] y);
assign y = s ? d1 : d0;

---
Verilog – parametrizované moduly
Verilog – parameterized modules
It is possible to write:
module mux4_12(input [11:0] d0, d1, d2, d3,
      input [1:0] s,
        output [11:0] y);
wire [7:0] low, hi;
mux2 #(12) lowmux(d0,d1,s[0],low); //change 8 to 12
mux2 himux (d2,d3,s[1],hi); //original width=8, error
mux2 #(12) outmux (low, hi, s[1], y);
It is better to create parameterized module…
Warning: #(…) specifies parameter value; #... is delay.

---
Verilog – závěrečné poznámky
Verilog – final notes
Verilog is a hardware description. When designing the hardware, the “top-down” principle is used, in which individual subsystems are gradually refined, and the functionality of the system as a whole can be simulated at the design stage without specific specification of sub-subsystems at the lowest level. The same HDL code describing the behavioral behavior of a circuit can be implemented differently depending on the synthesizer tool used, its setup and the degree of optimization. For example:
module adder (input [7:0] a, b,
 output [7:0] y);
assign y = a + b;	// how is addition implementd?

---
Kontrolní otázka č.1 – Co je špatně???
Quiz question no. 1 – What is wrong???
D flip-flop triggered by rising edge of clk (positive edge):
module D_flip_flop (input clk,
 input d,
    output q);
always @ (posedge clk)
q <= d;

---
Kontrolní otázka č.1 – Co je špatně???
Quiz question no. 1 – What is wrong???
D flip-flop triggered by rising edge of clk (positive edge):
module D_flip_flop (input clk,
 input d,
    output q);
always @ (posedge clk)
q <= d;
All signals (used in always clause) on the left side of ssignemnt (=, <=) has to be declared as reg

---
Kontrolní otázka č.2 – Co je špatně???
Quiz question no. 2 – What is wrong???
Multiplexor
module mux2 (input select, d0, d1,
        output reg y);
always @ (select)
   if(select) y <= d1;
      else y <= d0;

---
Kontrolní otázka č.2 – Co je špatně???
Quiz question no. 2 – What is wrong???
Multiplexor
module mux2 (input select, d0, d1,
        output reg y);
always @ (select)
   if(select) y <= d1;
      else y <= d0;
y values is not changed when only data inputs are changed. Solution:
always @(*)
or ternar operator: assign y = select ? d1 : d0; and do not use always

---
Verilog
Verilog
Literatura:
  1. Harris D.M. – Harris S.L.: Digital design and computer architecture, ed. Morgan–Kaufmann, 2007, chapter 4: Hardware description languages
Links:
  1. http://www.aldec.com/Products/Product.aspx?productid=0380ca74-7c15-4a01-b727-2f7caab53730
  2. http://vol.verilog.com/
  3. http://www.verilogtutorial.info/
  4. http://courses.cit.cornell.edu/ece576/Verilog/LatticeTestbenchPrimer.pdf