I/O Subsystem Part 2
Computer Architectures
I/O Subsystem Part 2
Pavel Píša, Richard Šusta,
Michal Štepanovský, Miroslav Šnorek
Czech Technical University in Prague, Faculty of Electrical Engineering
Ver.1.10

---
Lecture outline
Lecture outline
- Computer Buses Hardware Components
- Design of addon PCI cards
- Design of PCIe with use of FPGA chip

---
Computer Buses Hardware Components

---
Bus-line Electronics - Buffers
Bus-line Electronics - Buffers
bi-directional
uni-directional

---
IO Output: TP and OC? Practical Examples:
IO Output: TP and OC? Practical Examples:
OC – Open Collector
TP – Totem Pole
Internal structure NAND circuit equipped
by open collector output.
Pull up resistor is connected externally.
Internal structure of two inputs
NAND chip from TTL 7400 family
Vdd
Vdd
A
B
A
B
Vss
Out

---
Study of Conflict: Bi-directional Transfer on a Single Bus Line
Study of Conflict: Bi-directional Transfer
on a Single Bus Line
&
&
No problem with parallel inputs.
There can be short circuit on outputs!
Inputs
&
&
1
0
Outputs
switched on
Solution?
switched on
+Vcc
+Vcc

---
One Solution: Output Circuit as OC x Tri-state
One Solution: Output Circuit as OC x Tri-state
OC – Open collector
3S – Tri-state output
      OE = Output Enable
Bus line
Vin
+Vcc
Bus line
+Vcc
OE

---
Bus Switches and Multiplexers
Bus Switches and Multiplexers
Texas Instruments Digital Bus Switch Selection Guide
Source:
http://www.ti.com/signalswitches
OE
A
B
Two-Port
OE
1A
S
11
B
MUX/DeMUX
1B2
Control
Logic
1A1
Bus Exchange
OE
S
1B2
1B1
1A2
Control
Logic

---
PCI Device Design Example

---
PCI Device Card Interface Design Example
PCI Device Card Interface Design Example
- The card requires three address ranges
  - Two memory mapped, 4kiB each
  - One I/O space mapped, size 16B
- Design steps
  - Analyze bus cycles sequences that should be recognized
  - Remember electronics (CPU, bus) building blocks
  - Define interface structure
  - Implement address decoder
  - Implement control logic
  - Implement data path
  - And then think what the card should be used for
    - NO, regular design starts from function and its needs

---
Bus Cycle (Transaction)
Bus Cycle (Transaction)

---
Interface Building Blocks
Interface Building Blocks
- Data bus and block to control datapath (enable, direction)
- Address signals, address decoder
- Command decoder
- Control logic
- (Interrupt signal generator – INT#)
  - Only when card uses interrupt – but highly desirable
- Logic to request bus control (initiator/master) role from the bus arbiter
  - Only if card is/can act as master (bus master DMA etc.)

---
PCI Device/Card Interface
PCI Device/Card Interface
data
Address decoder
32 bits
Datapaths control
AD
BAR addr
C/BE#
Command
decoder
4 bity
Control logic
FRAME#
TRDY#
IRDY#
and more
reg index/addr

---
Address Decoder
Address Decoder
- The basic block is address comparator
  - It compares significant bits (according to the region size) of the address sent on bus with the address stored in one of the base address registers (one comparator for each BAR)
- Address is present on AD signals only in the first phase of the bus cycle ⇒ the address has to be latched (stored) in card's address register
- If block transfers are supported then address register has to provide autoincrement function – it is realized by up counter with parallel preset (LOAD)
- Consider relocable address decoder. Consider reduced comparator – mirroring.

---
Example of DIP Switch Programmed Address Decoder
Example of DIP Switch Programmed Address Decoder
SN74LS688N – 8-bit comparator
74LS138 – 3 to 1of8 decoder

---
Configurable Address Decoder (i.e. BAR Based)
Configurable Address Decoder (i.e. BAR Based)
Address
register
COMP_MEM1
KOMP_MEM2
COMP_I/O
32 bits
20 bits
Config.
registers
20 bits
28 bits
A[31:4]
LOAD
INC1
INC4
I/O range
selected
ADDRIO
ADDRMEM
12 bits
A[11:0]
to internal
logic
AD[1:0]
A[31:12]
AD[31:0]

---
Configurable Address Decoder Signals
Configurable Address Decoder Signals
- ADDRIO
  - Address matches I/O range
- ADDRMEM
  - Address matches one of two memory mapped ranges
- Address register is a synchronous counter with parallel synchronous preset
  - LOAD – synchronous address load on the next rising edge of the clocks
  - INC1 – increment stored value/address by 1
  - INT4 – increment stored value/address by 4
- AD[1:0] – informs internal logic about burst mode type

---
Other Required Blocks
Other Required Blocks
- Configuration space
  - Register array (size 256B). All cells can be read, writes to some registers/bits are ignored (i.e. BAR's low order bits)
- Parity check (generates PERR# signal)
- Error control, i.e. check for the address register/counter overflow during continuous/burst transfer (generates SERR# signal)
- Consider wait cycles logic TRDY# assignment etc.
- Address for memory reads/writes has to be 4 bytes aligned (partial bus use/data validity can be controlled by C/BE[3:0] signals) ⇒ address increment is 4 for memory accesses
- but for I/O byte wide accesses INC1 required as well

---
Datapaths and their Control
Datapaths and their Control
- Data bus is bidirectional ⇒ the interface requires (bidirectional) transceiver with three-state outputs
- 8/16/32-bit data transfers the direction and the high impedance state control is based on command type (read/write) and on mask selecting valid octets of bits on the bus C/BE#

---
Datapath Interfacing and Separation
Datapath Interfacing and Separation
AD[31:0]
AD[31:24]
AD[23:16]
AD[15:8]
AD[7:0]
C/BE# 3
C/BE# 2
C/BE# 1
C/BE# 0
RD
WR

---
Pre-PCI Style I/O Port Realization Example
Pre-PCI Style I/O Port Realization Example
74LS244N - Edge Triggered Flip-Flop
74LS245N - Octal Bus Transceiver with 3-State Outputs

---
PCI Command Decoder
PCI Command Decoder
- Command is latched into command register
- Command decoder is then realized as combinatorial logic
- Outputs are control signals which specify:
  - data transaction direction
  - transaction type
    I/O operation, memory space operation, configuration access/cycle, interrupt request/acknowledge
- Use of combinatorial decoder simplifies control logic design
  - Compare with opcodes decode and arithmetic operation specifications described in lecture “Processor”

---
Command Decoder
Command Decoder
Command
decoder
LOAD_CMD
Command
register
C/BE[3:0]#

---
Command Decode – C/BE[3..0]# Meaning
Command Decode – C/BE[3..0]# Meaning
C/BE[0::3]#	Bus command (BUS CMD)
0000	Interrupt Acknowledge
0001	Special Cycle
0010	I/O Read
0011	I/O Write
0100	Reserved
0101	Reserved
0110	Memory Read
0111	Memory Write
1000	Reserved
1001	Reserved
1010	Configuration Read (only 11 low addr bits for fnc and reg + IDSEL)
1011	Configuration Write (only 11 low addr bits for fnc and reg + IDSEL)
1100	Memory Read Multiple
1101	Dual Address Cycle (more than 32 bits for address – i.e. 64-bit)
1110	Memory Read Line
1111	Memory Write and Invalidate

---
Command Decoder Output Signals
Command Decoder Output Signals
- RD – read operation
- WR – write operation
- IO – operation targets I/O space
- MEM – operation targets memory space
- CONF – read/write from/to configuration space
- INT – command Interrupt Acknowledge

---
Interface Control
Interface Control
- Detect start and end of a cycle
- Generates DEVSEL# if address recognized by device/card, controls address register, command register and decoder, monitors IRDY# signal (wait cycle inserted by initiator – master) to inform card logic that given transaction phase is prolonged
- Input signals are
  - FRAME# – controls transaction start and transaction last transfer phase
  - IRDY# – initiator ready/wait request
  - ADDRIO, ADDRMEM, MEM, IO

---
Interface Control Realization
Interface Control Realization
- Sequential circuit can be described/realized as finite state machine
- PCI clock signal is used as clock input for designed FSM, synchronous bus and control design
- Quiz:
- Should be design based on Moore FSM or Meally FSM or it is not important?

---
Quiz Answer
Quiz Answer
- The control logic design has to be Meally FSM, because control signals have to be prepared even before first rising clock of the PCI clock to select the right function of address latch register and other components
- Design choice
  - We consider all control signals in positive logic for simplicity

---
Interface Controller/FSM Signals
 Interface Controller/FSM Signals
- Output signals
  - LOAD
  - LOAD_CMD
  - DEVSEL#
  - VALID_TRANS
  - INC1, INC4, PAUSE (wait/phase hold for internal logic)
- Design choices
  - only active output signals are shown in the transition graph
  - ADDRESS = ((ADDRIO==1 and IO==1) or (ADDRMEM==1 and MEM==1))

---
PCI Interface FSM
PCI Interface FSM
Q
0
Q
1
FRAME# = 1
FRAME# = 0 / LOAD=1,
LOAD_CMD=1
FRAME# = 1 and ADDRES=1 /
DEVSEL# = 0, VALID_TRANS=1
Q
3
FRAME# = 1
FRAME# = 0
FRAME# = 0
and ADDRESS=0
IRDY# = 1 /
PAUSE = 1
Q
2
FRAME# = 0 and ADDRMEM=1 and
MEM=1 / DEVSEL# = 0,
VALID_TRANS=1, INC4=1
IRDY# = 1 / PAUSE = 1,
VALID_TRANS = 1
FRAME# = 0, ADDRIO=1 /
INC = 1,VALID_TRANS=1
FRAME# = 0, ARDMEM = 1 /
INC4 = 1, VALID_TRANS=1
FRAME# = 1 /
VALID_TRANS=1
FRAME# = 0 a ADDRIO=1 and
IO=1/ DEVSEL# = 0,
VALID_TRANS=1, INC=1
FRAME# = 1 and ADDRESS=0

---
Data Path Direction and HiZ Control
Data Path Direction and HiZ Control
- The data path transceiver direction and high impedance state control can be derived from signals
  - VALID_TRANS and WR
  - VALID_TRANS and RD
  generated by command decoder

---
PCI Express Design based on FPGA Chip

---
The PCIe board DB4CGX15 example
- PCIe x1
- Altera
  EP4CGX15 BF14C6N FPGA
- EPCS16 Configuration device
- 32Mbyte DDR2 SDRAM
- 20 I/O Pins
- 4 Input Pins
- 2 User LEDs