I/O Subsystem Part 1
Computer Architectures
I/O Subsystem Part 1
Pavel Píša, Petr Štěpán, Richard Šusta,
Michal Štepanovský, Miroslav Šnorek
Czech Technical University in Prague, Faculty of Electrical Engineering
Ver.1.10

---
Picture of the Day - Pine near Houska Castle
Picture to Please Eyes

---
Lecture outline
Lecture outline
- I/O subsystem – introduction
- Memory mapped I/O
- QtRVSim I/O Examples
- Use of buses in real computers
- PCI Bus – Peripheral Component Interconnect
- PCIe – Peripheral Component Interconnect Express
- HDD, SSD and RAID

---
John von Neumann's Computer Architecture
John von Neumann's Computer Architecture
von Neumann's computer architecture
Princeton Institute for Advanced Studies
28. 12. 1903 - 8. 2. 1957
5 functional units – control unit, arithmetic logic unit, memory, input (devices), output (devices)
An computer architecture should be independent of solved problems. It has to provide mechanism to load program into memory. The program controls what the computer does with data, which problem it solves.
Programs and results/data are stored in the same memory. That memory consists of a cells of same size and these cells are sequentially numbered (address).
The instruction which should be executed next, is stored in the cell exactly after the cell where preceding instruction is stored (exceptions branching etc. ).
The instruction set consists of arithmetics, logic, data movement, jump/branch and special/control instructions.
Processor
Input
Output
Memory
ctrl
ALU

---
Data Path, Control and Memory from Our CPU Design
Data Path, Control and Memory from Our CPU Design
Return back to non-pipelined CPU version
Control unit
(control path)
Memory
WE
Instr. Memory
A RD
A RD
A RD
WD
Data/ALU
(data path)
WE
Data Memory
A RD
WD
MemWrite
MemToReg
Branch
ALUControl 2:0
ALUScr
TypeRISBUJ
RegWrite
+
+
4
PC’
PC
Instr
19:15
24:20
11:7
15:0, 24:0
11:7
SrcA
SrcB
Zero
AluOut
WriteData
WriteReg
PC
PCBranch
ReadData
Result
PCPlus4
Reg.
File
A1 RD1
A2 RD2
A3
WD3
WE3
0
1
0
1
0
1
Imm
decode
6:0
31:25, 14:12
Control Unit
Opcode
Funct
SignImm
ALU

---
Signals to Connect CPU to External Memory and Peripherals
Signals to Connect CPU to External Memory and Peripherals
Memory or I/O peripherals
Data bus (D0..D31)
can be bidirectional or separate parallel or serial lane for each direction
IOW#
Control bus or signals
IOW, IOR if input output is separated from memory operations
Byte enable if bytes writes are supported on bus wider than 8-bit
IOR#
MEMW#
MEMR#
Address bus (A0..A31)
can be separate or multiplexed or encoded on same signals as data
Processor (CPU)
BE0 to 3#

---
Classification of Input/Output Devices/Peripherals
Classification of Input/Output Devices/Peripherals
- Behavior
  - Input	read only
  - Output	write only, cannot be read
  - Storage can be reread and usually rewritten
  - Communications, often hierarchy (fast bus (PCIe), slower SPI, ADC)
- Partner
  - What’s on the other end? Human or Machine
- Data Rate
  - Peak Rate of transfer between I/O and Memory or CPU
- Example
  - Keyboard → Input Device → Used by Human → 10 B/s
  - Robotic sensors and actuators
- Today peripherals are usually complex, even sensor or input requires setup, output (i.e. motor driver) requires monitoring

---
Diversity of Use and Needs of IO Devices
Diversity of Use and Needs of IO Devices
Device	Behavior	Partner	Data rate (Mbit/s)	Max latency (msec)
Keyboard	Input	Human	0.0001	200
Mouse	Input	Human	0.0038	50
Voice input	Input	Human	0.2640	10 / 0.02
Sound input	Input	Machine	3.0000	10 / 0.02
Scanner	Input	Human	3.2000	na
Voice output	Output	Human	0.2640	10 / 0.02
Sound output	Output	Human	8.0000	10 / 0.02
Laser printer	Output	Human	3.2000	na
Graphics display	Output	Human	800 - 8000	40 / nsec range
Cable modem	Bidirectional	Machine	0.1 - 100	100 / nsec range
Network/WLAN	Bidirectional	Machine	11-8000	10 / nsec range
Magnetic disk	Storage	Machine	800-3000	30
Flash disk NVMe	Storage	Machine	Up to 30000	10
DC motor control	Actuator+FB	Environment	0.080	0.05 – 0.5
PMSM DQ control	Actuator+FB	Environment	0.8	0.01 – 0.05

---
Layers of the I/O Software System
Layers of the I/O Software System
- User application communicating with device
- User/level I/O software
- Operating systems interfaces (lecture about Syscall)
  - Device-independent operating system software
  - Generic subsystems interfaces (filesystems, block management and queues, networking, terminals, GPIO)
  - Device drivers – function interfaces
  - Device drivers – physical devices and bus drivers
  - Interrupt handlers and or direct memory access (DMA)
  - Hardware

---
Linux Storage Stack Diagram (Simplified but Complex Still)
Linux Storage Stack Diagram (Simplified but Complex Still)
Source: Werner Fischer and Georg Schönberger – simplified

---
Memory-mapped I/O
Memory-mapped I/O
The idea: Processors can use the interface used for memory access (RISC-V: lw, sw instructions) to communicate with input/output (I/O) devices such as keyboards, monitors, and printers.
Common address space for I/O and memory
memory-mapped peripheral (I/O) registers
Main/system memory

---
Address Decoder – Idea
Address Decoder – Idea
Logical
Structure:
(Illusion)
Possible
physical
arrangement :
CPU
MEM
I/O 1
I/O 2
I/O 3
CPU
MEM
I/O 1
Bridge
I/O 2
I/O 3

---
Address Decoder – Central or on Addon Boards
Address Decoder – Central or on Addon Boards
Option A:
(Central)
Option B:
(Autonomous)
CPU
MEM
I/O 1
I/O 2
I/O 3
Address
Decoder
CPU
MEM
I/O 1
I/O 2
I/O 3
Address decoder
Registers
Address decoder
Registers
Address decoder
Registers
Address decoder
Registers

---
Example: Speech Synthesizer – Hardware
Example: Speech Synthesizer – Hardware
- Words are composed of one or more allophones, the fundamental units of sound. The 64 different allophones appear in the English language.
- Problem: Integrate HW support and write synthesizer driver
- Simplified assumption: 5 units (allophones) are placed at address 0x10000000. They are read by driver and sent to SP0256 synthesizer chip.
http://little-scale.blogspot.cz/2009/02/sp0256-al2-creative-commons-sample-pack.html
Czech: allophone – artikulace určitého fonému
Top View
OSC2
28
•1
V
SS
OSC1
27
2
RESET
ROM CLOCK
26
3
ROM DISABLE
SBY RESET
25
4
C1
DIGITAL OUT
24
5
C2
V
D1
23
6
C3
TEST
22
7
V
DD
SER IN
21
8
SBY
ALD
20
9
LRQ
SE
19
10
A8
A1
18
11
A7
A2
17
12
SER OUT
A3
16
13
A6
A4
15
14
A5

---
Example: Speech Synthesizer – Integration
Example: Speech Synthesizer – Integration
- When the SBY output is 1, the speech chip is standing by and is ready to receive a new allophone. On the falling edge of the address load input ALD#, the speech chip reads the allophone specified by A6:1.
- We arbitrarily have chosen that the A6:1 port is mapped to address 0xFFFFFF00, ALD# to 0xFFFFFF04, and SBY to 0xFFFFFF08.

---
Example: Speech Synthesizer – Driver
Example: Speech Synthesizer – Driver
The device driver controls the speech synthesizer by sending an appropriate series of allophones over the memory-mapped I/O interface. It follows the protocol expected by the SPO256 chip, given below:
1. Set ALD# to 1
2. Wait until the chip asserts SBY to indicate that it is finished speaking the previous allophone and is ready for the next
3. Write a 6-bit code selecting allophone to A6:1
4. Reset ALD# to 0 to initiate speech
This sequence can be repeated for any number of allophones and speech is synthesized

---
Example: Speech Synthesizer – Driver on RISC-V
Example: Speech Synthesizer – Driver on RISC-V
init:
  li s0,0xffffff00 // s0 peripheral base address
  addi t1,zero,1 // t1 = 1 (value to write to ALD#)
  addi t2,zero,20 // t2 = array size ×4 (20 bytes)
  li t3,0x1000 // t3 = array base address
  addi t4,zero,0 // t4 = 0 (array index)
start:
  sw t1,0x04(s0) // ALD#=1
loop:
  lw t5,0x08(s0) // t5 = SBY (monitor state)
  beq zero,t5,loop // loop until SBY == 1
  add t5,t3,t4 // t5 = address of allophone
  lw t5,0(t5) // t5 = allophone
  sw t5,0x00(s0) // A6:1 = allophone
  sw zero,0x04(s0) // ALD# = 0 (to initiate speech)
  addi t4,t4,4 // increment array index
  beq t4,t2,done // all allophone in array done?
  j start // repeat
done:
1. Set ALD# to 1
2. Wait until the chip asserts SBY to indicate that it is finished speaking the previous allophone and is ready for the next
3. Write a 6-bit allophone code to A6:1
4. Reset ALD# to 0 to initiate speech
Notice polling loop to check for ready to speak condition. CPU is blocked to do useful work.
Instead of polling, the processor could use an interrupt connected to SBY. When SBY rises, the processor stops what it is doing and jumps to code that handles the interrupt.

---
Serial Port – UART, The First Chance to Say Hello for CPU
Serial Port – UART, The First Chance to Say Hello for CPU
QtRVSim serial port (UART) emulation
0x00000000 ... 0xefffffff
data
main memory
CPU
RX_ST
.1
.0
0xffffc000
address
receive status
IE
READY
RX_DATA
.7..0
0xffffc004
receive shift register
receive data
TX_ST
.1
.0
0xffffc008
address
decoder
trasmit status
IE
READY
TX_DATA
.7..0
0xffffc00c
TX
transmit shift register
transmit data
Source: Wikipedia

---
QtRVSim Serial Port Addresses
QtRVSim Serial Port Addresses
SERIAL_PORT_BASE 0xffffc000
base address of QtRVSim serial port, mirrors on 0xffff0000 for MARS and QtSpim
SERP_RX_ST_REG 0xffffc000 Receiver status register
SERP_RX_ST_REG_o 0x0000 Offset of RX_ST_REG
SERP_RX_ST_REG_READY_m 0x1 Data byte is ready to be read
SERP_RX_ST_REG_IE_m 0x2 Enable Rx ready interrupt
SERP_RX_DATA_REG 0xffffc004 Received data byte in 8 LSB bits
SERP_RX_DATA_REG_o 0x0004 Offset of RX_DATA_REG
SERP_TX_ST_REG 0xffffc008 Transmitter status register
SERP_TX_ST_REG_o 0x0008 Offset of TX_ST_REG
SERP_TX_ST_REG_READY_m 0x1 Transmitter can accept next byte
SERP_TX_ST_REG_IE_m 0x2 Enable Tx ready interrupt
SERP_TX_DATA_REG 0xffffc00c Write word to send 8 LSB bits to terminal
SERP_TX_DATA_REG_o 0x000c Offset of TX_DATA_REG

---
QtRVSim Write Hello World to Serial Port
QtRVSim Write Hello World to Serial Port
loop:
    li a0, SERIAL_PORT_BASE // load base address of serial port
    addi a1, zero, text_1 // load address of text
next_char:
    lb t1, 0(a1) // load one byte after another
    beq t1, zero, end_char // is this the terminal zero byte
    addi a1, a1, 1 // move pointer to next text byte
tx_busy:
    lw t0, SERP_TX_ST_REG_o(a0) // read status of transmitter
    andi t0, t0, SERP_TX_ST_REG_READY_m // mask ready bit
    beq t0, zero, tx_busy // if not ready wait for ready condition
    sw t1, SERP_TX_DATA_REG_o(a0) // write byte to Tx data register
    jal zero, next_char // unconditional branch to process next byte
end_char:
    ebreak // stop continuous execution
    jal zero, end_char
.data
text_1:
    .asciz "Hello world.\n" // store zero terminated ASCII text

---
QtRVSim Serial Port – Single Cycle
QtRVSim Serial Port – Single Cycle
SERP_RX_ST_REG
SERP_RX_DATA_REG
SERP_TX_ST_REG
SERP_TX_DATA_REG

---
QtRVSim Serial Port – Pipelined
QtRVSim Serial Port – Pipelined
SERP_TX_DATA_REG

---
QtRVSim – Simple I/O Peripherals
QtRVSim – Simple I/O Peripherals
base of SPILED port region
SPILED_REG_BASE 0xffffc100
RGB LED 1 color components – 8 bits each
SPILED_REG_LED_RGB1 0xffffc110
SPILED_REG_LED_RGB1_o 0x0010
RGB LED 2 color components – 8 bits each
SPILED_REG_LED_RGB2 0xffffc114
SPILED_REG_LED_RGB2_o 0x0014
Three 8 bit knob values
SPILED_REG_KNOBS_8BIT 0xffffc124
SPILED_REG_KNOBS_8BIT_o 0x0024
line of 32 LEDs for binary value representation
SPILED_REG_LED_LINE 0xffffc104
SPILED_REG_LED_LINE_o 0x0004
bit 26
bit 25
bit 24
bits 23..16
bits 15..8
bits 7..0
...0
bits 31 ...

---
QtRVSim Peripherals Documentation and Frame Buffer
QtRVSim Peripherals Documentation and Frame Buffer
- All peripherals supported by QtRVSim are described at QtRVSim project page (README.md file)
  https://github.com/cvut/qtrvsim/#peripherals
- The simple 16-bit per pixel (RGB565) framebuffer
  The size corresponds to MZ_APO 480 x 320 pixel display
  components
  - bits 11 .. 15	red
  - bits 5 .. 10	green
  - bits 0 .. 4	blue
  Frame buffer starts at address
  - LCD_FB_START	0xffe00000
  - LCD_FB_END	0xffe4afff

---
Generalized Summary Based on Example
Generalized Summary Based on Example
- There are two methods for I/O devices (peripherals) access
  - memory mapped I/O
  - I/O specialized instructions (if implemented/available) – they use address space independent of memory access
- There are address range(s) dedicated to device access in the case of memory mapped I/O. Reads/writes from/to these addresses are interpreted as commands or data transfers from/to peripheral devices. Memory subsystem is informed about I/O ranges and ignores these accesses. I/O devices/bus controller is aware of addresses assigned to it and fulfills requests.
- The CPU can be informed about I/O device request for service by:
  - repeated monitoring of its ready condition (status register) – polling
  - interrupt request – interrupt-driven I/O – it is asynchronous to the actual program execution (is initiated by device when it needs servicing)
- Have you noticed address decoder function?
- What about caches in the case of I/O range/region access?

---
Use of Buses for Input/Output on Real Systems
Use of Buses for Input/Output on Real Systems

---
Motivation to Use and Study Buses
Motivation to Use and Study Buses
bus interconnection
technologies are used
everywhere to connect
computer system
components/subsystems

---
Motivation – Intel – Only as an Example
Motivation – Intel – Only as an Example

---
Personal Computer Motherboard

---
Main Task of I/O Subsystem
What is the Main Task of I/O Subsystem?
- Interconnection of subsystems inside computer, connection of external peripherals and computers together
- Demands on I/O subsystem:
  Creating optimal data paths, especially critical for the most demanding peripherals (graphic cards, external memories)
- Possible solutions:
  There have to be compromises due to price/performance ratio when it is
  - possible to share data paths, or
  - advantageous to share them.

---
Some Other Examples and Solutions
Some Other Examples and Solutions
- Do you know Parallel ATA (PATA)?
- Integrated Drive Electronics (IDE) nebo EIDE (Enhanced IDE) from Western Digital may be more known term
- ATA = Advanced Technology Attachment
It has been the most used interface to connect hard-drives and optical units
40-pin header -> 40 leads (16 of these for data)
later 80 leads used for better signal integrity (shielding), but 40-pin header preserved

---
Serial ATA – Solution Used Today
Serial ATA – Solution Used Today
- Serial ATA (SATA) more used today
- SATA 1.0: 150 MB/s (PATA:130MB/s)
- SATA 2.0: 300 MB/s
- SATA 3.0: 600 MB/s
- SATA 3.2: about 2 GB/s
Interface used for drives and optical units connection today
7 leads only!!!
Pin		Mating	Function
	1	1st	Ground
	2	2nd	A+ (Transmit)
	3	2nd	A− (Transmit)
	4	1st	Ground
	5	2nd	B− (Receive)
	6	2nd	B+ (Receive)
	7	1st	Ground
http://en.wikipedia.org/wiki/Serial_ATA

---
Interfacing Terminology – Important Terms
Interfacing Terminology – Important Terms:
- Interface
  - Common communication part shared by two systems, equipment or programs.
  - Includes also boundary and supporting control elements necessary for their interconnection.
- Bus × point-to-point connection.
- Address, data, control bus.
- Multiplexed/separate bus.
- Processor, system, local, I/O bus.
- Bus cycle, bus transaction.
- Open collector, 3-state output, switched multiplexers
- Initiator/target

---
Reminder: bus x point-to-point connection
Reminder: bus x point-to-point connection
Bus – shared data path
Remark: logical topology as seen from computer system inside (OS, programs) can differ from the physical topology
Point-to-point connection
Many different combinations in between in real systems

---
Synchronous Parallel Data Transfer
Synchronous Parallel Data Transfer
The events are determined by a clock!
Good synchronization of all signals is absolutely essential!
Bus Clock
Address
RD/WR
Data
t1
t2
t0
t3
t4

---
Asynchronous Bus
Asynchronous Bus
  - Not clocked
  - Requires a handshaking protocol (It behaves as TCP internet protocol)
    - performance not as good as that of synchronous bus
    - No need for frequency converters, but does need extra lines
  - Does not suffer from clock skew like the synchronous bus
Source: Sudeep Pasricha,
On Chip Communication, Colorado 2011
B35APO Computer Architectures

---
Asynchronous Parallel Data Transfer by Strobing
Asynchronous Parallel Data Transfer by Strobing
Strobing accelerates asynchronous bus operations,
but it is less reliable. (It behaves as UDP internet protocol)
Strobe
RD/WR
Address
Data
t1
t2
t0
Source: Sudeep Pasricha,
On Chip Communication, Colorado 2011

---
PC Architecture (cca 2000+) … Based on PCI
PC Architecture (cca 2000+) … Based on PCI
Point-to-point
Source: http://computer.howstuffworks.com/pci.htm
Buses

---
PCIe Architecture - Bus is Replaced by Shared Switch
PCIe Architecture - Bus is Replaced by Shared Switch
More details later …
PCIe = PCI Express
Microprocessor
Root
complex
End
point
End
point
End
point
RAM
RAM
RAM
End
point
End
point
End
point
End
point
End
point
End
point
End
point
Switch
Microprocessor
Bus
bridge
L2
cache
RAM
Front Side bus (FSB)
AGP
chipset
Memory
controller
RAM
RAM
Graphic
controller
Bus
bridge
PCI Bus
ISA Bus
System
memory
Back Side bus (BSB)
PCI devices
ISA devices

---
PCI Bus – Peripheral Component Interconnect
PCI Bus – Peripheral Component Interconnect

---
PCI Signals – 32-bit Version
PCI Signals – 32-bit Version
PCI
device
address
and data
AD[31::00]
C/BE[3::0]#
PAR
FRAME#
interface
control
TRDY#
IRDY#
STOP#
INTA#
interrupts
DEVSEL#
INTB#
IDSEL#
INTC#
INTD#
PERR#
error
reporting
SERR#
REQ#
access
arbitration
(master only)
GNT#
CLK#
system
RST#

---
PCI Devices Examples
PCI Devices Examples

---
PCI 32-bit Bus Signals
PCI 32-bit Bus Signals

---
PCI 64-bit Signals
PCI 64-bit Signals

---
PCI - Architecture
PCI - Architecture
Note: During initial configuration transactions only, the IDSEL is used to indicate to a PCI endpoint (or bridge) that it is currently selected.
C/BE[3::0]#
Control
AD[31::00]
Slot 1
IDSEL
REQ#
GNT#
Slot 2
IDSEL
REQ#
GNT#
Slot 4
IDSEL
REQ#
GNT#
Slot 3
IDSEL
REQ#
GNT#
PCI
Bus access arbiter
Interrupt subsystem
IRQ
IDSEL

---
PCI terms and definitions I.
PCI terms and definitions I.
Two devices participate in each bus transaction:
Initiator (starts the transaction)
× Target (obeys request)
Initiator = Bus Master,
Target = Slave for current transaction.
Initiator and target role does not directly impose data source and receiver role!

---
PCI terms and definitions II.
PCI terms and definitions II.
What does it mean that bus is multimaster?
More participants can act as Bus Master – initiate transfers!
When bus signals are shared, then transactions need to be serialized and only one device can act as master at any given time instant
Bus master is responsible to grant bus to requesting participant
Who takes care of bus arbitration?
One dedicated device or bus backplane
Note: A decentralized (distributed) bus arbitration also exists, i.e., all devices participate in the selection of the next bus master, but not for PCI.

---
PCI terms and definitions III.
PCI terms and definitions III.
The rising clock edge is reference/trigger point for all phase of the bus cycle/transaction timing
Bus cycle is formed in most cases by
address phase
data phase
Premature termination of data transfer is possible during bus cycle
Transfer synchronization itself is pseudo-synchronous

---
Reduce Bus/Signal Lines Number – Share/Multiplexing
Reduce Bus/Signal Lines Number – Share/Multiplexing
AD[31::00] signals are used for address transfer during initial transfer phase, then they are used for data
C/BE[3::0]#
Control
AD[31::00]
Slot 1
IDSEL
REQ#
GNT#
Slot 2
IDSEL
REQ#
GNT#
Slot 4
IDSEL
REQ#
GNT#
Slot 3
IDSEL
REQ#
GNT#
PCI
Bus access arbiter
Interrupt subsystem
IRQ
IDSEL

---
Bus Cycle Kind/Direction – Command – Specified by C/BE
Bus Cycle Kind/Direction – Command – Specified by C/BE
C/BE[0::3]#	Bus command (BUS CMD)
0000	Interrupt Acknowledge
0001	Special Cycle
0010	I/O Read
0011	I/O Write
0100	Reserved
0101	Reserved
0110	Memory Read
0111	Memory Write
1000	Reserved
1001	Reserved
1010	Configuration Read (only 11 low addr bits for fnc and reg + IDSEL)
1011	Configuration Write (only 11 low addr bits for fnc and reg + IDSEL)
1100	Memory Read Multiple
1101	Dual Address Cycle (more than 32 bits for address – i.e. 64-bit)
1110	Memory Read Line
1111	Memory Write and Invalidate

---
A read operation on the PCI bus
A Read Operation on the PCI Bus
1
2
3
4
5
6
7
CLK
Frame#
AD
C/BE#
IRD
Y#
TRD
Y#
DEVSEL#
Adress
#1
#4
Cmnd
Byte enable
#2
#3

---
A Read Operation on the PCI Bus 2
A Read Operation on the PCI Bus
FRAME# indicate the beginning of a transaction.
Address on the AD lines
Read command on the C/BE# lines.
1
2
3
4
5
6
7
CLK
Frame#
AD
C/BE#
IRD
Y#
TRD
Y#
DEVSEL#
Adress
#1
#4
Cmnd
Byte enable
#2
#3

---
A Read Operation on the PCI Bus 3
A Read Operation on the PCI Bus
The initiator removes the address, from the AD lines
The selected target asserts DEVSEL# to indicate recognized its address and is ready to respond
1
2
3
4
5
6
7
CLK
Frame#
AD
C/BE#
IRD
Y#
TRD
Y#
DEVSEL#
Adress
#1
#4
Cmnd
Byte enable
#2
#3

---
A Read Operation on the PCI Bus 4
A Read Operation on the PCI Bus
Asserts IRDY# to indicate ready to receive data.
Target asserts TRDY# and begins to send data.
1
2
3
4
5
6
7
CLK
Frame#
AD
C/BE#
IRD
Y#
TRD
Y#
DEVSEL#
Adress
#1
#4
Cmnd
Byte enable
#2
#3

---
A Read Operation on the PCI Bus 5
A Read Operation on the PCI Bus
If target is not ready, it would delay asserting TRDY# until it is ready.
The entire burst of data need not be sent in successive clock cycles.
Note: Either the initiator or the target may introduce a pause by deactivating its ready signal, then asserting it again when it is ready to resume the transfer of data.
1
2
3
4
5
6
7
CLK
Frame#
AD
C/BE#
IRD
Y#
TRD
Y#
DEVSEL#
Adress
#1
#4
Cmnd
Byte enable
#2
#3

---
A Read Operation on the PCI Bus 6
A Read Operation on the PCI Bus
FRAME# deactivates this signal before the last word of the transfer.
1
2
3
4
5
6
7
CLK
Frame#
AD
C/BE#
IRD
Y#
TRD
Y#
DEVSEL#
Adress
#1
#4
Cmnd
Byte enable
#2
#3

---
A Read Operation on the PCI Bus 7
A Read Operation on the PCI Bus
Target sends the last word then stops.
After sending the last word, the target deactivates TRDY# and DEVSEL# and disconnects its drivers on the AD lines.
1
2
3
4
5
6
7
CLK
Frame#
AD
C/BE#
IRD
Y#
TRD
Y#
DEVSEL#
Adress
#1
#4
Cmnd
Byte enable
#2
#3

---
Some Remarks and Observations
Some Remarks and Observations
- The length of the transferred data block is controlled by the FRAME signal. It is negated (de-asserted) before last word transfer by initiator.
- Single world or burst transfer can be delayed by inserting wait cycles (pseudo-synchronous synchronization)!

---
PCI Bus Memory Write Timing
PCI Bus Memory Write Timing

---
PCI Bus Memory Read Timing
PCI Bus Memory Read Timing

---
Interrupt Acknowledge Cycle
Interrupt Acknowledge Cycle
- Processor needs time to save interrupted execution state to allow state restoration after return from service routine
- Interrupt controller provides vector number (assigned to the asynchronous event) and CPU is required to translate it to the interrupt service routine start address
- All these activities require some time

---
Interrupt Acknowledge Cycle Timing
Interrupt Acknowledge Cycle Timing

---
Some More Details About Standard PC PIC IRQ Routing
Some More Details About Standard PC PIC IRQ Routing
INTA#
INTB#
INTC#
INTD#
PCI#4
INTA#
INTB#
INTC#
INTD#
PCI#3
INTA#
INTB#
INTC#
INTD#
PCI#4
INTA#
INTB#
INTC#
INTD#
PCI#4
PCI slots
IRQX
IRQY
IRQZ
IRQW
IRQ2,9
IRQ3
IRQ4
IRQ5
IRQ6
IRQ7
IRQ10
IRQ11
IRQ12
IRQ14
IRQ15
Interrupts from mainboard integrated peripherals
Interrupt requests multiplexor (PCI chipset)
PIC 8259#1
Timer
Keyboard
CMOS RTC
0
1
2
3
4
5
6
7
INTR
to CPU
PIC 8259#2
0
1
2
3
4
5
6
7
NXP

---
Standard PC PIC Interrupt Vectors Assignment
Standard PC PIC Interrupt Vectors Assignment
Common interrupt numbers for PC category computers:
IRQ
0	Timer (for scheduler, timers)
1	Keyboard
2	i8259 cascade interrupt
8	Real-time clocks (CMOS wall time)
9	Available or SCSI controller
10,11	Available
12	Available or PS/2 mouse
13	Available or arithmetics co-processor
14	1-st IDE controller
15	2-nd IDE controller
3	COM2
4	COM1
5	LPT2 or available
6	Floppy disc controller
7	LPT1

---
Message Signaled Interrupt
Message Signaled Interrupt
- Memory address space write by device to a special address → interrupt to CPU
- MSI from PCI 2.2 (single interrupt per device)
- MSI-X from PCI 3.0 (up to 2048 can be allocated)
- Reasons
  - Pin-based PCI interrupts often shared
  - Pin-based can arrive before data reach memory
  - PCI devices supports only single pin-based per function.

---
Recapitulation of the Bus Description Steps
Recapitulation of the Bus Description Steps
- Notice: we started PCI description by bus topology analysis, PCI signals and then we moved to timing diagrams
  - simpler cases first (read and write)
  - then how bus access is arbitrated
  - the special functions (interrupt acknowledge) last
- Doc. Šnorek recommends: always follow these steps when trying to learn new bus technology.

---
PCI Bus Timing Laboratory Exercise
PCI Bus Timing Laboratory Exercise

---
Some more notes regarding the bus hardware realization
Some more notes regarding the bus hardware realization

---
How Signals are Transferred
How Signals are Transferred
English term Signalling
Single ended (asymmetric) versus. differential (symmetric)

---
Typical Signaling Levels and Some Speed Considerations
Typical Signaling Levels and Some Speed Considerations
Differential signaling
Single ended signaling

---
PCIe – Peripheral Component Interconnect Express
PCIe – Peripheral Component Interconnect Express

---
PCIe Architecture
PCIe Architecture
Source:
  http://computer.howstuffworks.com/pci-express.htm
Microprocessor
Root
complex
End
point
End
point
End
point
RAM
RAM
RAM
End
point
End
point
End
point
End
point
End
point
End
point
End
point
Switch

---
PCIe Topology and Components
PCIe Topology and Components

---
Why Switch to Serial Data Transfer
Why Switch to Serial Data Transfer

---
RC Delay in Wire
RC Delay in Wire
R
R
`R
`R
Wire: The length of one wire element → 0 and the number of elements → ∞
uc(t)=uin (1-e-t /τ), τ=R.C
50 % = 0.69 RC
R
C
   uin
uc(t)
0
τ
2τ
3τ
86,3% uin
95% uin
63,2% uin
capacitor C is charged by R
t - time
50% uin
   C
   G
   C
   G
   C
   G
   C
   G

---
Deformation of Signals
Deformation of Signals
Source:

---
High Speed Serial Link
High Speed Serial Link
PLL
= Phase-locked Loop
(cz: fázový závěs)
generates frequency
with phase related to
input reference signal
ref clk.
Only ideal theoretical signals:-)
Source: S. Palermo: High-Speed Serial I/O Design for Channel-Limited and Power-Constrained Systems , Texas A&M University 2010

---
High Speed Serial Link Reality
High Speed Serial Link Reality
Source: TELEDYNE LECROY, 2018

---
PCIe Transfers Signaling, PCIe Lanes 1
PCIe Transfers Signaling, PCIe Lanes
- Link interconnect switch with exactly one device
- Differential AC signaling is used – two wires for single direction
- Each link consists of one or more lanes
- Lane consists of two pair of wires
- One pair for Tx and other one for Rx
- Data are serialized by 8/10 code
- The separate pairs allow full-duplex operation/transfers
Up to x16 lanes scalable

---
PCIe Slot Signals
PCIe Slot Signals

---
PCIe Transfers Signaling, PCIe Lanes
PCIe physical link layer
Differential full-duplex physical layer
8b/10b encoding provides enough edges for clock signal reconstruction/synchronization and balanced number of ones and zeros. This ensures zero common signal (DC) and AC (only) coupling is possible

---
PCIe Physical Layer Model
PCIe Physical Layer Model
Source: Budruk, R., at all: PCI Express System Architecture

---
PCIe Characteristics
PCIe Characteristics
- 2.5 GHz clock frequency (1 GT/s), raw single link single direction bandwidth 250 MB/s (can be multiplied by parallel lanes – 2×, 4×, 8×)
- Single link efficient data rate is 200 MB/s, this is 2× … 4× more than for classic PCI
- The bandwidth is not shared, point to point interconnection
- Two pairs of wires, differential signaling
- Data are encoded (modulated) using 8b/10b code
- Expected up to 10 GHz clocks due technology advances
- PCI Express 2.x (2007) allows 5 GT/s (5 GHz clock)
- PCI Express 3.x (started at 2010) increases it to 8 GT/s
- Encoding changed from 8b/10b (20% bandwidth used by encoding) to "scrambling" and 128b/130b encoding (takes only 1.5% of the bandwidth)

---
PCI and PCIe Slots on the PC Motherboard
PCI and PCIe Slots on the PC Motherboard
PCIe x4
PCIe x16
PCIe x1
PCIe x16
32-bit classic
PCI slot
LanParty nF4 Ultra-D mainboard from DFI
Picture source: Wikipedia

---
ExpressCard
ExpressCard
PCIe 1
PCIe 4
CardBus
PCMCI
ExpressCard/34
ExpressCard/54
PCIe 8
PCIe 1

---
The PCIe board DB4CGX15 example
The PCIe board DB4CGX15 Example
- PCIe x1
- Altera
  EP4CGX15 BF14C6N FPGA
- EPCS16 Configuration device
- 32Mbyte DDR2 SDRAM
- 20 I/O Pins
- 4 Input Pins
- 2 User LEDs

---
PCIe Communication Protocol – HW and SW Layers
PCIe Communication Protocol – HW and SW Layers
PCIe physical topology is serial, point-to-point, packet oriented, but its logical view and behavior is the same as PCI – that is multi-master bus, same enumeration, read/write cycles

---
Data Packet Structure and Transport Layers
Data Packet Structure and Transport Layers
Source: http://zone.ni.com/devzone/cda/tut/p/id/3767#toc0

---
PCIe Packet Format
PCIe Packet Format
Specification highlights:
Packet length from 4B to 4096B
PCIe packed has o be exchanged as the whole (no option to preempt when higher priority transfer is requested)
Long packed can cause increase of latencies in the system
On the other hand, short packets overhead (frame/data) is considerable

---
USB-C, Alternative Modes, PCIe and Thunderbolt
USB-C, Alternative Modes, PCIe and Thunderbolt
- SuperSpeed+ / USB 2.0 with up to 480 Mbit/s data rate
- 10 and 20 Gbit/s (1 and ~2.4 GB/s) when two lanes used
- USB Power Delivery 2.0 3 A current (@ 20 V, 60 W), high-power 5 A current (@ 20 V, 100 W).
- Cable electronic ID chip
- Alternate Mode partner specifications: DisplayPort, Mobile High-Definition Link, Thunderbolt, HDMI

---
USB-C Signals
USB-C Signals
Pin	Name	Description	Pin	Name	Description
A1	GND	Ground return	B12	GND	Ground return
A2	SSTXp1	SuperSpeed diff. pair #1, TX, pos.	B11	SSRXp1	SuperSpeed diff. pair #2, RX, pos.
A3	SSTXn1	SuperSpeed diff. pair #1, TX, neg.	B10	SSRXn1	SuperSpeed diff. pair #2, RX, neg.
A4	VBUS	Bus power	B9	VBUS	Bus power
A5	CC1	Configuration channel	B8	SBU2	Sideband use (SBU)
A6	Dp1	USB 2.0 diff. pair, position 1, pos.	B7	Dn2	USB 2.0 diff. pair, position 2, neg.
A7	Dn1	USB 2.0 diff. pair, position 1, neg.	B6	Dp2	USB 2.0 diff. pair, position 2, pos.
A8	SBU1	Sideband use (SBU)	B5	CC2	Configuration channel
A9	VBUS	Bus power	B4	VBUS	Bus power
A10	SSRXn2	SuperSpeed diff. pair #4, RX, neg.	B3	SSTXn2	SuperSpeed diff. pair #3, TX, neg.
A11	SSRXp2	SuperSpeed diff. pair #4, RX, pos.	B2	SSTXp2	SuperSpeed diff. pair #3, TX, pos.
A12	GND	Ground return	B1	GND	Ground return
Source: https://en.wikipedia.org/wiki/USB-C

---
PCI(e) I/O Bandwidth Expectations and Reality
PCI(e) I/O Bandwidth Expectations and Reality
PCIe buses overcome theoretical expectations
Source: Nextpatform

---
PCI-signal Bandwidth in Numbers
PCI-signal Bandwidth in Numbers
Source: Nextpatform

---
PCI/PCIe Programmer/Operating System Model
PCI/PCIe Programmer/Operating System Model

---
Computer Startup Procedure (from PCI perspective)
Computer Startup Procedure (from PCI perspective)
1. CPU is directed by BIOS code to retrieve device identification for each PCI slot. This is done by read cycle from PCI configuration space. The read (topological) address decodes to IDSEL (Initialization Device Select) signal to the corresponding PCI slot (bus/device/function) + register number
2. Each device identification (Vendor ID, Device ID) and request for I/O resources (sizes of I/O ports and memory ranges and interrupt link (A/B/C/D) use by function) are read. All this information is available in card/slot configuration space. This search is done together with bus numbers assignment when bridge is found.
3. BIOS allocates non-overlapping ranges to the devices. It ensures that there is no collision with system memory and I/O. Interrupts can be, and are, shared but sharing level can be balanced. Allocated ranges/resources are written to the corresponding device/function Base Address Register (BAR). They usually stay constant till computer power off but OS can reconfigure them under certain circumstances.
4. Operating System is loaded and given control. OS reads devices identifications again from PCI configuration space and locates device drivers according to VID:PID (+class,+subsystem IDs).
This process of device “searching” is called enumeration and is used in some form by each PnP aware bus (PCI, USB, etc.).

---
PCI Bus Hierarchy
PCI Bus Hierarchy

---
PCI BUS Address Space(s)
PCI BUS Address Space(s)
- PCI bus recognizes three address spaces:
  - memory – address is 32 or 64-bit
  - I/O – exists mainly for compatibility with x86 specific I/O ports and I/O instructions concept
  - configuration space – 256 bytes are assigned to each device function in the basic PCI bus variant, 8 functions per device/slot/card and 32 devices per bus can exist in maximum.
- Each end-point device can implement up to 6 Base Address Registers (BARs) which can define up to 6 independent regions (address ranges) – each for I/O or memory mapped access. For 64-bit ranges BARs are used in pairs. The requested size is obtained by writing ones into BAR bits and reading back where BAR's bits corresponding to the range size are fixed on zero. LSB bits then informs about address space type. Then BIOS/OS writes allocated region start address back to the BAR.

---
PCI Configuration Space Address and Access
PCI Configuration Space Address and Access
1 from n original IDSEL activation address – not used today
Topological/geographical BDF address
- There are two mechanisms of accessing configuration space on x86 PC:
  - Through well known I/O ports
    0xCF8 – PCI CONFIG_ADDRESS (write address first, A0:1=0)
    0xCFC – PCI CONFIG_DATA (read/write corresponding byte, 16-bit or 32-bit entity, address bits 0 and 1 added to 0xCFC)
  - Enhanced Configuration Access Mechanism (ECAM) – required for PCI express – 4kB per slot, memory mapped

---
PCI Device Header
PCI Device Header
Device's PCI header is located in PCI bus configuration space
0
1
31
Reserved
Base Address
1
Base Address for PCI I/O Space
2
2
3
4
Base Address
Type
prefetchable
Base Address for PCI Memory Space
0
1
0
31

---
PCI Device Header Type 0 – End-point device
PCI Device Header Type 0 – End-point device

---
PCI Device Header Type 1 – Bus Bridges
PCI Device Header Type 1 – Bus Bridges

---
PCI BARs Mapping
PCI device/card is informed about assigned addresses …
I/O address space (x86 in, out instructions)
Memory space: common for I/O and system memory
I/O
PCI card #0
Mem
BAR 0
BAR 1
Memory
BAR 2
BAR 3
If CPU writes to this location, write is recognized by PCI device/card #0. Its effect depends on card logic. I.e. for graphic card frame-buffer it behaves same as regular memory, but data are seen on the screen.
data
BAR 4
data
BAR 5
data
BAR registry
I/O
Mem
PCI card #1
BAR 0
Mem
BAR 1
BAR 2
BAR 3
data
data
BAR 4
Mem
BAR 5
data

---
PCI BARs Mapping to Virtual Addresses
PCI device/card is informed about assigned addresses …
I/O address space (x86 in, out instructions)
Memory space: common for I/O and system memory
I/O
PCI card #0
Mem
BAR 0
BAR 1
Memory
BAR 2
This is physical
/bus address
BAR 3
If CPU writes to this location, write is recognized by PCI device/card #0. Its effect depends on card logic…
data
BAR 4
data
BAR 5
data
BAR registry
I/O
Mem
mmap(BAR1)
PCI card #1
BAR 0
Mem
BAR 1
Study mmap() function manual.
Do not forget to munmap()…
BAR 2
CPU/code use virtual addresses and are translated by MMU !!!
base addr. +4
BAR 3
data
mmap(BAR0)
data
BAR 4
Mem
BAR 5
mmap(BAR1)
data

---
Linux /proc/bus/pci Directory
Linux /proc/bus/pci Directory
- Each directory represents one PCI bus (with its number assigned) and each file mirrors one PCI device function PCI header (the first 64 bytes)
- Homework: Write C/C++ language program that can traverse and open files in given directory and its subdirectory and searches for given sequence of four characters (4B) at each file start. The full path of the first matching file is printed.

---
Linux /proc/bus/pci Directory – Command lspci -vb
Linux /proc/bus/pci Directory – Command lspci -vb
00:00.0 Host bridge: Intel Corporation 82X38/X48 Express DRAM Controller
        Subsystem: Hewlett-Packard Company Device 1308
        Flags: bus master, fast devsel, latency 0
        Capabilities: [e0] Vendor Specific Information <?>
        Kernel driver in use: x38_edac
        Kernel modules: x38_edac
00:01.0 PCI bridge: Intel Corporation 82X38/X48 Express Host-Primary PCI Express Bridge
        Flags: bus master, fast devsel, latency 0
        Bus: primary=00, secondary=01, subordinate=01, sec-latency=0
        I/O behind bridge: 00001000-00001fff
        Memory behind bridge: f0000000-f2ffffff
        Kernel driver in use: pcieport
        Kernel modules: shpchp
00:1a.0 USB Controller: Intel Corporation 82801I (ICH9 Family) USB UHCI Controller #4 (rev 02)
        Subsystem: Hewlett-Packard Company Device 1308
        Flags: bus master, medium devsel, latency 0, IRQ 5
        I/O ports at 2100
        Capabilities: [50] PCI Advanced Features
        Kernel driver in use: uhci_hcd

---
Disk – Another Critical Memory Hierarchy Component
Disk – Another Critical Memory Hierarchy Component
- Enhancement required
  - Speedup
  - Reliability

---
Hard Drive
Hard Drive
Drawing source: Junfeng Yang
Picture source: https://www.hddzone.com/hard_disk_drive_compontents.html

---
Disk Storage
Disk Storage
Source: U. Ramachandran and W. D. Leahy Jr.: An Integrated Approach to Architecture and Operating Systems , 2008
Head Assembly
All heads move
together
Platter
Sector
Top and bottom
Surfaces
Head
Spindle
Track
Shaft
Arm

---
Disk Storage 1
Disk Storage
Source: U. Ramachandran and W. D. Leahy Jr.: An Integrated Approach to Architecture and Operating Systems , 2008
Cylinder X: Track X
from all 12 surfaces
(2 per platter)
Each circle represents
two tracks: one for top surface
and one for bottom surface

---
Sequential v.s. Random
Sequential v.s. Random
A sequential access
Seek to the right track
Rotate to the right sector
Transfer
A random access of the same amount of data
Seek to the right track
Rotate to the right sector
Transfer
Repeat
Since seek and rotate are slow, sequential access is much faster than random access

---
Examples of HD Parameters
Examples of HD Parameters
	Barracuda 180	Cheetah X15 36LP
Capacity	181GB	36.7GB
Disk/Heads	12/24	4/8
Cylinders	24247	18479
Sectors/track	~609	~485
Speed	7200 RPM	15000 RPM
Rotational latency (ms)	4.17	2.0
Avg seek (ms)	7.4	3.6
Track-2-track(ms)	0.8	0.3
Table source: Junfeng Yang

---
Maximum RPM
Maximum RPM
The sound velocity at the HDD circuit is reached at RPM
Diameter	RPM
3.5 inch	73105
2.5 inch	102347
But RPM also increases spinning and centrifugal power
Sonar boom - source: U.S. Navy/Travis K. Mendoza

---
IOPS
IOPS
IOPS stands for input/output operations per second
IOPS=1 / (Average Seek Time + Average Latency)
Pameter	HD	SSD
IOPS	55-180	3000-40000
IOPS/Watt	10-30	2000-60000
$/GB	$0.02 - $0.04	$0.25-$0.50
Data retention if unplugged	10 - 60 years	1 - ?100? years / 25 °C SSD are used for short time, reliable data are unknown yet
Backblaze Hard Drive Stats https://www.backblaze.com/b2/hard-drive-test-data.html

---
SSD vs HDD
SSD vs HDD
Google test of SSD:
The annual replacement rates of hard disk drives have previously been reported to be 2-9%, which is high compared to the 4-10% of flash drives we see being replaced in a 4 year period.
However, flash drives are less attractive when it comes to their error rates. More than 20% of flash drives develop uncorrectable errors in a four year period, 30-80% develop bad blocks and 2-7% of them develop bad chips.
In comparison, previous work [1] on HDDs reports that only 3.5% of disks in a large population developed bad sectors in a 32 months period
– a low number when taking into account that the number of sectors on a HDD is orders of magnitudes larger than the number of either blocks or chips on a SSD, and that sectors are smaller than blocks, so a failure is less severe.
[1] An analysis of latent sector errors in disk drives. BAIRAVASUNDARAM, L. N., GOODSON, G. R., PASUPATHY, S., AND SCHINDLER, JIn Proceedings of the 2007 ACM SIGMETRICS International Conference on Measurement and Modeling of Computer Systems, SIGMETRICS ’07, ACM, pp. 289–300.

---
RAID 0
RAID 0
- RAID – Redundant Array of Inexpensive/Independent Disks
- Can be used to achieve higher performance/throughput of the hard disks
- Method called stripping
- Raw bandwidth up to two times higher
- Capacity is sum of the both devices
Images source: Wikipedia

---
RAID 1
RAID 1
- Each data block exists in two copies, each on one of two independent disks
- The total capacity is same as of a single disk
- Data reliability is much higher, probability of coincidence of two independent events (disk failures) is much much lower than for single device
- Method is called mirroring
- Write has some overhead against single device. Reads can be optimized for less head movement

---
RAID 10
RAID 10
- It is combination of both previous techniques
- RAID 0 is created first on two (or more) devices and all data are copied on the second set of devices (same as for RAID1)
- RAID 10 contributes to both – reliability and performance
- Disadvantage – at least 4 drives with same capacity are required.
- Total capacity T, disk capacity D, number of drives n
n = 2 cdot ceil left ( {T} over {2 cdot D} right )
n = 2 cdot ceil left ( {T} over {D} right )
RAID 1
RAID 0
n = 4 cdot ceil left ( {T} over {2 cdot D} right )
RAID 10

---
RAID 5
RAID 5
- The data blocks are distributed over n-1 drives (for each disk LBA) and last block represents parity (XOR for example) of previous blocks
- But disk used for parity is chosen sequentially for each disk LBA – it balances number of rewrites and speed gain for degraded mode
- It speeds-up reads, single block write is slower because of checksum computation overhead
n = ceil left ( {T} over {D} right ) + 1

---
RAID 6
RAID 6
- Uses two parity blocks on different disks for given disk LBA. Each parity is computed different way.
- It is resistant to two concurrent disk failures
- The read is speed similar to RAID 5, write is more demanding/complex
n = ceil left ( {T} over {D} right ) + 2

---
RAID Discs Failure Probability for 2 Disks
RAID Discs Failure Probability for 2 Disks
Use of 2 same disks
- RAID0
  T = 2D
- RAID1
  T = D
RAID1 2-way
single disk
RAID0 2 disks
single disc survival probability
whole array survival probability

---
RAID Discs Failure Probability for 4 Disks
RAID Discs Failure Probability for 4 Disks
Use of 4 same disks
- RAID0
  T = 4D
- RAID1
  T = D
- RAID5
  T = 3D
- RAID6
  T = 2D
RAID1 4-way
RAID6 2+2
RAID5 3+1
RAID0 4 diskd
single disc survival probability
whole array survival probability

---
RAID Discs Failure Probability for 6 Disks
RAID Discs Failure Probability for 6 Disks
Use of 6 same disks
- RAID0
  T = 6D
- RAID1
  T = D
- RAID5
  T = 5D
- RAID6
  T = 4D
RAID1 6-way
RAID6 4+2
RAID5 5+1
RAID0 6 disks
single disc survival probability
whole array survival probability