## Slide 1: fMR Processing(1)
Ing. Jan Šanda

## Slide 2: fMR processing (1. excercise) Pipeline
Conversion of data: DICOM -> NIFTI  (done; *.nii suffix)
Slice Timing: temporal correction (TR vs. HRF)  (skipping this step)
Realignment of functional data - spatial correction of data in time
Smooth with Gauss filter kernel
Model specification + Review
Estimate Model
Results + Display
DICOM = Digital Imaging and Comminications in Medicine
NIFTI = Neuroimaging Informatics Technology Initiative

## Slide 3: Necessary SW: Matlab + SPM12 toolbox (Win, MacOS)
Statistical Parametric Mapping
SPM12 download:
https://www.fil.ion.ucl.ac.uk/spm/software/spm12/
SPM12 manual:
„../toolbox/spm12/man/manual.pdf“
4 basic SPM windows: - Menu
- Results
- Graphic
- Batch Editor

## Slide 4: Recommended resources
SPM12
https://www.fil.ion.ucl.ac.uk/spm/doc/
GLM
https://www.fil.ion.ucl.ac.uk/mfd_archive/2011/page1/mfd2011_GLM.pdf

## Slide 5: fMR processing Data
Paradigm:
  FingerTapping (upper extremities fingers) 150vol, TR=2000ms, 60 slices
Volunteer data: folders Subj01, Subj02, … Subj08
Folder structure: fMR_HK (150 nii-files: “fMR_hk_[XXX].nii”)
t1 (1 nii-file: “t1.nii”)
Subj01 | V-B | 2000 | 1.3.2023
Subj02 | P-D | 1999 | 1.3.2023
Subj03 | T-G | 1998 | 8.3.2023
Subj04 | P-K | 2000 | 15.3.2023
Subj05 | M-K | 2000 | 8.3.2023
Subj06 | K-P | 2000 | 8.3.2023
Subj07 | M-S | 2000 | 1.3.2023
Subj08 | J-V | 2000 | 15.3.2023

## Slide 7: Slice timing (skipping this step, TR=2s)
1
60
TR = 6000ms
1. volume
2. volume
3. volume
4. volume
. . . . .

## Slide 8: Realign data
This routine realigns a time-series of images acquired from the same subject using a least squares approach and a 6 parameter (rigid body) spatial transformation. The first image in the list specified by the user is used as a reference to which all subsequent scans are realigned. The reference scan does not have to the the first chronologically and it may be wise to chose a "representative scan" in this role.
The aim is primarily to remove movement artefact in fMRI and PET time-series (or more generally longitudinal studies). The headers are modified for each of the input images, such that. they reflect the relative orientations of the data. The details of the transformation are displayed in the results window as plots of translation and rotation. A set of realignment parameters are saved for each session, named rp_*.txt. These can be modelled as confounds within the general linear model

## Slide 9: Realign data

## Slide 10: Realign data
MENU: Realign (Estimate & Reslice)
BATCH EDITOR:
Data – Session … all fMR files
Run batch
Output:
Resliced files (prefix „r*.nii“)
„mean*.nii“ file (mean of all fMR files)
Realign parameters file „rp_*.txt“

## Slide 11: Smooth

## Slide 12: Smooth
MENU: Smooth
BATCH EDITOR:
Images to smooth … select all r*.nii files
FWHM … [4 4 4] (Full width at half maximum of the Gaussian smoothing kernel in mm, doubled size of voxel recommended)
Run batch
Output:
Smoothed files (all with prefix „s*.nii“)

## Slide 13: Data check (!)

## Slide 14: GLM – General Linear Model
y = X + e
Dependent variable
BOLD signal in particular voxels
Independent variable (Predictor)
Experiment conditions
Beta parameters (regression coeff.)
Quantifies how much each predictor (X)
independently influences
the dependent variable (Y)
Error (Residuals)
Variancein the data (y), which is not explained
By the linear combination of predictors (x)
https://www.fil.ion.ucl.ac.uk/mfd_archive/2011/page1/mfd2011_GLM.pdf

## Slide 16: fMR Statistics Model specification

## Slide 17: fMR Statistics Model specification
MENU: Specify 1st-level
BATCH EDITOR:
Directory … select (pre-created) folder “model” to store model and statistics results
Units for design … Scans
Interscan interval … 2 (equals to TR)
Data & Design
  Scans … select sr*.nii data
  Conditions
    Condition
      Name … name of processed paradigm, for example “RightHand”, “LeftHand”
      Onset … vector of scans where the activations begins
      Durations … duration of activation (in scans)
Run batch
Output:
SPM.mat file (GLM model)

## Slide 18: fMR Statistics Model specification
Condition LeftHand
  Name … LeftHandFingerTapping
  Onset … [16 61 106]
  Durations … 15
Condition RightHand
  Name … RightHandFingerTapping
  Onset … [31 76 121]
  Durations … 15

## Slide 19: fMR Motor paradigm (in scans; scan = 2s)
1
16
31
46
61
76
91
106
121
136
150
15
15
15
rest
left
fingertapping
right
fingertapping

## Slide 20: fMR Statistics Model review

## Slide 21: fMR Statistics Model review

## Slide 22: fMR Statistics Model review
MENU: Review
BATCH EDITOR:
Select SPM.mat … select SPM.mat
Run batch
RESULTS:
Design – Design Matrix (model design for selected parameters)
Design – Explore – Session 1 – LeftHandFingerTapping (time and frequency domain of the model)
Design – Explore – Session 1 – RightHandFingerTapping (time and frequency domain of the model)

## Slide 23: fMR Statistics Model estimation

## Slide 24: fMR Statistics Model estimation
MENU: Estimate
BATCH EDITOR:
Select SPM.mat … select SPM.mat
Run batch

## Slide 25: fMR Statistics Results

## Slide 26: fMR Statistics Model estimation
MENU: Results
Select SPM.mat
SPM contrast manager:
Define new contrast
  Name: LeftHand / RightHand
type: t-contrast
contrast: 1 0 0 / 0 1 0 …submit
OK
Done

## Slide 27: fMR Statistics Model estimation
RESULTS:
  apply masking … none
  P value adjustment to control … FWE
  P value (FWE) … 0.05
  & extent threshold {voxels} … 60

## Slide 28: fMR Statistics Display
overlays…:
  Slices
  Sections (multiplanar)
  Montage (Axial / Coronal / Sagittal)
  mean*.nii
plot:
Plot … Fitted responses – adjusted
Plot against … scan or time