RISC architectures examples – ARM, AArch64 a RISC-V
Advanced Computer Architectures
RISC architectures examples – ARM, AArch64 a RISC-V
Czech Technical University in Prague, Faculty of Electrical Engineering
Slides authors: Pavel Píša, Michal Štepanovský

---
ARM architecture - registers
ARM architecture - registers

---
ARM architecture – ALU and operands encoding
ARM architecture – ALU and operands encoding
Register, optionally with shift operation
Shift value can be either be:
5 bit unsigned integer
Specified in bottom byte of another register.
Used for multiplication by constant
Immediate value
8 bit number, with a range of 0-255.
Rotated right through even number of positions
Allows increased range of 32-bit constants to be loaded directly into registers
Result
Operand 1
Barrel
Shifter
Operand 2
ALU

---
ARM architecture – program status word
ARM architecture – program status word
Interrupt Disable bits.
I = 1: Disables the IRQ.
F = 1: Disables the FIQ.
T Bit
Architecture xT only
T = 0: Processor in ARM state
T = 1: Processor in Thumb state
Mode bits
Specify the processor mode
Condition code flags
N = Negative result from ALU
Z = Zero result from ALU
C = ALU operation Carried out
V = ALU operation oVerflowed
Sticky Overflow flag - Q flag
Architecture 5TE/J only
Indicates if saturation has occurred
J bit
Architecture 5TEJ only
J = 1: Processor in Jazelle state
27
31
N Z C V Q
28
6
7
I F T mode
16
23
8
15
5
4
0
24
f
s
x
c
U n d e f i n e d
J

---
ARM architecture – CPU execution modes
ARM architecture – CPU execution modes
- User : unprivileged mode under which most tasks run
- FIQ : entered when a high priority (fast) interrupt is raised
- IRQ : entered when a low priority (normal) interrupt is raised
- Supervisor : entered on reset and when a Software Interrupt instruction is executed
- Abort : used to handle memory access violations
- Undef : used to handle undefined instructions
- System : privileged mode using the same registers as user mode

---
ARM 64-bit – AArch64
ARM 64-bit – AArch64
- Calling uses LR, no register banking, ELR for exceptions
- PC is separate register (not included in general purpose registers file)
- 31 64-bit registers R0 to R30 (R30 = X30 ≅ LR)
  - Symbol Wn (W0) used for 32-bit access, Xn (X0) for 64-bit
  - Reg. code 31 same role as MIPS 0, WZR/XZR in code
  - Reg. code 31 special meaning as WSP, SP for some opcodes
- Immediate operand 12-bit with optional LS 12 for arithmetic operations and repetitive bit masks generator for logic ones
- 32-bit operations ignore bits 32–63 for source and zeroes these in the destination register

---
AArch64 – Branches and conditional operations
AArch64 – Branches and conditional operations
- Omitted conditional execution in all instructions as well as Thumb IT mechanism
- Conditional register retain, CBNZ, CBZ, TBNZ, TBZ added
- Only couple of conditional instructions
- add and sub with carry, select (move C?A:B)
- set 0 and 1 (or -1) according to the condition evaluation
- conditional compare instruction
- 32-bit and 64-bit multiply and divide (3 registers), multiply with addition 64×64+64 → 64 (four registers), high bits 64 to 127 from 64×64 multiplication

---
AArch64 – Memory access
AArch64 – Memory access
- 48+1 bit address, sign extended to 64 bits
- Immediate offset can be multiplied by access size optionally
- If register is used in index role, it can be multiplied by access size and can be limited to 32 bits
- PC relative ±4GB can be encoded in 2 instructions
- Only pair of two independent registers LDP and STP (omitted LDM, STM), added LDNP, STNP
- Unaligned access support
- LDX/STX(RBHP) for 1,2,4,8 and 16 bytes exclusive access

---
AArch64 – Address modes
AArch64 – Address modes
- Simple register (exclusive)
  [base{,#0}]
- Offset
  [base{,#imm}]	– Immediate Offset
  [base,Xm{,LSL #imm}]	– Register Offset
  [base,Wm,(S|U)XTW {#imm}]	– Extended Register Offset
- Pre-indexed
  [base,#imm]!
- Post-indexed
  [base],#imm
- PC-relative (literal) load
  label
Bits	Sign	Scaling	WBctr	LD/ST type
0	-	-	-	LDX, STX, acquire, release
9	signed	scaled	option	reg. pair
10	signed	unscaled	option	single reg.
12	unsig.	scaled	no	single reg.

---
Apple A12Z Bionic – 64-bit ARM-based
Apple A12Z Bionic – 64-bit ARM-based
People who are really serious about software should make their own hardware. Alan Kay
Apple A12Z, 8 cores (ARM big.LITTLE: 4 "big" Vortex + 4 "little" Tempest), Max. 2.49 GHz, ARMv8.3‑A
Cache L1 128 KB instruction, 128 KB datam L2 8 MB
GPU Apple designed 8-Core

---
Apple M1, A14, 4 Firestorm, 4 Icestorm
Source: https://www.anandtech.com/show/16226/apple-silicon-m1-a14-deep-dive

---
Intel versus Apple Top Single Thread Performance
Intel versus Apple Top Single Thread Performance
Last 5 years
Intel +28%
Apple +198%
        2.98×

---
Fujitsu – Supercomputer Fugaku – A64FX, 2020 TOP500 #1
Fujitsu – Supercomputer Fugaku – A64FX, 2020 TOP500 #1
Combine Armv8.2-A (AArch64 only) with Fujistu supercomputer technology, SPARC64 V till now
48 computing cores + 4 assistant cores, SVE 512-bit wide SIMD
HBM2 32GiB, 7nm FinFET, 8,786M transistors
Tofu 6D Mesh/Torus, 28Gbps x 2 lanes x 10 ports, PCIe
Netwrok
on
Chip
HBM2
PCIe
controller
Tofu
controller
HBM2
HBM2
HBM2

---
ARM Cortex-X1
ARM Cortex-X1
- Cortex-X1 based on Cortex-A78
- 5-wide decode out-of-order superscalar
- 3K macro-OP (MOPs) cache
- Fetch 5 instructions / 8 MOPs per cycle
- Rename and dispatch 8 MOPs / 16 µOPs / cycle.
- Out-of-order window size 224 entries
- 15 execution ports
- Pipeline depth of 13 stages
- Execution latencies consists of 10 stages
- 4x128b SIMD units.

---
RISC-V – optimize and simplify RISC again
RISC-V – optimize and simplify RISC again
- Patterson, Berkeley RISC 1984 → initiation of RISC era, evolved into SPARC (Hennessy MIPS, Stanford University)
- Commercialization and extensions results in too complex CPUs again, with license and patents preventing even the original inventors to use real/actual implementations in silicon to be used for education and research
- MIPS is model architecture for prevalent amount of base courses and implementation of similar processor is part of follow up courses (A4M36PAP)
- Krste Asanovic and other Dr. Patterson's students initiated development of new architecture (start of 2010)
- BSD License to ensure openness in the future
- Supported by GCC, binutils, Linux, QEMU, etc.
- Simpler than SPARC, more like MIPS but optimized on gate level load (fanout) and critical paths lengths in future designs
- Some open implementations already exist: Rocket (SiFive, BOOM ), project lowRISC contributes to research in security area, in ČR Codasip
- Already many implementations in silicon

---
RISC-V – architecture specification
RISC-V – architecture specification
- ISA specification can be found at
  - The RISC-V Instruction Set Manual, Volume I: User-Level ISA, Version 2.0
  - Andrew Waterman, Yunsup Lee, David Patterson, Krste Asanovic
  - Not only architecture description but even choices analysis with pros&cons of each selection and cost source description/analysis of alternatives
- classic design, 32 integer registers, the first tied to zero. regsrc1, regsrc2, regdest operands, uniqueness, rule kept strictly even for SaveWord, leads to non-continuous immediate operands encoding, PC not part of base register file, PC-relative addressing
- variants for 32, 64 a 128-bit registers and address-space defined
- high code density (16-bit instruction encoding variant planned)
- encoding reserves space for floating point (single, double, quad) and multimedia SIMD instructions in a systematic way, etc.

---
RISC-V – registers
RISC-V – registers
Integer registers
Floating point registers
Variant	XLEN
RV32	32
RV64	64
RV128	128
Variant	FLEN
F	32
D	64
Q	128
Floating-point control and status register
Source: https://riscv.org/specifications/

---
RISC-V – instruction length encoding
RISC-V – instruction length encoding
Source: https://riscv.org/specifications/

---
RISC-V – 32-bit instructions encoding
RISC-V – 32-bit instructions encoding
Source: https://riscv.org/specifications/

---
RISC-V – calling convention
RISC-V – calling convention
Register	ABI Name	Description	Saver
x0	zero	Hard-wired zero
x1	ra	Return address	Caller
x2	sp	Stack pointer	Callee
x3	gp	Global pointer	–
x4	tp	Thread pointer	–
x5	t0	Temporary/alternate link register	Caller
x6–7	t1– 2	Temporaries	Caller
x8	s0/fp	Saved register/frame pointer	Callee
x9	s1	Saved register	Callee
x10–11	a0–1	Function arguments/return values	Caller
x12–17	a2–7	Function arguments	Caller
x18–27	s2–11	Saved registers	Callee
x28–31	t3–6	Temporaries	Caller
f0–7	ft0–7	FP temporaries	Caller
f8–9	fs0–1	FP saved registers	Callee
f10 – 11	fa0–1	FP arguments/return values	Caller
f12–17	fa2–7	FP arguments	Caller
f18–27	fs2–11	FP saved registers	Callee
f28–31	ft8–11	FP temporaries	Caller

---
RISC-V Rocket Core
 RISC-V Rocket Core
Source: http://www-inst.eecs.berkeley.edu/~cs250/fa13/handouts/lab2-riscv.pdf
Implemented in chisel
https://github.com/freechipsproject/rocket-chip
git clone git://github.com/freechipsproject/rocket-chip.git
branches boom, boom-devel, boom2 …

---
CS250 Rocket Pipeline and Memory Hierarchy
CS250 Rocket Pipeline and Memory Hierarchy
Source: http://www-inst.eecs.berkeley.edu/~cs250/fa13/handouts/lab2-riscv.pdf
Uncore
Rocket
L1 D$
L1 I$
Processor
Logic
2:1 Mux
Emulated
DRAM

---
Why Chisel?
Why Chisel?
- RTL generator written in Chisel
  - HDL embedded in Scala
- Full power of Scala for writing generators
  - object-oriented programming
  - functional programming
Chisel Program
Scala/JVM
C++
FPGA
code
ASIC
Verilog
Verilog
C++ Compiler
FPGA Tools
Software
Simulator
ASIC Tools
FPGA
Emulation
GDS
Layout
5

---
CHISEL
CHISEL
- Open-source hardware construction language
- UC Berkeley
- Supports advanced hardware design
- Highly parameterized generators
- Layered domain-specific hardware languages.
- Embedded in the Scala programming language
- Algebraic construction and wiring
- Hierarchical + object oriented + functional construction
- Highly parameterizable using metaprogramming in Scala
- Generates low-level Verilog designed to pass on to standard ASIC or FPGA tools
- Multiple clock domains
Source: https://chisel.eecs.berkeley.edu/

---
“Rocket Chip” SoC Generator
“Rocket Chip” SoC Generator
Tile
Tile
Tile
Tile
HTIF
- Generates n Tiles
  - (Rocket) Core
  - RoCC Accelerator
  - L1 I$
  - L1 D$
- Generates HTIF (The host-target interface)
  - Host DMA Engine
- Generates Uncore
  - L1 Crossbar
  - Coherence Manager
  - Exports
  - MemIO
  - Interface
Rocket
Rocket
Core
Core
ROCC
ROCC
Accel.
Accel.
FPU
FPU
L1 Inst
L1 Data
L1 Inst
L1 Data
sets,
sets,
sets,
sets,
ways
ways
ways
ways
client
client
client
client
client
L1 Network
arb
Coherence Manager
L2Cache
L2Cache
L2Cache
L2Cache
L2Cache
mngr
mngr
mngr
mngr
mngr
sets,
sets,
sets,
sets,
sets,
ways
ways
ways
ways
ways
client
client
client
client
client
TileLink / MemIO Converter
mngr
Source: https://riscv.org/wp-content/uploads/2015/02/riscv-rocket-chip-generator-tutorial-hpca2015.pdf
TileLink
TileLink

---
BOOM Superscalar RISC-V into Rocket Chip
BOOM Superscalar RISC-V into Rocket Chip
Rename Map Tables & Freelist
Issue
ALU
Window
Unified
Physical
Decode &
Fetch
Register
Rename
File
FPU
(PRF)
ROB
Commit
out-of-order
back-half
in-order
front-half
9k source lines + 11k from Rocket
Main developer: Christopher Celio
Source: https://riscv.org/wp-content/uploads/2016/01/Wed1345-RISCV-Workshop-3-BOOM.pdf

---
BOOM Stages
BOOM Stages
Fetch
Decode
Rename
Dispatch
Issue
RegisterRead
Execute
Memory
WB
Branch
Prediction
Br
Resolve
Fetch
BP
Logic
Branch
Unified
ALU
Register
Decode
Register
Rename
File
Fetch
Buffer
Issue Window
LAQ
ROB
addr
Data
SAQ
rdata
Mem
wdata
Commit
SDQ
Source: https://github.com/ccelio/riscv-boom-doc

---
BOOM Parameterized Superscalar
BOOM Parameterized Superscalar
bypassing
val exe_units =	ArrayBuffer[ExecutionUnit]()
dual-issue (5r,3w)
ALU
exe_units += Module(new ALUExeUnit(
        is_branch_unit = true,
        has_fpu = true,
        has_mul = true))
FPU
imul
exe_units += Module(new ALUMemExeUnit(
        fp_mem_support = true,
        has_div = true))
Reg.
file
Read
By-
pass
Net-
work
Regfile
Issue
Select
Writeback
bypassing
ALU
Quad-issue (9r,4w)
div
bypassing
ALU
Agen
D$
LSU
ALU
OR
FPU
Reg.
file
Read
By-
pass
Net-
work
Regfile
Issue
Writeback
imul
Select
exe_units += Module(new ALUExeUnit(
        is_branch_unit = true))
ALU
div
exe_units += Module(new ALUExeUnit(
        has_fpu = true, has_mul = true))
exe_units += Module(new ALUExeUnit(
        has_div = true))
Agen
D$
LSU
exe_units += Module(new MemExeUnit())
Source: https://riscv.org/wp-content/uploads/2016/01/Wed1345-RISCV-Workshop-3-BOOM.pdf

---
BOOM – Expected CoreMark Results
BOOM – Expected CoreMark Results
CoreMark/MHz
6.00
5.00
4.00
3.00
2.00
1.00
0.00
out-­‐of-­‐order
in-­‐order
processors
processors
CoreMark/MHz
BOOM-­4w
BOOM-­2w
Rocket
Cortex-­A15
Cortex-­A9
Cortex-­A8
Cortex-­A5
MIPS74k

---
SonicBOOM: The 3rd Generation Berkeley Out-of-Order
Article by Jerry Zhao

---
BOOM Pipeline
BOOM Pipeline
Figure 2: BOOM pipeline across BOOMv1, BOOMv2, and BOOMv3 (SonicBOOM)

---
SonicBOOM Benchmarks
SonicBOOM CoreMark/MHz compared
SonicBOOM SPEC17 IPC compared to Intel Skylake and AWS Graviton cores.

---
RISC-V Tools and OS Status
RISC-V Tools and OS Status
- Linux kernel – upstream, from 4.13
- GCC – upstream from 7.1
- Binutils – upstream
- Glibc – upstream
- Newlib – upstream
- GDB – upstream
- OpenOCD – upstream
- LLVM – upstream
- FreeBSD – upstream RV64I, RV32I unsupported
- QEMU – upstream
- Spike – upstream

---
SiFive RISC-V Cores
SiFive RISC-V Cores
- E Cores, 32-bit embedded cores
  - MCU, edge computing, AI, IoT
- S Cores, 64-bit embedded cores
  - Storage, AR/VR, machine learning
  - Example S76-MC, 64-bit quad-core
- U Cores, 64-bit application processors
  - Linux, datacenter, network baseband
  - Example U74-MC, 4x 64-bit U74 + 1x 64-bit S7
  - U84, single-core, 3-wide issue out-of-order RISC-V pipeline depth of 12 stages, feeding 3 execution units, 16 byte, 4-wide fetch but 3 renames only,
    up to 9 CPU cores into a coherent cluster with a shared L2
- P Cores, performance
  - from 8-stage to out-of-order, 256-bit vector engine
- I Cores, intelligence
  - AI/ML, SiFive AI ISA and RISC-V Vector Extensions

---
RISC-V – HiFive1 MCU from SiFive
RISC-V – HiFive1 MCU from SiFive
- SiFive Freedom E310
- SiFive E31 RISC-V Core
- 32-bit RV32IMAC
- Speed: 320+ MHz
- 1.61 DMIPs/MHz, 2.73 Coremark/MHz
- 16 KB Instruction Cache 16 KB Data Scratchpad
- Hardware Multiply/Divide, Debug Module, Flexible Clock Generation with on-chip oscillators and PLLs
Source: https://www.sifive.com/products/hifive1/

---
RISC-V – HiFive1 from SiFive Pinout
RISC-V – HiFive1 from SiFive Pinout
- Arduino pinout
- OpenOCD
- RISC-V GNU Toolchain
https://github.com/sifive/freedom-e-sdk

---
RISC-V – HiFive Unleashed
RISC-V – HiFive Unleashed
- SiFive FU540-C000 (built in 28nm)
  - 4+1 Multi-Core Coherent Configuration, up to 1.5 GHz
  - 4x U54 RV64GC Application Cores with Sv39 Virtual
  - Memory Support
  - 1x E51 RV64IMAC Management Core
  - Coherent 2MB L2 Cache
  - 64-bit DDR4 with ECC
  - 1x Gigabit Ethernet
- 8 GB 64-bit DDR4 with ECC
- Gigabit Ethernet Port
- 32 MB Quad SPI Flash
- MicroSD card for removable storage
- FMC connector for future expansion with add-in card

---
RISC-V – HiFive Unleashed 1
RISC-V – HiFive Unleashed

---
Microchip PolarFire® SoC+FPGA
Microchip PolarFire® SoC+FPGA
Platform Interrupt Controller
Perfomance/Event Counters
Local Interrupt Controller
Instruction Trace
Fabric Logic Monitor
System Controller
128 KB
Boot Flash
RISC-V
E51 RV64IMAC
Monitor Core
RISC-V
RV64GC U54
Application Core
AXI BUS Monitors
SmartDebug
SPI Programming
Hart
Software
Services
50 Breakpoints
Debug Locks
System Services
PMP
Secure
Boot
PMP
MMU
PUF
sNVM
Crypto*
DMA
16K I$ITIM
8K DTIM
32K I$ITIM
32K D$
2×GbE
128b
4–128b
128b
Anti Tamper
MMC 5.1
Coherent Switch
2×CAN
128b
5–64b AXI4
64b AXI4
2MB Memory
(L2 Cache, Scratchpad Memory,
Deterministic Memory modes)
XIP-QSPI
64b
64b AXI4
AXI4
AMBA Switch with Memory Protection and QoS
2×SPI
IO
32b AHB
128b AXI4
2×I2C
2–64b AXI4; 32b APB
3–64b AXI4
36-bit DDR3/4,
LPDDR3/4 Controller
5× UART
PolarFire®
 FPGA Fabric
18 × 18
MACC
Pre Adder
LSRAM 20 Kb
SECDED
uSRAM
768 bits
PLLs/DLLs
GPIO
DDRIO PHY
RTC
USB OTG
Hardened
Microprocessor
Subsystem
  HSIO
1.8V to 1.2V
DDR4/
LPDDR4
1.6 Gbps
PCIe®
Gen 2
EP/RP,
DMA
x1, x2, x4
PCIe
Gen 2
EP/RP,
DMA
x1, x2
GPIO
3.3V to 1.2V
SGMII
1.6 Gbps
LVDS
Transceivers
64b6xb
8b10b
CTLE
DFE
PIPE
OOB
Loop
Back
Eye
Monitor
PolarFire® FPGA
*DPA-Safe Crypto co-processor supported in S devices
**SECDED supported on all MSS memories
Dedicated MSIO

---
StarLight JH7100
StarLight JH7100
- StarLight JH7100
- StarFive RISC-V U74 @1.0 GHz dual-core 64-bit RV64GC ISA
- 4GB/ 8GB LPDDR4, USB 3.0 ports, 40 pin GPIO
- Vision DSP Tensilica-VP6 @ 600MHz
- NVDLA Engine (2048 MACs @ 800MHz)
- Neural Network Engine (1024MACs @ 500MHz)
- Origially https://beagleboard.org/beaglev
- VisionFive V1 SBC https://rvspace.org/
- https://www.sifive.com/cores/u74-mc
- Lightning Talk: Enabling RISC-V Software Ecosystem with VisionFive (RISC-V Summit)
  https://youtu.be/84VZpjzWMRw

---
SiFive Performance P650 RISC-V Core
SiFive Performance P650 RISC-V Core
- up to 16 cores
- >11 SPECint2006/GHz
- Sv39/Sv48 Virtual Memory Support
- Four-issue, 13 stages, out-of-order pipeline
- Up to 128KB of L1
- Private L2 Caches and Streaming Prefetcher
- 4x 256-bit memory port
- SECDED ECC with Error Reporting
- Hypervisor Extension and System Level Virtualization IP
- SiFive WorldGuard System Security
- Cache stashing to L3 for tightly coupled accelerators
- 2.7GHz @ 5nm fabrication SoCs

---
SiFive P650 Core Architecture
SiFive P650 Core Architecture
- Integer Pipeline: F1, F2, F3, ID, REN, DIS, ISS, RR, EX, WB
- Load/Store: F1, F2, F3, ID, REN, DIS, ISS, RR, LSTA, LSTR, LDF, LDWB

---
More RISC-V projects
More RISC-V projects
- Libre RISC-V
  - Quad-core 28nm RISC-V 64-bit (RISCV64GC core with Vector SIMD Media / 3D extensions)
  - 300-pin 15x15mm BGA 0.8mm pitch
  - 32-bit DDR3/DDR3L/LPDDR3 memory interface
- PolarFire SoC+FPGA, SiFive U540 based
  - https://www.crowdsupply.com/microchip/polarfire-soc-icicle-kit
- Cobham Gaisler AB – NOEL-V Processor
  - https://www.gaisler.com/index.php/products/processors/noel-v
- Allwinner D1 RISC-V, RV64GCV XuanTie C906, T-Head, Alibaba
  - https://linux-sunxi.org/D1

---
RISC-V Organization
RISC-V Resources
- RISC-V International
  - https://riscv.org/
  - https://www.youtube.com/c/RISCVInternational/videos
- Simulators for education
  - QtRvSim
    https://github.com/cvut/qtrvsim
    https://dev.jakubdupak.com/qtrvsim/
  - RARS
    https://github.com/TheThirdOne/rars
  - RIPES
    https://github.com/mortbopet/Ripes/